## Slide 1: HS5.3.4 | EGU25-6596 Opportunities for Hydropower under Climate Change in Snow-ice Dominated Landscapes: Case of the Hálslón Catchment Kárahnjúkar Powerplant in Eastern Iceland
Antonius Heger
Peter Molnar
David C. Finger
02.05.2025
EGU2025, Vienna
https://www.landsvirkjun.com/
Notes: https://www.landsvirkjun.com/

## Slide 2: How will Climate Change influence Runoff?
2 Minute Madness
https://res.cloudinary.com/icelandtours/g_auto,f_auto,c_fill,w_3840,q_auto:best/vatnajokull_glacier_martin_robles_unsplash_c2f641f9d6.jpg
Notes: Iceland‘s runoff dominated by glacier melt  50% of total runoff
large HP potential across the country
Catchment contains largest reservoir
70% covered by Vatnajökull glacier

## Slide 3: Run Climate Projections to Model Glacier Melt
Combination of RCP and SSP
Radiative forcing development
2 Minute Madness
Notes: Emission scenarios from IPCC 6th assessment report
12 global climate models used, bias corrected with CARRA data by Vedurstofa

## Slide 4: Excess discharge increases significantly  Largely increased hydropower potential!
2 Minute Madness

## Slide 5: EGU25-6596: Opportunities for hydropower under climate change in snow-ice dominated landscapes
Scope and Study area
Data, Model Overview
Methods
Results and Discussion
Conclusion
Antonius Heger1,2
Peter Molnar1
David C. Finger2
1Eidgenössische Technische Hochschule Zürich
2Háskólinn í Reykjavík
Click on the Contents on this slide to jump to sections
Click on the arrows to go to the next slide
Click on the icons in the orientation bar to jump to sections

## Slide 6: Scope and Study Area
Location of the catchment
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Catchment area: 1‘614 km2
550m to 1‘825m a.s.l.
70% covered by Vatnajökull glacier

## Slide 7: Kárahnjúkar Powerplant: 690 MW
https://engineers-channel.blogspot.com/p/karahnjukar-dam.html
Landsvirkjun, 2009
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Biggest power plant in Iceland
690 MW
20% of icelandic electricity

## Slide 8: Input Data
Geodata, Landvover: 2016 DEM (Icelandic Land Survey)
Calculated inflow and withdrawal Hálslón reservoir (Landsvirkjun (National Power Company))
Climate Projections: Veðurstofa Islands (Icelandic Met Office)
Meteorological, Snow, Glacier: LamaH-ICE (Helgasson, Nijssen, 2023)
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: LamaH-ICE = Large sample dataset for hydrology Iceland

## Slide 9: Climate Projections
Combination of RCP and SSP
Radiative forcing development
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Emission scenarios from IPCC 6th assessment report
12 global climate models used, bias corrected with CARRA data by Vedurstofa

## Slide 10: Model Overview: HBV-Light
HBV-light model structure (Seibert, Vis, 2012)
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: based on HBV, developed by Jan Seibert, Marc Vis, UZH

## Slide 11: Methods: Summary
Catchment definition
Calibration + Validation of the model
Future Projections
Uncertainty Analysis
Calculation of excess discharge
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 12: Catchment Definition
Elevation classes
Land cover
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: DEM Classification: 12 elevation classes, 105 m each
Reduction of vegetation classes from 9 to 4 for HBV input

## Slide 13: Calibration + Validation
Kling-Gupta Efficiency
Glacier Mean Absolute Error
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Calibrated for Flow and Glacier Mass balance
KGE: Better fit for peak flows than NSE

## Slide 14: Calibration + Validation
10‘000 calibration runs with Monte Carlo
Validation: 01.01.2010 – 31.12.2015
Select 10, 100 best Parameter sets
Calibration: 01.01.2016 – 31.12.2021
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 15: Climate Data Operators
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 16: Future Projections
3 Emission Scenarios
12 climate models
10 and 100 parameter sets
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: 3600 simulations run

## Slide 17: Future Projections: Time Periods
Current: 2016 - 2035
Intermediate: 2051 - 2070
Long Term: 2081 - 2100
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: 20 years each period: Trend stronger than variability, less than 30 years ok

## Slide 18: Future Projections
Change in monthly mean inflow
  Change in run off components (glacier melt, snow melt, rain)
Total yearly inflow
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: i = scenario. j = model, k = parameter set

## Slide 19: Calculation of Spillway Discharge
Assumption: Constant Withdrawal
No adaption, 94 m3/s
144 m3/s constantly
Linear increase to 144 m3/s
https://www.landsvirkjun.com/
3 Scenarios:
Inflow – Withdawal = Δvolume
Level >= 625 m a.s.l. Inflow = Spill
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Constant: no seasonality in withdrawal time series
Inflow – Outflow,
Volume-Level rating curve to calculate lake level.
Level >= 625 m: inflow = Spill

## Slide 20: Uncertainty analysis
ANOVA:
  Analysis of Variance
  Contribution to uncertainty from
    Emission scenarios
    Climate models
    Parameter sets
Inter annual variability
  Significance of change
  Trend > variabilitty
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 21: Results: Summary
Calibration + Validation of the model
Future Projections
Uncertainty Analysis
Calculation of excess discharge
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 22: Results and Discussion
Currently, up to 20% of inflow bypass the turbines via the spillway
Expected increased inflow will increase the spill
Significant amount of potential energy stays unused
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: First: Current situation. Between 5-20% Spilled each year

## Slide 23: Calibration + Validation
Calibration | KGE mean | KGE max | KGE min | MAE mean | MAE max | MAE min
Best 10 | 0.83 | 0.86 | 0.80 | -250.5 | -133.0 | -429.7
Best 100 | 0.80 | 0.90 | 0.72 | -417 | -108.7 | -1389.8
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 24: Future Projection Data
Temperature development in the catchment:
Temperature increases in all Scenarios
Similar development until mid century
Larger deviations after 2060
Average temperature stays below 0°, apart from SSP5-8.5
Precipitation development in the catchment:
No significant change of precipitation in any scenario
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 25: Inflow Change and Uncertainty
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Small compared to change  significant change caused by climate, not weather variability
Rel. variability lower in summer, decreases in future periods

## Slide 26: Inflow increases significantly
Inflow into Hálslón in current and future time periods, total and divided into run off components, glacier melt (b) dominates runoff
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Careful, axes upper and lower are not same

## Slide 27: Spillway discharge increases
No Adaption, constant withdrawal of 94 m3/s
Constant withdrawal of 144 m3/s
Linear increase to 144 m3/s
No Adaption of the system causes 50% of inflow to be wasted by the end of the century
Operational adaptions can mitigate this to a degree
In the long term, structural adaptions are necessary because the plant‘s current capacities are too low
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Noo adaption: 50% wasted by end of century, 4 – 5 TWh / a
constant 144: Frequent drawdown of the reservoir, not. feasible
linear: Operational adaption until mid century, then capacities are exploited

## Slide 28: Uncertainty Contributions
2051 - 2070
2081 - 2100
10 Parameter sets
100 Parameter sets
10 Parameter sets
100 Parameter sets
Climate Models (CM) contribute the largest share of uncertainty
Emission scenarios increase contribution in long term, but are still significantly lower than CM
Parameter uncertainty increases over time but even with 100 parameter sets only adds small amount of uncertainty. Parameter uncertainty is highest in summer due to highly uncertain glacier calibration
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 29: Interannual variability
Mean change and variability
Interannual variability is significantly lower than mean change signal
This shows significance of the change caused by climate trends, not random weather conditions
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Small compared to change  significant change caused by climate, not weather variability
Rel. variability lower in summer, decreases in future periods

## Slide 30: Interannual variability
Relative Variability
Absolute variability
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Small compared to change  significant change caused by climate, not weather variability
Rel. variability lower in summer, decreases in future periods

## Slide 31: Adaptation of Kárahnjúkar possible?
Turbine cavern of Kárahnjúkar (https://www.landsvirkjun.com/)
Spillway discharge with gradual adaption
Scope and study area Data, model overview Methods Results & Discussion Conclusion
Notes: Until mid century: Probably operational measures possible
after that: Strtuctural measures needed

## Slide 32: Conclusion
Significant increase in inflow until the end of the century
Large uncertainties, mainly due to climate models
Adaption of Kárahnjúkar system should be considered
Active Spillway of Kárahnjúkar (https://www.landsvirkjun.com/)
Scope and study area Data, model overview Methods Results & Discussion Conclusion

## Slide 33: The End Thank you!