## Slide 1
Development of a Low-Cost Soil Moisture Sensor Station for Hydrological Monitoring
Veethahavya Kootanoor Sheshadrivasan,
Jakub Langhammer.
Faculty of Science, Charles University, Prague
0/26 · gallery · development · tests · deployment
veethahavya@natur.cuni.cz

## Slide 2
1/26 · home · gallery · development · tests · deployment
RTC module
Microcontroller
micro SD card module
Analog Ports (SMS)
Digital Port (OW/DHT)
Custom
3D Printed
Housing
Status LED

## Slide 3
2/26 · home · gallery · development · tests · deployment
Exposed
Electronic
Components
3D Printed
Enclosure
Filled with
Epoxy Resin

## Slide 4
3/26 · home · gallery · development · tests · deployment
Testing
Temperature Response
Testing Salinity
Response
Testing Saturation Response

## Slide 5
4/26 · home · gallery · development · tests · deployment
In
Beech-Stand,
Šumava,
Czechia
In Semi-Arid
Farmland,
Deccan India
In Peat,
Šumava
Czechia

## Slide 6
Testing · Debugging · Iterative Design
Development of the Sensor Station
5/26 · home · gallery · development · tests · deployment

## Slide 7
Attributes anticipated before development
Reasonably accurate (± 5% VWC)
Low-cost
Easy to program
Low-power usage, to be battery powered
Robust for outdoor use
Reproducible
6/26 · home · gallery · development · tests · deployment

## Slide 8
Choice of Hardware: Core
Soil Moisture Sensor: DFRobot SEN0193
  Capacitive Measurement
  Analog Output
  ! Not waterproof – fixed by waterproofing with epoxy
Microcontroller: Raspberry Pi Pico
  Widely used
  Inbuilt ADC (x3)
  Easy to program on micropython
  Low-power on deep-sleep
  ! Deep-sleep not easy to achieve
7/26 · home · gallery · development · tests · deployment

## Slide 9
Choice of Hardware: Peripheral
Storage: micro SD Card module, SPI
  Ensured data integrity
  ! Relatively complex setup
Clock: Real-time clock module, I2C
  Robust time management, even on power-off
  ! Relatively complex setup
Power:
  LiPo Battery: provides required voltage, expensive
  Solar Panel: enables uninterrupted operation
  DFRobot Solar LiPo Charging module: protected battery charging circuit
8/26 · home · gallery · development · tests · deployment

## Slide 10
Optional Peripherals
Subsurface Temperature Sensor: ‘OneWire’ DS18B20
  Can help with calibration
Air Temperature and Humidity Sensor: DHT11/DHT22
  Useful for hydrological modelling applications
9/26 · home · gallery · development · tests · deployment

## Slide 11
Saturation · Temperature · Salinity
Assessing the Response of Capacitive Soil Moisture Sensors
10/26 · home · gallery · development · tests · deployment

## Slide 12
11/26 · home · gallery · development · tests · deployment
Testing
Temperature Response
Testing Salinity
Response
Testing Saturation Response

## Slide 13
Measuring Principle of Capacitive Soil Moisture Sensors
Non-contact Measurement via Dielectric Constant change
Sensor body = Capacitor with Soil as Dielectric
Sensor forms part of RC circuit → Frequency shift
Microcontroller measures voltage output ∝ moisture
↑Moisture⇒ ↑Dielectric constant⇒ ↑Capacitance⇒ ↓Value
RC time constant: τ = R⋅C (time to charge capacitor to ~63% of final voltage)
Capacitance Relation: C = εr​ε0​ (A/d)​
12/26 · home · gallery · development · tests · deployment

## Slide 14
Saturation vs Sensor Response
Not linear
Exponential Decay
In line with what one expects from the measuring principle
13/26 · home · gallery · development · tests · deployment

## Slide 15
Saturation vs Sensor Response …
Due to the testing method, the sensor was not sensitive to saturation <0.26
More noise at lower saturation, possibly from contact establishment
14/26 · home · gallery · development · tests · deployment

## Slide 16
Saturation vs Sensor Response …
A better relationship that takes into account the uncertainty at lower saturation
Better validation results
15/26 · home · gallery · development · tests · deployment

## Slide 17
Temperature vs Sensor Response
Satisfyingly Linear Response
In line with what can be expected from the measuring principle of the device.
16/26 · home · gallery · development · tests · deployment

## Slide 18
Temperature vs Sensor Response …
Satisfyingly even spread of sensor response across temperatures
Some outliers may be attributed to the not-so robust ADC on Rpi Pico
17/26 · home · gallery · development · tests · deployment

## Slide 19
Salinity vs Sensor Response
Low magnitude noise
No discernible relationship
18/26 · home · gallery · development · tests · deployment

## Slide 20
Rokytka Catchment, Sumava, Czechia · Berembadi Catchment, Deccan India
Field Deployment and Validation
19/26 · home · gallery · development · tests · deployment

## Slide 21
20/26 · home · gallery · development · tests · deployment
In
Beech-Stand,
Šumava,
Czechia
In Semi-Arid
Farmland,
Deccan India
In Peat,
Šumava
Czechia

## Slide 22
Measurements from Rokytka
Beech Stand
Depths:
  SM1 – 20 cm
  SM2 – 40 cm
  SM3 – 60 cm
21/26 · home · gallery · development · tests · deployment

## Slide 23
Measurements from Rokytka …
Peat, Down
Away from drainage
Depths:
  SM1 – 10 cm
  SM2 – 20 cm
  SM3 – 40 cm
22/26 · home · gallery · development · tests · deployment

## Slide 24
Measurements from Rokytka …
Peat, Down
Near drainage
Depths:
  SM1 – 10 cm
  SM2 – 20 cm
  SM3 – 40 cm
23/26 · home · gallery · development · tests · deployment

## Slide 25
Measurements from Berembadi
Depth – 5 cm
Uncalibrated values still demonstrate the sensor’s ability as seen from the agreeable match in the trend
24/26 · home · gallery · development · tests · deployment

## Slide 26
Measurements from Berembadi …
Depth – 15 cm
Shows the need for multivariate calibration – in line with lab tests
25/26 · home · gallery · development · tests · deployment

## Slide 27
Contact me at veethahavya@natur.cuni.cz for more details
Thank You
26/26 · home · gallery · development · tests · deployment