## Slide 1: Refining Hydrogen Emission Measurements: Methodological Insights and Pilot Findings
Malgven Roudot 1, Victoria Krohl 1, Tomas Mikoviny 2,3, Felix Piel 2, Nikita Sobolev 3, Armin Wisthaler 2,3
Equinor ASA, Oslo, Norway
Advanced Monitoring Solutions (adMS), Oslo, Norway
Department of Chemistry, University of Oslo, Oslo, Norway

## Slide 2
Objectives :
Choose the instrument / technology
Test instrument at 1-2 industrial sites
Objectives :
Improve H2 release scenarios
Communicate results and conclusions with relevant policymakers and stakeholders
Objectives :
Quantify H2 emissions from 2-3 industrial facilities (tracer ratio method, land-based & airborne)
Raising the standard of trust for hydrogen in the energy transition
2023 : Phase 1
2024-2026: Phase 2
2025 - 2026
Wind
Known tracer emission rate

## Slide 3: H2MS
Mass spectrometer optimized to measure small concentrations of hydrogen in the atmosphere
Field data comparison: Performance equivalent to CH4 analyser (Picarro G2311-f)
Patent application submitted
67 cm
H2 (ppm)
CH4 (ppm)
1 ppm

## Slide 4: Demonstration experiment in Oslo Tracer ratio system test – co-located controlled-release
H2 flow rate: 0.0075 kg / hour *
Ratio H2/He: 0.615 ± 0.009
Release of H2 and He mixture
Air sampling
H2 flow rate: 0.0074 kg / hour *
Ratio H2/He: 0.604 ± 0.044
Error ≈ 2%
* At 20 °C

## Slide 5: Validation experiment in industrial environment with
Operator H2 flow rate: 0.8 ± 0.02 kg / hour
Estimated H2 flow rate: 0.8 ± 0.06 kg / hour

## Slide 6: Validation experiment in industrial environment with
Error ≤ 3 %
Error ≤ 25 %
Operator H2 flow rate: 0.8 ± 0.02 kg / hour

## Slide 7: Full-scale campaign at hydrogen processing plant
Steam Methane Reformer (SMR)
2 experiments
Fugitive emissions
Distance H2 source to tracer release point
  Unknown (< 150 m)
Flare
2 experiments
Point source
Distance H2 source to tracer release point
  Horizontal ~ 15 m (east)
  Vertical ~ 20 m
Cold Vent
3 experiments over 3 days
Point source
Distance H2 source to tracer release point
  Horizontal ~ 55 m (south)
  Vertical < 5 m

## Slide 8: First full-scale campaign at hydrogen processing plant
Average production during campaign: 3862 kg/h
Confidently assigned to production site
If all measured emissions assigned to production site
8 kg/h | 15 kg/h | 13.4 kg/h
0.21 % | 0.39% | 0.35%
27.2 kg/h | 38.5 kg/h | 34 kg/h
0.7 % | 1 % | 0.88%
H2 emissions related to production rate
Sum of median values
Sum of (Weighted average of all plumes
(number of points x R2))
Sum of (median value + (max rate * 1 h/day))
Preliminary results

## Slide 9: Take-aways and way forward
HEQ method shows good performance
Initial results from SMR production sites show low hydrogen emissions (< 1%)
Wind conditions and road access limitations are a challenge
Test airborne approach for integrated site emissions
Emissions from other parts of the value chain
Scientific publication coming soon
WIND
First test flight (31/03/2025)
* * * * *

## Slide 10: Refining Hydrogen Emission Measurements: Methodological Insights and Pilot Findings
Malgven Roudot 1, Victoria Krohl 1, Tomas Mikoviny 2,3, Felix Piel 2, Nikita Sobolev 3, Armin Wisthaler 2,3
Equinor ASA, Oslo, Norway
Advanced Monitoring Solutions (adMS), Oslo, Norway
Department of Chemistry, University of Oslo, Oslo, Norway
Acknowledgments: