## Slide 1
A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS
Paola Di Fluri1,2, Matthew D. Wilson2,3, Alessio Domeneghetti1
1 Department of Civil, Chemical, Environmental and Materials Engineering, Alma Mater Studiorum University of Bologna, Bologna, Italy
2 Geospatial Research Institute | Toi Hangarau, University of Canterbury, New Zealand
3 School of Earth and Environment | Te Kura Aronukurangi, University of Canterbury, New Zealand
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 2
Digital Elevation Model (DEM)
Bathymetry
River discharge
Rainfall
Tidal
TOPOGRAPHIC DATA
HYDROLOGICAL AND METEOROLOGICAL DATA
FRICTION DATA
Manning’s coefficient
Data requirement
HYDRAULIC MODEL
OIL SPILL MODEL
OIL DATA
Density Initial volume
ENVIRONMENTAL DATA
Water temperature
Water density
Wind velocity
Flow velocity
Discharge
Caesar-Lisflood model
Output data
Flow velocity
Water depth
Oil thickness
Area extent
Oil concentration
Mass balance
Visualisation
Chart: VOLUME BUDGET
SUPERFICIAL OIL | 49.9991 | 49.9968 | 49.9944 | 49.9918 | 49.9888 | 49.8159 | 48.4745 | 45.6954 | 41.8645 | 37.4619 | 25.3068
OIL OUT | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6.7702e-11 | 1.8758e-09 | 0.00086188 | 4.0797
EVAPORATED OIL | 0.00094143 | 0.0032375 | 0.0056118 | 0.0082135 | 0.011154 | 0.18411 | 1.5255 | 4.3046 | 8.1355 | 12.5372 | 20.6137
WATER DEPTH
VELOCITY
OIL CONCENTRATION
OIL DEPTH
HYDRODINAMIC DATA
Model Framework: From Input Data to Output Assessment
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 3
Spreading
Advection
Evaporation
Dispersion
Emulsification
Dissolution oxidation
Sedimention
biodegradation
Time of occurrence
Selected processes
Oil spill module: process selection
OUR MODEL!
Deterministic model
eulerian model
2D model
Far-field model
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 4
Assignment of model input
void oil_spill_input(double local_time_factor)
{
iteration_t += local_time_factor;
for (int x = Math.Min(oil_fromx, oil_tox); x <= Math.Max(oil_fromx, oil_tox); x++)
{
for (int y = Math.Min(oil_fromy, oil_toy); y <= Math.Max(oil_fromy, oil_toy); y++)
{
oil_depth_init = oil_ratev * local_time_factor / (oil_n_cells * DX * DX);
if (iteration_t > oil_spillt)
{
oil_ratev = 0;
}
oil_depth[x, y] += oil_ratev * local_time_factor / (oil_n_cells * DX * DX);
}
}
}
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
Code implementation: oil input
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 5
Triggering condition – the oil spill starts when a certain water depth threshold is exceeded
INPUT CELL
// check triggering of event
if (cycle > oil_startt && oil_check_depth_threshold() == true)
{
oil_eventtriggered = true;
} bool oil_check_depth_threshold()
{
for (int x = Math.Min(oil_fromx, oil_tox); x <= Math.Max(oil_fromx, oil_tox); x++)
{
for (int y = Math.Min(oil_fromy, oil_toy); y <= Math.Max(oil_fromy, oil_toy); y++)
{
if (water_depth[x, y] > oil_starth) return true;
}
}
return false;
}
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
Code implementation: triggering condition
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 6
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
Cell count containing oil and calculation of the oil spill area
void oil_area()
{
count_cells = 0;
for (int x = 1; x < xmax; x++)
{
for (int y = 1; y < ymax; y++)
{
if (oil_depth[x, y] > 0)
{
count_cells++;
}
oil_S = count_cells * DX * DX;
}
}//);
}
Code implementation: oil spill area computation
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 7
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
Implementation of the Mackey and Fingas formula for calculating the evaporation rate.
void oil_evaporation(double local_time_factor)
{
var options = new ParallelOptions { MaxDegreeOfParallelism = Environment.ProcessorCount * 4 };
Parallel.For(1, ymax + 1, options, delegate (int y)
{
int inc = 1;
while (down_scan[y, inc] > 0)
{
int x = down_scan[y, inc];
inc++
if (oil_depth[x, y] > 0)
{
iteration_t += local_time_factor;
//evaporation exposure
oil_exp = oil_transf_coeff * oil_S * (local_time_factor) / oil_totalv;
Ev = (oil_T / (oil_B * oil_Tg)) * Math.Log(oil_exp * (oil_B * oil_Tg / oil_T) * Math.Exp(oil_A - (oil_B * oil_To / oil_T)) + 1);
}
}
Code implementation: oil evaporation 1/3
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna
Notes: Definition of the evaporation process.
Need to track the evaporated oil quantity to ensure accurate mass balance calculations.

## Slide 8
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
Implementation of the Mackey and Fingas formula for calculating the evaporation rate.
Advection + spreading
Advection + spreading
Evaporation (Mackey method)
Advection + spreading
Evaporation (Fingas method)
Code implementation: oil evaporation 2/3
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna
Notes: Development and comparison of two different evaporation formulations.
Fingas's simplified formula: Depends on temperature and time, derived from laboratory experiments.
Mackay model considerations: Accounts for oil properties and wind influence  more complex but more reliable (not many parameter needed)

## Slide 9
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
Implementation of the Mackey’s formula
Wind influence on evaporation
Chart: % of volume evaporated oil
Code implementation: oil evaporation 3/3
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 10
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
FIRST ORDER UPWIND INTERPOLATION SCHEME
Code implementation: advection-dispersion equation
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna

## Slide 11
Oil_spill_input()
Erodepo()
Cycle +=time_factor/60
Oil_check_depth_threshold()
Oil_area()
Oil_evaporation()
Oil_route()
Oil_update()
START
END
yes
no
Code implementation: oil depth update
void oil_update()
{
var options = new ParallelOptions { MaxDegreeOfParallelism = Environment.ProcessorCount * 4 };
Parallel.For(1, ymax + 1, options, delegate (int y)
{
int inc = 1;
while (down_scan[y, inc] > 0)
{
int x = down_scan[y, inc];
inc++;
if (elev[x, y] > -9999 )
{
oil_depth_prev[x, y] = oil_depth[x, y];
oil_depth[x, y] += (oil_hx[x + 1, y] - oil_hx[x, y] + oil_hy[x, y + 1] - oil_hy[x, y]);
// oil concentration
oil_conc[x, y] = (((oil_depth[x, y] * oil_density ) / (oil_depth[x, y] * oil_density + water_depth[x, y] * ro_water)) * oil_density) ; // g/L
if (oil_conc[x, y] > 0)
{
oil_concentration[x, y] = oil_conc[x, y];
}
Update of the oil depth in the cell and oil concentration calculation
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna
Notes: Update of oil thickness in each cell by calculating incoming and outgoing oil.
Calculation of oil concentration within the same cell.

## Slide 12
Results and visualisation: how it should be

## Slide 13
Any feedback or question is welcome!
paola.difluri2@unibo.it
Supplementary material for poster presentation A NEW PHYSICALLY-BASED NUMERICAL MODEL TO SIMULATE RIVER FLOOD TRIGGERED OIL SPILLS - EGU European Geoscience Union 2025, 27 April – 2 May Vienna