## Slide 1
A Feature Selection Framework for Enhancing Interpretability and Performance in Multi-Objective Water Systems Operations
Guang Yang, Matteo Giuliani, Andrea Castelletti,
Zengchuan Dong
May 01, 2025
guang.yang@hhu.edu.cn

## Slide 2
Constraint
C(Θ)
Reservoir inflow
Q(i,t)
Reservoir operation
Decision-making
O(Yt)
Power generation,
water supply
S(Ri,t)
Reservoir storage
F(i,t)
Inflow forecasts
Reservoir operation model optimization
（hydroclimatic predictions and demand estimations）
  Multiple factors effecting the reservoir operation decision-making
Release
Reservoir
inflow
Given a finite set of states S and actions A, the reward can be obtained at each state-action pair: r(s,a).
Find a best action series such that:

## Slide 3
Why we need feature selection in water systems operation?
Qtout=Q(τt, St, Qtin)
Single reservoir operation
Qtout=Q(τt, S1t, S2t , Qtin, Qt+1in…)
Cascade reservoir operation
τt Seasonal information St Reservoir storage Qtin Reservoir inflow
Inflow
Storage
Season
Conventional input variables
Relevant input variables
Selected input variables
Cascade reservoir operation
with input variable selection
Water resources
development
Feature selection
Low-dimensional
High-dimensional
Median-dimensional
  Reduce the dimensionality in reservoir operation optimization

## Slide 4
Case study descriptions
3 Reservoirs
(GERD, MER, HAD)
5 objectives
(HPGERD, HPMER, HPHAD, IrrSudan, IrrHAD)
Hydropower generation (HP)
Irrigation water supply (Irr)
Reservoirs operation system in the Nile River Basin
12 relevant variables
(hGERD, hMER, hHAD, QGERD, QWN, …)

## Slide 5
Input variables in the Nile system operation
Conventional inputs
F3
Coordinated conventional inputs
Selected inputs
F2
F1

## Slide 6
Candidate input variables
Variable name | Definition
h_GERD | GERD reservoir water level at the current time step
h_MER | MER reservoir water level at the current time step
h_HAD | HAD reservoir water level at the current time step
moy | Month of the year
qIn_GERDs | GERD reservoir inflow in the previous time period
qIn_WNs | White Nile inflow in the previous time period
qIn_Atbs | Atbara inflow in the previous time period
qIn_DinRas | Dinder+Rahad inflow in the previous time period
demandSUD1s | Water demand of irrigation district 1 in the current time period
demandSUD2s | Water demand of irrigation district 2 in the current time period
demandSUD3s | Water demand of irrigation district 3 in the current time period
WtHADs | Water demand downstream of HAD in the current time period

## Slide 7
Feature selection in multi-purpose water systems
Recursive Feature Elimination
Multi-objective optimization
Rules optimization
Rules simulation
Feature selection
Water system operation
Select input variables for each reservoir by integrating Recursive Feature Elimination (RFE) with Evolutionary Multi-Objective Direct Policy Search.

## Slide 8
Input variables selections in multi-objective Nile operation
Water level
Water levels
Water levels
Water demand
Inflow
Inflow
Interval basin flow
Inflow
Month of year

## Slide 9
Input variables selections in multi-objective Nile operation

## Slide 10
Input variables selections considering DM preferences
hGERD
hMER
QinGERD
hGERD
hMER
QinGERD
hGERD
hMER
Month of year
HPGERD-preferred
HPMER-preferred
HPHAD-preferred

## Slide 11
Input variables selections considering DM preferences
hGERD
hMER
QinAtbs
hGERD
hMER
QinAtbs
hGERD
hMER
QinGERD
HPMER-preferred
IrrSudan-preferred
HPHAD-preferred

## Slide 12
Input variables selections considering DM preferences
WtHADs
hHAD
QinGERD
WtHADs
hHAD
hGERD
IrrHAD-preferred
HPHAD-preferred

## Slide 13
Multi-objective optimization with various input variables
Conventional inputs
F3-F5
Coordinated conventional inputs
Selected inputs
F2
F1

## Slide 14
Summary and Highlights
Variables that reflect collaborative operations among different reservoirs consistently received higher importance rankings in the selection process.
The selected input variables of each reservoir can vary with decision-making preferences, allowing for rules design that aligns with shifting goals and priorities.
The operating rules using selected input variables can improve the performance of Nile operation and mitigate power generation and water supply conflicts.

## Slide 15
THANKS!
Guang Yang
Hohai University, Nanjing, China
Email: guang.yang@hhu.edu; gyang82@gatech.edu