## Slide 1
Geochemical modeling of CO2 occurrence state in gas field produced water reinjection reservoir
Shugang Yang1, 2, Shuangxing Liu1, 2, Mingyu Cai1, 2, Ming Xue1, 2, Xingchun Li1, 2, and Kunfeng Zhang1, 2
1 CNPC Research Institute of Safety and Environment Technology, Beijing, China, 102206 2 State Key Laboratory of Petroleum Pollution Control
Acknowledgement: This work was supported by the Scientific Research and Technology Development Project of CNPC (Grant Nos. 2023ZZ1301 and 2021DQ03-A2).
References:
Pearce, J.K., Khan, C., Golding, S.D., et al. Geological storage of CO2 and acid gases dissolved at surface in production water. Journal of Petroleum Science and Engineering, 2022, 210, 110052.
Eyitao, S.I., Okere, C.J., Hussain, A., et al. Synergistic sustainability: Future potential of integrating produced water and CO2 for enhanced carbon capture, utilization, and storage (CCUS). Journal of Environmental Management, 2024, 351, 119713.
Introduction
The gas field produced water reinjection and CO2 geosequestration have become hot topics in the field of energy and environment. Gas field produced water reinjection is similar to CO2 geological storage in terms of site selection, well construction, injection method and environmental monitoring technology. Under the background of synergistic reduction of pollution and carbon emissions, the coordination of gas field produced water reinjection and CO2 geological storage could provide a potential way to promote the synergistic reduction of pollution and carbon emissions and expand the benefit path of CO2 geological storage.
Research objective
The CO2 injected into the reservoir would be presented in dissolution-mineralization phase and free phase. Based on the interaction mechanism of CO2-gas field produced water-reservoir rock, this work focuses on investigating the effects of CO2 pressure, produced water salinity, reservoir rock type and formation temperature on the CO2 occurence state (dissolution-mineralization phase and gas phase) using PHREEQC program.
Methodology
Sample |  | Quartz | Feldspar | Chlorite | Illite | Calcite | Dolomite
Sandstone | Proportions | 38% | 47% | 8% | 7% | _ | _
 | Moles | 3.17 | 0.42 | 0.05 | 0.09 | — | —
Limestone | Proportions | 1% | - | - | - | 83% | 15%
 | Moles | 0.08 | - | - | - | 4.15 | 0.41
Table 1. The mineral compositions of rock samples
Compostion | PW1 | PW2 | PW3 | PW4 | PW5
CaCl2 | 0 | 30 | 30 | 30 | 30
NaCl | 0 | 0.585 | 58.5 | 119 | 175.5
MgCl2 | 0 | 7 | 7 | 7 | 7
KCl | 0 | 10 | 10 | 10 | 10
BaCl2 | 0 | 3 | 3 | 3 | 3
TDS | 0 | 50.585 | 108.5 | 169 | 225.5
Table 2. The salinity, and ion composition of produced water(g/L)
Sample | CO2 Pressure MPa | Produced water | Temperatuire ℃
Sandstone | 1, 3, 6, 8, 10, 14, 20, 40 | PW1, PW2, PW3, PW4, PW5 | 40, 50, 70, 90, 120
Limestone |  |  | 
Table 3. The set of simulation conditions
where M is moles of CO2 before reaction, Mf is moles of CO2 after reaction, pf is the proportion of free phase CO2, pm is dissolution-mineralization phase CO2.
Modeling Results
Implications
Figure 1. The moles and proportions of dissolution-mineral CO2 phase at different CO2 injection pressures in limestone reservoir.
Figure 2. The moles and proportions of dissolution-mineral CO2 phase at different CO2 injection pressures in sandstone reservoir.
Figure 3. The moles and proportions of dissolution-mineral CO2 phase at different brine salinity pressures in limestone reservoir.
The change of CO2 pressure leads to the change of proportion of dissolution-mineralization phase CO2 in the sandstone and limestone system range from 47% to 72%.
Figure 4. The moles and proportions of dissolution-mineral CO2 phase at different brine salinity pressures in sandstone reservoir.
Figure 5. The moles and proportions of dissolution-mineral CO2 phase at different temperatures (left: sandstone, right: limestone).
The variation of the proportion of dissolution-mineralization phase CO2 caused by the difference of rock type ranges from 10% to 45%, the changes of the proportion caused by the produced water salinity and formation temperature fall 2% ~ 30 % and 1 % ~ 15 %, respectively.
In the practice of gas field produced water reinjection combining with CO2 geological storage, the injection volume and pressure should be adjusted in time according to the water salinity, reservoir physical properties and temperature, so as to reduce leakage risk caused by gas phase CO2 accumulation in the early stage of storage.
E-mail：yshugang@cnpc.com.cn