## Slide 1
The Impact of Organic Solvent Oil Extraction on Shale Pore System-Key Issues in Shale Pore Evaluation
Xinbin Zhao Min Wang
China University of Petroleum(East China)
2025.04.28

## Slide 2
01
Background & Questions
02
Experiments & Results
03
Conclusions

## Slide 3
Conventional Oil
Shale Oil
Shale Oil Proportion
Shale Oil Production/106bbl*d-1
Shale Oil Proportion/%
Shale oil production increase year by year in the US
The proportion of shale oil is over 60% of the oil production in the US
1. Background & Questions
The shale oil and gas resources in the United States have already achieved large-scale development. Especially shale oil, whose production increase progressively year by year has become the main force in oil production in the US. Shale oil and gas are wide globally distributed with enormous reserves and broad prospects.

## Slide 4
Shale oil is mainly preserved in micro- and nanopores, which makes the pore evaluation extremely important. Additionally, the porosity of shale oil reservoirs is a key parameter in resource and reserve evaluation models.
Porosity
Specification of shale oil reserves estimation
1. Background & Questions

## Slide 5
Lots of methods are applied to evaluate the porosity of shale reservoirs, such as the image processing methods and fluid intrusion methods. For these methods, solvent extraction (oil washing) is required to expose the pores before the experiments.
SEM-FIB
BET
MIP
GIP
WIP
NMR
CT
Image processing methods
Fluid intrusion methods
1. Background & Questions

## Slide 6
How does shale porosity change after solvent extraction?
What causes the reduction in shale porosity after solvent extraction?
DiStefano.2019
Questions：
Researchers found that：
DiStefano.2016
Clay-
rich
Carbonaterich
High Maturity
Low Maturity
1. after solvent extraction, not all shale porosities increase（porosity increases in carbonate-rich shale, but decrease in clay-rich shale）
2. the porosity increments after solvent extraction are various with different solvents, and some solvents may even lead to a reduction in porosity
1. Background & Questions

## Slide 7
01
Background & Questions
02
Experiments & Results
03
Conclusions

## Slide 8
Sample | A | B
TOC | 1.74 | 3.00
Ro | 0.86 | 1.67
S1/mg/g | 1.86 | 2.72
S2/mg/g | 4.72 | 7.44
clay /% | 11.5 | 47.8
quartz/% | 15.1 | 22.5
calcite/% | 46.6 | 3.4
Samples
Sample A
Sample B
Bohai Bay Basin, Jiyang Depression, Dongying Sag, Shahejie Formation
Songliao Basin, Gulong Sag, Qingshankou Formation
Low to medium maturity, carbonate-rich shale with moderate organic matter
Medium to high maturity, organic-rich and clay-rich shale
Ro=0.86%
Ro=1.67%
2. Experiments & Results
SAMPLE INFORMATION

## Slide 9
1. Distillation extraction apparatus was used for solvent extraction
2. Shale samples were divided into five equal parts, and five different solvents were used for the solvent extraction, separately.
3. NMR, helium porosity, and nitrogen adsorption experiments were conducted at 3, 7, and 12 days of solvent extraction
2. Experiments & Results

## Slide 10
2. Experiments & Results
Sample A
Sample B
He ф（increase）
Extracted fluid ф（increase）
Porosity increment/%
Porosity increment/%
Extraction time/d
Extracted fluid ф（increase）
He ф（increase then decrease）
As the extraction time increased, the volume of extracted fluid gradually increased for both samples.
In Sample A, He porosity increased with the extraction time. The pore volume increment roughly equal to the volume of extracted fluid.
In Sample B, the porosity increment initially increased and then decreased with extraction time. After 7 days, He porosity weas lower than the extracted fluid porosity.

## Slide 11
As the extraction time increased, the volume of extracted fluid gradually increased for both samples.
In Sample A, He porosity increased with the extraction time. The pore volume increment roughly equal to the volume of extracted fluid.
In Sample B, the porosity increment initially increased and then decreased with extraction time. After 7 days, He porosity weas lower than the extracted fluid porosity.
2. Experiments & Results
Before
Extraction, 3days
Fluid porosity：
No1
No2
Nw1
Nw2
ΔNo=No1-No2
ΔNo=No1-No2

## Slide 12
Pore structure changes after extraction
Sample A
Sample B
Sample A
Sample B
1. Based on the adsorption-desorption isotherms, solvent extraction increased the pore volume of the samples compared with the original state
Why solvent extraction decrease the pore volume?
2. Experiments & Results

## Slide 13
Pore structure changes after extraction
Sample A
Sample B
Sample A
Sample B
2. With the increase of extraction time, in Sample A, pores < 20 nm gradually increased, while pores > 20 nm gradually decreased.
3. With the increase of extraction time, in Sample B, pores < 8 nm increased, and pore > 8 nm decreased and then increased
Why solvent extraction decrease the pore volume?
2. Experiments & Results

## Slide 14
Reason 1: Clay minerals could absorb organic solvents, especially alcohol-based solvents, which caused the clay volume expansion. Such expansion could occupy the pore space and decrease the pore volume.
Solidification
Alcohol-based solvents
Quantitative analysis of the expansion phenomenon of clay minerals (Height method) after contact with solvents
1. The volume of illite and montmorillonite increased after solvent absorption, with montmorillonite showing the most significant increase.
2. The volume of chlorite decreased the most significantly, may due to solidification.
2. Experiments & Results

## Slide 15
1. Kerogen expansion after absorbing organic solvents, which occupies pores and decrease pore volume
2. The higher the maturity, the lower the expansion coefficient; different organic solvents have different expansion coefficients.
Reason 2：
2. Experiments & Results

## Slide 16
3. A comparison of helium porosity and saturated oil porosity indicates that the saturated oil method overestimates shale porosity, with the overestimation more pronounced in shales with higher TOC and lower maturity.
Reason 2：
2. Experiments & Results

## Slide 17
Model of pore changes during the extraction
①coexistence of oil, water, and organic matter in pores
②solvent extract the oil and water
③expansion of organic matter and clay minerals after contacting with the solvent
④the extracted organic matter and mineral fragments block the pores
The actual change in porosity during the solvent extraction depends on the balance between fluid extraction increasing pore volume and mineral expansion decreasing pore volume.
2. Experiments & Results

## Slide 18
Before extraction
After extraction
T1-T2 map
SEM
2. Experiments & Results
In addition to the structural changes caused by solvent extraction, it is challenging to completely remove fluids in micro- and nanopores during the process.
Sample A
(Low to medium maturity, carbonate-rich shale with moderate organic matter)
Solvent: Dichloromethane
Extraction duration: 12 days

## Slide 19
Co
Cw
Classification and quantification of oil and water NMR signals.（Co、Cw）
Establishment of conversion relationship（ko、kw）
To avoid the aforementioned issues, NMR technology is proposed for evaluating shale porosity without solvent extraction
Fuld volume calculation
Porosity evaluation
When the sealed cores are effective
1. Sealed coring shale samples
2. Experiments & Results

## Slide 20
Residual fluid porosity(Փ1)
Fluid saturated porosity (Փ2)
No
Nw
Ns
AAPG Bulletin submitted
2、conventional coring shale samples,
③Shale porosity（Փ1+ Փ2 ）
2. Experiments & Results
To avoid the aforementioned issues, NMR technology is proposed for evaluating shale porosity without solvent extraction

## Slide 21
The porosities by NMR in conventional coring and sealed coring samples are generally the same
Sealed sample
Porosity 1
Post-placement sample
Storage for 90 Days
Saturated sample
Saturated Fluid
Porosity 2
Porosity 3
Porosity 1
Porosity 2
Porosity 3
2. Experiments & Results

## Slide 22
01
Background & Questions
02
Experiments & Results
03
Conclusions

## Slide 23
In clay-rich shale, porosity increases and then decreases during the extraction.
In solvent extraction, the removal of fluids from the shale pores increases pore volume. However, the expansion of clay minerals and swelling of kerogen could lead to the reduction of pore volume
Solvent extraction of low to medium maturity shale is more challenging with an efficiency generally around 60%
For both sealed coring and conventional coring shale samples, it is recommended to use an NMR-based porosity evaluation method without solvent extraction.
3. Conclusions

## Slide 24
Thanks for listening!