## Slide 1: Water Availability Assessment in a Data-Scarce Region: Application to the District of Southern Italy Screen: PICO 4.13
Felice Daniele Pacia1,2, Pasquale Perrini 3,1 , Angelo Avino1, Awais Naeem Sarwar1, Afshin Jahanshahi1, Pasquale Coccaro6, Luciana Giuzio6, Vera Corbelli6, Mauro Fiorentino4, Vito Iacobellis5, Salvatore Manfreda1
1 Department of Civil, Building and Environmental Engineering, University of Naples Federico II, Naples, Italy; 2 University School of Advanced Studies IUSS Pavia, Italy; 3 Department of Soil, Plant and Food Science, University of Bari Aldo Moro, Bari, Italy; 4 Department of European and Mediterranean Cultures: Architecture, Environment and Cultural Heritage, University of Basilicata, Matera, Italy; 5 Department of Civil, Environmental, Land, Building Engineering and Chemistry, Polytechnic University of Bari, Bari, Italy; 6 Autorità di Bacino Distrettuale dell'Appennino Meridionale,Caserta, Italy.

## Slide 2: Overview
Hydrological balance at the Southern Italy scale
Assessment of water availability to achieve optimal resource management in a highly heterogeneous climate context and to address more effectively projected climate change.
Applying a Hydrological model all over the district area
DREAM model
Calibration of the Hydrological model in data-scarce region
Automatic calibration with a genetic algorithm was performed through three different setups
Notes: The main aim of our work was the reconstruction of the hydrological balance IN A DATA SCARCE REGION to be able to describe the water availability of the area. In order to address this aim, we applied a DISTRIBUTED hydrological model, NAMED DREAM model. The study area is the area covered by the River Basin District Authority of Southern Italy, a large REGION where the availability of HYDROLOGICAL data is really poor. So, the main challenge of our work was the calibration of the model WITH A LIMITED AVAILABILITY OF DATA. To overcome this challenge, we reconstructed discharge time series BY USING THE water balance OF selected artificial reservoirs.

## Slide 3: Study Area
883 Protected Natural Areas
Popolazione: 12.977.357 (ISTAT 2024)
Provinces
n. 25
Municipalities:
n. 1.632
Total number of surface water bodies:
n. 1021
Regional territories:
n. 7
Abruzzo, Lazio Basilicata, Molise Calabria, Campania, Apulia
Surface:
67.459
Total number of groundwater bodies:
n. 189
Total rib length: 2509 kml
Unit of Management (River Basins):
n. 17
Total number of Hydrostructure:
n. 184
Mountain Communities:
n. 100

## Slide 4
Conza
Area [km²] : 233
P Mean [mm] : 893
T Mean [°C] :12.7
Acerenza
Area [km²] : 143
P Mean [mm] : 832
T Mean [°C] :12.9
Camastra
Area [km²] : 343
P Mean [mm] : 816
T Mean [°C] : 13
Pertusillo
Area [km²] : 581
P Mean [mm] : 925
T Mean [°C] : 12.2
Turbolo
Area [km²] : 7
P Mean [mm] : 1167
T Mean [°C] : 13.2
Serra del Corvo
Area [km²] : 282
P Mean [mm] : 689
T Mean [°C] : 13.6
Menta
Area [km²] : 13.4
P Mean [mm] : 1414
T Mean [°C] : 15.3
Alaco
Area [km²] : 14
P Mean [mm] : 1492
T Mean [°C] : 15.7
San Pietro
Area [km²] : 68.6
P Mean [mm] : 926
T Mean [°C] : 12.3
Fiumarella
Area [km²] : 31
P Mean [mm] : 875
T Mean [°C] : 13
Salsola
Area [km²] : 445
P Mean [mm] : 693
T Mean [°C] : 14.6
Candelaro
Area [km²] : 337
P Mean [mm] : 758
T Mean [°C] : 14.3
Carapelle
Area [km²] : 489
P Mean [mm] : 738
T Mean [°C] : 14.1
Cervaro
Area [km²] : 507
P Mean [mm] : 746
T Mean [°C] : 13.9

## Slide 5: Discharge reconstruction
Inflow
W(t)
Outflow
Evaporation
(m3) is the daily volume flowing into the reservoir, (m3) is the accumulated volume in the reservoir, (m3) is the volume exiting the reservoir (irrigation, industrial, drinking, release and/or spillway).
(mm/day) is evaporation from the lake, correction factor, is the monthly average of the astronomical length of day, expressed as a % of the total daylight hours of the year, is the average daily temperature.
.

## Slide 6: Discharge reconstruction
Area = 143 Km2
Fixed lake surface area = 2 Km2
Availability of inflow data = 2011-2023

## Slide 7: Discharge reconstruction
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 8: Discharge reconstruction
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 9
Availability of inflow data for the 14 reference basins
9

## Slide 10
DREAM Model
DREAM is a distributed hydrological model developed to process the state of soil imbibition at the daily scale and at the hourly scale.
Manfreda, S., M. Fiorentino, V. Iacobellis, “DREAM: a Distributed model for Runoff, Evapotranspiration, and Antecedent Soil Moisture Simulation”. Advances in Geosciences, 2, 31–39, 2005.
Schematization of incoming and outgoing fluxes related to a single representative soil cell (Manfreda et al., 2004)
The DREAM model represents the soil as a bucket with limited capacity (Manabe, 1969). According to the basin discretization, the model uses two different balance equations for the calculation of vertical or lateral flows, applied above and below the soil surface. The first equation relates to the soil water content at the time t + Δt, while the second refers to the total runoff cumulated during the time step Δt (Rtot,t+Δt).
Where It (mm/Δt) is the water infiltrated into the soil, ETsoil (mm/Δt) is the evapotranspiration from the soil, RGt (mm/Δt) is the water percolated into the deep soil, RSt (mm/Δt) is the subsurface lateral flow into the computational cell, Smax (mm) is the soil water capacity, Pgross,t (mm/Δt) is the gross precipitation, ΔWint,t (mm/Δt) is the water intercepted by the canopy, ΔWdep,t (mm/Δt) is the water stored into the surface depression, and SSt (mm/Δt) is the saturation‐excess OF.
1)

## Slide 11
Precipitation
Canopy Interception
Evaporation from Canopy
Throughfall
Infiltration
Evapotraspiration from Soil
Deep Percolation
Net Rainfall Excess
Depression Storage
Infiltration Excess Overland Flow
Evaporation from Depression
Total Runoff
Base Flow
Total Discharge
Boudary condition
Surface processes
Surface losses
Soil processes
Soil losses
Discharge
DREAM Model

## Slide 12: DREAM model Dataset
Data | Resolution | Source
Digital Elevation Model | 1km, 500 m | STRM
Land Use | 100 m | Corine Land Cover
Topsoil physical properties: clay content (%) | 500 m | ESDAC https://esdac.jrc.ec.europa.eu
Topsoil physical properties: sand content (%) | 500 m | ESDAC https://esdac.jrc.ec.europa.eu
Topsoil physical properties: Silt content (%) | 500 m | ESDAC https://esdac.jrc.ec.europa.eu
Topsoil physical properties: soil texture | 500 m | ESDAC https://esdac.jrc.ec.europa.eu
Topsoil physical properties: organic matter content (%) | 1000 m | ESDAC https://esdac.jrc.ec.europa.eu
LAI | 500m | MODIS – LAI MCD15A3H v061
Daily rainfall | 1km | CIMA
Mean, maximum, minimum daily temperature | 1km | CIMA
All the maps have been upscaled to the spatial resolution of 1 km

## Slide 13
Correction Precipitation data
~ 1900 mm
Very big value
Correcting the CIMA maps using the BIG BANG maps, but at the same time, we are also working on generating precipitation and temperature maps based on the measured data.

## Slide 14: Calibration
Setup 1:
Reference Series :Surface runoff from Acerenza, Camastra, Conza, Pertusillo, Serra del Corvo;
Calibration period : 2019;
Method : Multi-objective Genetic Algorithm;
Objective function : KGE on chronological time-series ;
Parameter :
Correction coefficient for Root depth : 0.54 [0.1 ; 1]
Correction coefficient for Ks : 0.01 [0.01 ; 2]
Correction coefficient for Runoff coefficient : 0. 86 [0.01 ; 2 ]
Expopential of runoff De Smedt equation : 1.83 [0.01 ; 3 ]

## Slide 15: Calibration
Setup 2:
Reference Series :Total Discharge from Acerenza, Camastra, Conza, Pertusillo, Fiumarella, Turbolo;
Calibration period : 2019;
Method : Multi-objective Genetic Algorithm;
Objective function : KGE on chronological time-series ;
Parameter :
Correction coefficient for Root depth : 0.47 [0.1 ; 1]
Correction coefficient for Ks topsoil : 0.72 [0.005 ; 2]
Correction coefficient for Ks deepsoil : 0.46 [0.01 ; 2]
Correction coefficient for Runoff coefficient : 0. 86 [0.01 ; 2 ]
Expopential of runoff De Smedt equation : 1.45 [0.01 ; 3 ]

## Slide 16: Calibration
Setup 3:
Reference Series : Flow duration Curves from Acerenza, Camastra, Conza, Pertusillo, Fiumarella, Turbolo;
Calibration period : 2019;
Method : Multi-objective Genetic Algorithm;
Objective function : RMSE on Flow Duration Curves ;
Parameter :
Correction coefficient for Root depth : 0.47 [0.1 ; 1]
Correction coefficient for Ks topsoil : 0.071 [0.005 ; 2]
Correction coefficient for Ks deepsoil : 0.33 [0.01 ; 2]
Correction coefficient for Runoff coefficient : 0. 78 [0.01 ; 2 ]
Expopential of runoff De Smedt equation : 1.61 [0.01 ; 3 ]

## Slide 17
Calibration Results

## Slide 18
Calibration Results

## Slide 19
Calibration Results

## Slide 20: Calibration Results
Calibration Setup 1
Calibration Setup 2
Calibration Setup 3
Blue is observed Discharge
Red is Simulated Discharge
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 21: Calibration Results
Calibration Setup 1
Calibration Setup 2
Calibration Setup 3
Blue is observed Discharge
Red is Simulated Discharge
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 22: Calibration Results
Calibration Setup 1
Calibration Setup 2
Calibration Setup 3
Blue is observed Discharge
Red is Simulated Discharge
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 23: Validation results

## Slide 24
-14.04
-14.94
-12.45
-8.70
-3.89
Validation results

## Slide 25
Validation results

## Slide 26: Validation results
Calibration Setup 1
Calibration Setup 2
Calibration Setup 3
Blue is observed Discharge
Red is Simulated Discharge
Black is Warm-up period
Magenta is Calibration period
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 27: Validation results
Calibration Setup 1
Calibration Setup 2
Calibration Setup 3
Blue is observed Discharge
Red is Simulated Discharge
Black is Warm-up period
Magenta is Calibration period
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 28: Validation results
Calibration Setup 1
Calibration Setup 2
Calibration Setup 3
Blue is observed Discharge
Red is Simulated Discharge
Black is Warm-up period
Magenta is Calibration period
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 29: Validation results
Calibration Setup 1
Calibration Setup 2
Calibration Setup 3
Blue is observed Discharge
Red is Simulated Discharge
Black is Warm-up period
Magenta is Calibration period
Notes: La modellazione idrologica gioca un ruolo chiave non solo nella descrizione dei fenomeni idrologici ma anche nella quantificazione e gestione ottimale delle disponibilità idriche. La principale sfida che si è chiamati ad affrontare quando si parla di modellazione idrologica è la calibrazione dei modelli, sfida che divine particolarmente interessante e ardua quando si parla di applicazioni a larga scala e in aree con scarsa disponibilità di dati.
In questo lavoro insieme ai miei co-autori ci siamo

## Slide 30: Forward developments
Include a SNOW meting module in DREAM model to improve the model performance;
Try to integrate remote sensing data of Soil moisture and snow cover / Snow water equivalent in the calibration to improve the spatial variability of modelled phenomena;
Use of specific performace index that describe the spacial variability;
Improve calibration with a longer period;

## Slide 31: Reference
Braca, G., Mariani, S., Lastoria, B., Tropeano, R., Casaioli, M., Piva, F., Marchetti, G., e Bussettini, M., 2024: Bilancio idrologico nazionale: stime BIGBANG e indicatori sulla risorsa idrica. Aggiornamento al 2023. Rapporti n. 401/2024, ISPRA, Roma.
De Smedt, F., Yongbo, L., & Gebremeskel, S. (2000). Hydrologic modelling on a catchment scale using GIS and remote sensed land use information. WIT Transactions on Ecology and the Environment, 45.
Dickinson, R. E. (1984). Modeling evapotranspiration for three‐dimensional global climate models. Climate Processes and Climate Sensitivity, 29, 58–72.
Francés, Félix, Jaime Ignacio Vélez, and Jorge Julián Vélez. "Split-parameter structure for the automatic calibration of distributed hydrological models." Journal of Hydrology 332.1-2 (2007): 226-240.
Eagleson, P. S. (1978). Climate, soil, and vegetation: 5. A derived distribution of storm surface runoff. Water Resources Research, 14(5), 741–748.
Manfreda, S., L. Mita, S. F. Dal Sasso, C. Samela, L. Mancusi, Exploiting the Use of Physical Information for the Calibration of a Lumped Hydrological Model, Hydrological Processes, 32(10), 1420-1433, (doi: 10.1002/hyp.11501) 2018
Perrini, P., L. Cea, F. Chiaravalloti, S. Gabriele, S. Manfreda, M. Fiorentino, A. Gioia, V. Iacobellis, A Runoff-On-Grid approach to embed hydrological processes in shallow water models, Water Resources Research, 2024
Ruiz-Pérez, G., J. Koch, S. Manfreda, K.K. Caylor, F. Francés, Calibration of a parsimonious distributed ecohydrological daily model in a data scarce basin using exclusively the spatio-temporal variation of NDVI, Hydrology and Earth System Sciences, 21, 6235-6251, (doi: 10.5194/hess-21-6235-2017) 2017

## Slide 32
HydroLab

## Slide 33
Contact:
Prof. Salvatore Manfreda : salvatore.manfreda@unina.it
Felice Daniele Pacia: felice.pacia@iusspavia.it
Avino Angelo : angelo.avino@unina.it
Pasquale Perrini : pasquale.perrini@uniba.it

## Slide 36
2024
Hydrological Modelling - DREAM model
DREAM is a distributed hydrological model developed to process the state of soil imbibition at the daily scale and at the hourly scale.
The two modules can be used disjointly for different purposes or work in cascade in a single model for flood simulation that takes due account of the spatial and temporal variability of soil imbibition states.
The model is physically based and schematizes the basin through grid discretization. This discretization permits to consider the spatial heterogeneity of the basin using data contained in digital elevation models, land use maps, soil texture maps, hydraulic soil properties and vegetation parameters.

## Slide 37
DREAM Model
DREAM is a distributed hydrological model developed to process the state of soil imbibition at the daily scale and at the hourly scale.
Manfreda, S., M. Fiorentino, V. Iacobellis, “DREAM: a Distributed model for Runoff, Evapotranspiration, and Antecedent Soil Moisture Simulation”. Advances in Geosciences, 2, 31–39, 2005.
Schematization of incoming and outgoing fluxes related to a single representative soil cell (Manfreda et al., 2004)
The DREAM model represents the soil as a bucket with limited capacity (Manabe, 1969). According to the basin discretization, the model uses two different balance equations for the calculation of vertical or lateral flows, applied above and below the soil surface. The first equation relates to the soil water content at the time t + Δt, while the second refers to the total runoff cumulated during the time step Δt (Rtot,t+Δt).
Where It (mm/Δt) is the water infiltrated into the soil, ETsoil (mm/Δt) is the evapotranspiration from the soil, RGt (mm/Δt) is the water percolated into the deep soil, RSt (mm/Δt) is the subsurface lateral flow into the computational cell, Smax (mm) is the soil water capacity, Pgross,t (mm/Δt) is the gross precipitation, ΔWint,t (mm/Δt) is the water intercepted by the canopy, ΔWdep,t (mm/Δt) is the water stored into the surface depression, and SSt (mm/Δt) is the saturation‐excess OF.
1)

## Slide 38
Hydrological Modelling - DREAM model
The storage capacity of vegetation is schematized by the expression proposed by Dickinson (1984);
The actual evapotranspiration is represented in the model by four conceptual components, two for the vegetated fraction of the surface (〖ET〗_veg,E_can) and two for the remaining bare surface (〖E_bare,E〗_dep).(Perrini et al 2024)
Infiltration into the soil is modelled as described in De Smedt et al 2000.
Deep percolation losses are related to relative soil moisture according to a power function (Egelson, 1978).
Schematization of incoming and outgoing fluxes related to a single representative soil cell (Manfreda et al., 2004)

## Slide 39: Base flow extraction
Base flow rates are estimated by interpolation, using cubic splines, on the series of minimum recorded values and identified using the Matlab 'findpeaks' function applied to recorded values of flow rates below the mean plus the standard deviation.
m3/s
t
Base flow

## Slide 40
m3/s
t
Surface runoff
Surface runoff was calculated as the difference between the total discharge and the extracted base flow.
SR = TD - BF
Surface Runoff extraction

## Slide 41
SNOW Module – DREAM
The snow module incorporated into the DREAM model combines the reduced degree-day algorithm (for estimating accumulated degree-days) with an energy and mass balance method, thus leading to a more accurate and physically-based modeling of the energy exchange processes between the snow cover and the surrounding environment.
is the snowmelt height [mm];
is a physical constant for the conversion of energy into water height [=0.26 mm W-1m2day-1] ;
is the net solar radiation [Wm-2];
T is the daily average temperature [°C];
is the reduced degree-day factor [mm °C-1day-1]
N.B. The reduced degree-day factor varies less over time than the classic degree-day factor
q*
T1
T2
Snow-air interface
Snow-ground
interface
SNOWPACK
d=d(rsnow)
(rsnow , lsnow , d)
AIR
(Tair , aair)
Snowpack
medium level
d/2
d/2

## Slide 42
SNOW Module – DREAM
The module contains six calibration parameters:
DT a parameters useful to control the rainfall/snowfall partitioning;
Mf restricted degree day factor;
Mfr refreezing day factor;
WT a parameter controlling the water retained by the snowpack;
Tn freezing temperature;
T0 melting temperature.
For the calibration of the DREAM snow module, the recent IT-SNOW dataset is used as a reference.
The grid-based model is calibrated using a composite objective function, which considers:
Spatially averaged daily SWE
Coefficient of variation of daily SWE
Skewness of daily SWE
Number of cells with positive SWE.
For each of the four variables are computed the KGEs. Later, the averaged KGE is used as objective function of a Gradient-based Meta Heuristic optimizer.