## Slide 1
Compact Soil (Barrier for Water Flow)
Water puddle in rural areas could be due to compact soil
Soil de-compaction for more groundwater recharge
Deep Percolation Leading to Groundwater Recharge?
No more puddle.
More infiltration. More recharge!
1
How much can be recharged? Solve using hydrological models
Wait! Are you sure about me…?
Here, we show:
Uncertainties in vegetation can largely change model outcomes!

## Slide 2
What we did: Experimental Plots
Presenter: Jayson Pinza
What we did: HYDRUS-1D numerical models
Compact Sand
LooseSand
Loose Sand
Loose Sand
Evaporation
Deep Percolation
(Groundwater Recharge)
Transpiration
Stored Soil
Moisture
New Evaporation?
New Transpiration?
New Stored
Soil Moisture?
Compact Sand
Loose Sand
Loose Sand
De-compacted
Compacted
New
Deep Percolation?
Change Root
Depth
Change LAI
Visit our PICO Spot 4.6!

## Slide 3
(3) Numerical Modeling
(2) Experimental Setup
Home Page. Click a section below
(4) Conclusion
(1) Introduction
Photo © US Department of Agriculture (n.d.)
Presenter:
Jayson Gabriel Pinza
University of Antwerp
KU Leuven
Belgium
jayson.pinza@uantwerpen.be
Co-authors:
Ona-Abeni D. Stoffels
Robrecht Debbaut
Patrick Willems
Jan Vanderborght
Sarah Garré
Jan Staes
Hydrological impacts of compacted sandy subsoils & soil water flow simulations (importance of vegetation parameterization)
Scan for the Abstract (OSPP)!
Scan for the Preprint (under review)!

## Slide 4
(3) Numerical Modeling
(2) Experimental Setup
(4) Conclusion
(1) Introduction
Photo © US Department of Agriculture (n.d.)
Hydrological impacts of compacted sandy subsoils & soil water flow simulations (importance of vegetation parameterization)
Click next to proceed.
Otherwise, either click home or the inactive box for other sections

## Slide 5
Photo © Jan Staes, 2022
Compact Soil (Barrier for Water Flow)
Photo © Jan Staes (2022)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
Water puddle in rural areas could be due to compact soil
(4) Conclusion

## Slide 6
Photo © Jan Staes, 2022
Compact Soil (Barrier for Water Flow)
Photo © Jan Staes (2022)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
Water puddle in rural areas could be due to compact soil
Soil de-compaction for more groundwater recharge
Deep Percolation Leading to Groundwater Recharge?
No more puddle.
More infiltration. More recharge!
(4) Conclusion

## Slide 7
Photo © Jan Staes, 2022
Water puddle in rural areas could be due to compact soil
Photo © Jan Staes (2022)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
Soil de-compaction for more groundwater recharge
Deep Percolation Leading to Groundwater Recharge?
No more puddle.
More infiltration. More recharge!
How much can be recharged? Solve using hydrological models
(4) Conclusion

## Slide 8: In these models, however, vegetation is a problem
Why? Often parameterized using only:
  limited field measurements
  literature
  derivations from other variables
Adapted from Philip Halling (2022) (Creative Commons License)
Are you sure about me…?
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 9: Here, we show:
Uncertainties in vegetation can cause large changes in model outcomes!
Adapted from Philip Halling (2022) (Creative Commons License)
Check me again, please…
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 10
(3) Numerical Modeling
(2) Experimental Setup
(4) Conclusion
(1) Introduction
Photo © US Department of Agriculture (n.d.)
Hydrological impacts of compacted sandy subsoils & soil water flow simulations (importance of vegetation parameterization)
Click next to proceed.
Otherwise, either click home or the inactive box for other sections

## Slide 11
(2) Experimental Setup
Photo © Belgium-mapped-out, 2003
Study area
Setting: sandy soils of Campine Region (Northeast Belgium)
More info on the site’s soil profile
Hydrological impacts of compacted sandy subsoils & soil water flow simulations (importance of vegetation parameterization)
(1) Introduction
(3) Numerical Modeling
(4) Conclusion

## Slide 12: Subsoil compaction has already been present for 50 years
Depth [cm]
Penetrologger Profile
General Soil Profile
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 13: 2 setup cases considered:
Plots have grasses (Italian ryegrass)
Exposed under the sun/rain
Occasionally irrigated and mowed
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 14: 2 setup cases considered:
Only loose sand
With compact sand (40-55 cm depth)
Both have sensors at 10- (near surface) & 40-cm depth (above compact layer)
More info on
De-compaction
Sensor Photo
© HOBO, n.d.
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 15: De-compaction had lower penetration resistances across the profile
More info on De-compaction
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 16: De-compaction had reduced soil moisture content @ 40-cm depth
Precipitation
Irrigation
Average ± standard deviation
Amount [mm]
Soil Moisture (cm3/cm3)
40-cm depth (above compact layer)
10-cm depth
n = 4
n = 4
n = 4
Average ± standard deviation
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
n = 4
Compacted
De-compacted

## Slide 17: De-compaction had reduced soil moisture content @ 40-cm depth
More soil moisture
Less soil moisture because “barrier” (compact layer) is removed)
Precipitation
Irrigation
Average ± standard deviation
Amount [mm]
Soil Moisture (cm3/cm3)
40-cm depth (above compact layer)
10-cm depth
n = 4
n = 4
n = 4
n = 4
Average ± standard deviation
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
Compacted
De-compacted

## Slide 18: De-compaction had reduced soil moisture content @ 40-cm depth
These are exceptional
(influence of
groundwater?)
More soil moisture
Less soil moisture because “barrier” (compact layer) is removed)
Precipitation
Irrigation
Average ± standard deviation
Amount [mm]
Soil Moisture (cm3/cm3)
40-cm depth (above compact layer)
10-cm depth
n = 4
n = 4
n = 4
n = 4
Average ± standard deviation
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
Compacted
De-compacted

## Slide 19: De-compaction increased LAI and root depth
More info on LAI
More info on
Root Distribution
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 20: De-compaction increased grass’ LAI
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 21: De-compaction increased grass’ LAI
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 22: De-compaction increased root depths too
Depth
[cm]
Depth
[cm]
n=4
n=4
n=4
n=4
No more roots!
Not much roots!
Still has roots!
Still has roots!
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 23: Now, per plot: quantify the hydrological processes
Evaporation
Deep Percolation
(Groundwater Recharge)
Stored Soil Moisture
Transpiration
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 24: Now, per plot: quantify the hydrological processes
Evaporation
Deep Percolation
(Groundwater Recharge)
Stored Soil Moisture
Transpiration
New Evaporation?
New
Deep Percolation?
New Transpiration?
New Stored
Soil Moisture?
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 25: Now, per plot: quantify the hydrological processes
Evaporation
Deep Percolation
(Groundwater Recharge)
Stored Soil Moisture
Transpiration
New Evaporation?
New
Deep Percolation?
New Transpiration?
New Stored
Soil Moisture?
Use a 1D numerical model
(HYDRUS-1D)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 26
(3) Numerical Modeling
(2) Experimental Setup
(4) Conclusion
(1) Introduction
Photo © US Department of Agriculture (n.d.)
Hydrological impacts of compacted sandy subsoils & soil water flow simulations (importance of vegetation parameterization)
Click next to proceed.
Otherwise, either click home or the inactive box for other sections

## Slide 27: 1D Model Layers
Loose Sand
Compact Sand
40 cm
15 cm
Loose Sand
45 cm
De-compacted
Compacted
298 cm/day
1.3 cm/day
(so, it hinders water flow)
Saturated
Hydraulic Conductivity
[Ksat]
298 cm/day
All K sat values are obtained
from calibrations by inverse modeling
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 28: 1D Model Layers
Loose Sand
Compact Sand
40 cm
15 cm
Compacted Sand Layer
LooseSand
Loose Sand
45 cm
100 cm
De-compacted
Compacted
298 cm/day
1.3 cm/day
(so, it hinders water flow)
Saturated
Hydraulic Conductivity
[Ksat]
298 cm/day
All K sat values are obtained
from calibrations by inverse modeling
298 cm/day
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 29: 1D Model Boundary Conditions
Compacted
De-compacted
LooseSand
Loose Sand
Loose Sand
Compact Sand
Upper Boundary:
We permitted atmospheric processes
(e.g., precipitation, evapotranspiration)
(1) Introduction
(2) Experimental Setup
(4) Conclusion
(3) Numerical Modeling

## Slide 30: 1D Model Boundary Conditions
Compacted
De-compacted
LooseSand
Loose Sand
Loose Sand
Compact Sand
Upper Boundary:
We permitted atmospheric processes
(e.g., precipitation, evapotranspiration)
Assumption: Water Table is deep
Lower Boundary:
Water drains freely
(1) Introduction
(2) Experimental Setup
(4) Conclusion
(3) Numerical Modeling

## Slide 31: 2 approaches were considered to parameterize vegetation (grass)
Compact Sand
40 cm
15 cm
LooseSand
Loose Sand
45 cm
60 cm
De-compacted
Compacted
40 cm
Photo of Grass
© Shmector.com (n.d.)
Loose Sand
Approach 1: Same High LAI, Same Shallow Roots
(1) Introduction
(2) Experimental Setup
(4) Conclusion
(3) Numerical Modeling

## Slide 32: 2 approaches were considered to parameterize vegetation (grass)
Compact Sand
40 cm
15 cm
LooseSand
Loose Sand
45 cm
60 cm
De-compacted
Compacted
40 cm
Loose Sand
Approach 1: Same High LAI, Same Shallow Roots
Compact Sand
40 cm
15 cm
Loose Sand
45 cm
De-compacted
Compacted
100 cm
Loose Sand
Approach 2 (based on field observations) De-compacted has more LAI and deeper roots
Loose Sand
Deeper Roots
Lower LAI
More info on
Model Performances
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 33: The 1D models from both approaches capture the general soil water behavior
10-cm depth
Months
2022
2023
2024
2022
2023
2024
Soil moisture [cm3/cm3]
40-cm depth
De-compacted
Compacted
Observed
Observed
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 34: The 1D models from both approaches capture the general soil water behavior
10-cm depth
Months
2022
2023
2024
2022
2023
2024
Except for these
(influence of
groundwater?)
Soil moisture [cm3/cm3]
40-cm depth
Observed
Simulated (Approach1)
Simulated
(Approach1)
Observed
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
Compacted
De-compacted

## Slide 35: The 1D models from both approaches capture the general soil water behavior
10-cm depth
Months
2022
2023
2024
2022
2023
2024
Except for these
(influence of
groundwater?)
Soil moisture [cm3/cm3]
40-cm depth
Observed
Simulated (Approach1)
Simulated
(Approach1)
Observed
Simulated (Approach2)
Simulated (Approach2)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
Compacted
De-compacted

## Slide 36: The 1D models from both approaches capture the general soil water behavior
10-cm depth
Months
2022
2023
2024
2022
2023
2024
Except for these
(influence of
groundwater?)
Soil moisture [cm3/cm3]
40-cm depth
Observed
Simulated (Approach1)
Simulated
(Approach1)
Observed
Simulated (Approach2)
Simulated (Approach2)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
Compacted
De-compacted
We can now use the models
to simulate climate scenarios
(Neglecting groundwater influence)

## Slide 37: We simulate under future climate scenarios:
Annual Precipitation
Annual Potential Evapotranspiration
More Info on these Climate Scenarios
Amount
[mm]
Historical
(1971–2000)
Future Dry
(2071–2100)
Future Wet
(2071–2100)
Historical
(1971–2000)
Future Dry
(2071–2100)
Future Wet
(2071–2100)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 38: More details on the future climate scenarios
Scenario | Future Wet | Future Dry
Years Covered | 2071–2100 | 2071–2100
Main Basis for Selection | 95 percentile mean annual hydric excess (Precipitation minus Potential Evapotranspiration) | 95 percentile mean annual hydric deficit (Potential Evapotranspiration minus Precipitation)
RCP | RCP4.5 | RCP6.0
Regional Climate Model | HadGEM2-CC-r1 | MIROC-ESM-r1
Statistical Downscaling Method | Quantile Perturbation Method (Willems and Vrac, 2011)* | Quantile Perturbation Method (Willems and Vrac, 2011)*
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
*Willems, P. and Vrac, M.: Statistical precipitation downscaling for small-scale hydrological impact investigations of climate change, J. Hydrol., 402, 193–205

## Slide 39: Result: Decompaction seems to increase deep percolation, thus reducing evaporable and storable water
Compact Sand
LooseSand
Loose Sand
De-compacted
Compacted
Loose Sand
Approach 1: Same High LAI, Same Shallow Roots
(+) Deep Percolation
(Wet: +38 | Dry: +21)
(–) Evaporation
(Wet: –37 | Dry: –24)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –24 | Dry: –18)
(=) Transpiration
[mm/yr]
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
Photo of Grass
© Shmector.com (n.d.)

## Slide 40: What if we change the vegetation parameterization?
Compact Sand
LooseSand
Loose Sand
De-compacted
Compacted
Photo of Grass
© Shmector.com (n.d.)
Loose Sand
Approach 1: Same High LAI, Same Shallow Roots
Compact Sand
Loose Sand
De-compacted
Compacted
Loose Sand
Approach 2 (based on field observations) De-compacted has higher LAI and deeper roots
Loose Sand
(+) Deep Percolation
(Wet: +38 | Dry: +21)
(–) Evaporation
(Wet: –37 | Dry: –24)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –24 | Dry: –18)
(=) Transpiration
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 41: Result: Considering de-compaction’s impacts to vegetation, more grown vegetation takes up deeper water too
Compact Sand
LooseSand
Loose Sand
De-compacted
Compacted
Loose Sand
Approach 1: Same High LAI, Same Shallow Roots
Compact Sand
Loose Sand
De-compacted
Compacted
Loose Sand
Approach 2 (based on field observations) De-compacted has higher LAI and deeper roots
Loose Sand
(+) Deep Percolation
(Wet: +38 | Dry: +21)
(–) Evaporation
(Wet: –37 | Dry: –24)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –24 | Dry: –18)
(=) Transpiration
(±) Deep Percolation
(Wet: +7 | Dry: –23)
(–) Evaporation
(Wet: –45 | Dry: –32)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –22 | Dry: –18)
(+) Transpiration
(Wet: +36 | Dry: +59)
[mm/yr]
The boxplots of all values are here
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion
Photo of Grass
© Shmector.com (n.d.)

## Slide 42: Annual values
De-compacted minus Compacted (+) : De-compacted > Compacted (–) : De-compacted < Compacted
Transpiration
[mm]
Evaporation
[mm]
Stored Soil
Moisture
(0–40 cm depth)
[mm]
Approach 1: Same High LAI, Same Shallow Roots
Approach 2 (based on field observations) De-compacted has higher LAI and deeper roots
Deep Percolation
[mm]
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 43
(3) Numerical Modeling
(2) Experimental Setup
(4) Conclusion
(1) Introduction
Photo © US Department of Agriculture (n.d.)
Hydrological impacts of compacted sandy subsoils & soil water flow simulations (importance of vegetation parameterization)
Click next to proceed.
Otherwise, either click home or the inactive box for other sections

## Slide 44: Outcomes on hydrological variables are different! Thus, vegetation parameterization matters a lot!
Compact Sand
LooseSand
Loose Sand
De-compacted
Compacted
Photo of Grass
© Shmector.com (n.d.)
Loose Sand
Approach 1: Same High LAI, Same Shallow Roots
Compact Sand
Loose Sand
De-compacted
Compacted
Loose Sand
Approach 2 (based on field observations) De-compacted has more LAI, deeper Roots
Loose Sand
(+) Deep Percolation
(Wet: +38 | Dry: +21)
(–) Evaporation
(Wet: –37 | Dry: –24)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –24 | Dry: –18)
(=) Transpiration
(±) Deep Percolation
(Wet: +7 | Dry: –23)
(–) Evaporation
(Wet: –45 | Dry: –32)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –22 | Dry: –18)
(+) Transpiration
(Wet: +36 | Dry: +59)
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 45: So what? Differing model approaches? Conflicting water management strategies
Compact Sand
LooseSand
Loose Sand
De-compacted
Compacted
Photo of Grass
© Shmector.com (n.d.)
Loose Sand
Approach 1: Same High LAI, Same Shallow Roots
Compact Sand
Loose Sand
De-compacted
Compacted
Loose Sand
Approach 2 (based on field observations) De-compacted has more LAI, deeper Roots
Loose Sand
(–) Evaporation
(Wet: –37 | Dry: –24)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –24 | Dry: –18)
(=) Transpiration
(–) Evaporation
(Wet: –45 | Dry: –32)
(–) Soil Moisture
at 0–40 cm depth
(Wet: –22 | Dry: –18)
(+) Transpiration
(Wet: +36 | Dry: +59)
(+) Deep Percolation
(Wet: +38 | Dry: +21)
(±) Deep Percolation
(Wet: +7 | Dry: –23)
Hey, we must de-compact to have more recharge!
Wait! Maybe better to leave the soil alone…
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion

## Slide 46: So what? For soil (de-)compaction’s hydrological models:
Know how (de-)compaction affects vegetation growth
Adapted from Philip Halling (2022) (Creative Commons License)
I hope you take me more seriously now…
Field evidence of vegetation growth is vital!
(1) Introduction
(2) Experimental Setup
(3) Numerical Modeling
(4) Conclusion