## Slide 1
EGU25-9750
Ten-year trend of PM2.5 sulfate, nitrate, and other inorganic constituents from 2012 to 2021 at urban and suburban sites of Hong Kong, China
Session AS3.32
Presenter: Zijing ZHANG
Email: zzhangfi@connect.ust.hk
April 28, 2025
Zhang, Z. and Yu, J.: Ten-year trend of PM2.5 sulfate, nitrate, and other inorganic constituents from 2012 to 2021 in urban and suburban sites of Hong Kong, China, EGU General Assembly 2025, Vienna, Austria, 27 Apr–2 May 2025, EGU25-9750, https://doi.org/10.5194/egusphere-egu25-9750, 2025.

## Slide 2: 1. Introduction and Method
Sampling sites
  Urban: Yuen Long Air Quality Monitoring Station (YL)
  Suburban: HKUST Supersite (UST)
Offline vs. online monitoring
  Offline: Mid-volume sampler with Teflon filters
  Online: Monitor for AeRosols and Gases in Ambient air (MARGA)
Offline sampler
Online MARGA
YL
UST

## Slide 3: 2. Results and conclusions
PM2.5 showed a decreasing trend over the years (p < 0.01), and sulfate contributed around 40% of the reduction.
Nitrate and ammonium took up a larger mass fraction of PM2.5.
Fig. 1 Annual trend of filter measured concentration of PM2.5 and total inorganic ions.
Fig. 3 Annual trend of filter-measured mass fractions of inorganic ions.
Fig. 2 Annual trend of filter measured concentration of each ion.

## Slide 4: 2. Results and conclusions
Particulate nitrate concentration was under-measured by filter-based sampling under high temperature conditions (>23oC).
Fig. 4 Comparison between offline filter- and online MARGA-measured nitrate concentrations
Filter
MARGA
Fig. 5 Annual trend of mass fractions of inorganic ions

## Slide 5: Thank you for your attention!
EGU25-9750
Session AS3.32

## Slide 6: Offline filter results
Annual trend of PM2.5 and the inorganic constituents
PM2.5 concentration decreased by 1.49 ug/m3 and 1.24 ug/m3 per year on average in YL and UST, respectively. Inorganic compounds took up ~50% of PM2.5 mass.
Sulfate was the dominant constituent in both sites.

## Slide 7
Annual trend of PM2.5 and the inorganic constituents
Variation (μg/m3/yr) | SO42- | NO3- | NH4+ | Cl- | NVC | PM2.5
YL | -0.60 | -0.03 | -0.17 | -0.005 | -0.04 | -1.49
UST | -0.60 | +0.02 | -0.15 | 0.00 | -0.05 | -1.24
Offline filter results

## Slide 8
Annual trend of mass fraction of inorganic constituents
The mass fraction of sulfate in inorganic compounds gradually decreased, while the fraction of nitrate increased over the years in both sites.
Offline filter results

## Slide 9
The trend was comparable between YL and UST.
Nitrate concentration was very low in summer according to filter measurement result.
Annual trend of PM2.5 and the inorganic constituents during summer in urban YL and suburban UST
Offline filter results

## Slide 10
Variation (μg/m3/yr) | SO42- | NO3- | NH4+ | Cl- | NVC | PM2.5
YL | -0.35 | -0.01 | -0.10 | 0.00 | -0.04 | -0.88
UST | -0.37 | 0.00 | -0.10 | 0.00 | -0.05 | -0.82
Annual trend of PM2.5 and the inorganic constituents during summer in urban YL and suburban UST
Offline filter results

## Slide 11
The annual trend of winter was also comparable between YL and UST.
Nitrate concentration in urban YL was higher than in suburban UST
Annual trend of PM2.5 and the inorganic constituents during winter in urban YL and suburban UST
Offline filter results

## Slide 12
Variation (μg/m3/yr) | SO42- | NO3- | NH4+ | Cl- | NVC | PM2.5
YL | -0.72 | -0.14 | -0.26 | -0.02 | -0.05 | -2.11
UST | -0.73 | +0.03 | -0.21 | 0.00 | -0.05 | -1.65
Annual trend of PM2.5 and the inorganic constituents during winter in urban YL and suburban UST
Offline filter results

## Slide 13
Comparison between offline filter measured and online MARGA measured nitrate concentration.
Offline vs. Online
The correlation was less satisfying under high temperature conditions.
High temperature will introduce more uncertainty into offline filter measurement.

## Slide 14
Comparison between offline filter measured and online MARGA measured nitrate concentration under high and low temperature condition.
Offline vs. Online
The correlation was much better under low temperature condition.

## Slide 15
Offline vs. Online
Filter
MARGA

## Slide 16
Comparison between annual trend of summer derived from offline filter and online MARGA
Offline vs. Online
Variation (μg/m3/yr) | SO42- | NO3- | NH4+ | Cl- | NVC | PM2.5
Filter | -0.37 | 0.00 | -0.10 | 0.00 | -0.05 | -0.82
MARGA | -0.33 | +0.09 | -0.07 | 0.00 | -0.05 | -
Filter
MARGA

## Slide 17
Comparison between annual trend of winter derived from offline filter and online MARGA
Offline vs. Online
Variation (μg/m3/yr) | SO42- | NO3- | NH4+ | Cl- | NVC | PM2.5
Filter | -0.73 | +0.03 | -0.21 | 0.00 | -0.05 | -1.65
MARGA | -0.83 | +0.24 | -0.26 | -0.03 | -0.03 | -
Filter
MARGA

## Slide 18
Corrected annual trend of ion concentration in UST site with nitrate replaced by MARGA measured results.
Offline vs. Online