## Slide 1
“Integration of stochastic and statistical approaches for drought risk estimation
through long-length time series”
Sofia Efraimia Vrettou1, Demetris Koutsoyiannis2, Panayiotis Dimitriadis2, Theano Iliopoulou2 and Alberto Montanari1
1Department of Civil, Chemical, Environmental and Materials Engineering (DICAM), Alma Mater Studiorum – University of Bologna, Bologna, Italy
2Department of Water Resources and Environmental Engineering, School of Civil Engineering, National Technical University of Athens (NTUA), Athens, Greece
Photo by Kiptoo Addi, via Pexels (https://www.pexels.com/el-gr/photo/14924252/)

## Slide 2
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
Sofia Efraimia Vrettou1, Demetris Koutsoyiannis2, Panayiotis Dimitriadis2, Theano Iliopoulou2 and Alberto Montanari1
1Department of Civil, Chemical, Environmental and Materials Engineering (DICAM), Alma Mater Studiorum – University of Bologna, Bologna, Italy
2Department of Water Resources and Environmental Engineering, School of Civil Engineering, National Technical University of Athens (NTUA), Athens, Greece
Droughts are among the most impactful and costly natural hazard-related disasters.
Need for better understanding of the drivers and their underlying mechanisms leading to the droughts, mitigate impacts create resilient societies.
Stochastic models simulate the natural variability of the natural processes.
Focus on the meteorological droughts  study of precipitation patterns
Specify the multi-year drought characteristics through the application of stochastic models
Use as a case study the precipitation time series of Bologna, Italy.
Suggest a framework of integration of two different stochastic models applied in daily and annual time scales.
Apply Monte Carlo simulation approach.
Specify the multi-year drought characteristics: drought intensity, duration, frequency and maximum deficit through the application of run theory.
Introduction:
Scope of work:
Methodology- Novelty:

## Slide 3
Acknowledgement: This study was carried out within the RETURN Extended Partnership and received funding from the European Union Next-Generation EU (National Recovery and Resilience Plan – NRRP, Mission 4, Component 2, Investment 1.3 – D.D. 1243 2/8/2022, PE0000005)
Thank you for your attention!
For results: PICO spot A.7

## Slide 4
“Integration of stochastic and statistical approaches for drought risk estimation
through long-length time series”
Photo by Kiptoo Addi, via Pexels (https://www.pexels.com/el-gr/photo/14924252/)
Introduction
Methodology
Objectives
Theoretical background
Results
Acknowledgement: This study was carried out within the RETURN Extended Partnership and received funding from the European Union Next-Generation EU (National Recovery and Resilience Plan – NRRP, Mission 4, Component 2, Investment 1.3 – D.D. 1243 2/8/2022, PE0000005)
1Department of Civil, Chemical, Environmental and Materials Engineering (DICAM), Alma Mater Studiorum – University of Bologna, Bologna, Italy
2Department of Water Resources and Environmental Engineering, School of Civil Engineering, National Technical University of Athens (NTUA), Athens, Greece
Sofia Efraimia Vrettou1, Demetris Koutsoyiannis2, Panayiotis Dimitriadis2, Theano Iliopoulou2 and Alberto Montanari1
Run theory
ARFIMA model
CoSMoS model

## Slide 5
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
Droughts are among the most intense and impactful natural-hazard related disasters (IPCC, 2021; CRED, 2025).
In 2025 18.4 million people were affected* by drought phenomena (the natural disaster that affected the most people in 2025).
Droughts are characterized as “creeping disasters” because it is difficult to specify those onset, termination, extend and potential impact.
To limit the impacts and create resilient societies we need to study the drivers that lead to droughts and estimate their uncertainty.
*Affected people are those requiring immediate assistance due to the disaster.

## Slide 6
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
Stochastic models are capable of capturing and simulating the inherent uncertainty and variability of natural hydroclimatic processes.
They enable the generation of ensembles of synthetic time series that reproduce the statistical characteristics of the observation record.
Through the generation of a synthetic and arbitrarily long time series provide valuable insights into the likelihood of occurrence of the natural process of interest.
Application of advanced stochastic methods pave the way for drought risk awareness and early detection systems like drought monitoring, which can provide societies with evidence for drought anticipation.
By incorporating a stochastic modeling approach, the inherent surprise factor of these natural phenomena could be significantly reduced, allowing policymakers to adopt more efficient mitigation strategies.
A key research challenge remains in the selection of the appropriate stochastic model and the amount of information required to optimize their performance in estimating the probability of occurrence of rare events. In particular, classical simulation models often underestimate the risk associated to multi-year droughts (Guo and Montanari, 2023).

## Slide 7
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
We focus on the study of the meteorological droughts as the initial step of drought propagation.
Study precipitation time series, define precipitation patterns.
The scope of the study is to:
  Improve the estimation of multi-year drought characteristics (drought frequency, intensity, duration, and maximum deficit percentage) applying the well-established run theory throught the implementation of stochastic models.
  Propose an integrated framework of stochastic models that simulate short term variability and long term dependence.
  Compare the resulting statistics with those obtained from climate model projections (SSP2.6, SSP8.5 scenarios).

## Slide 8
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
Methodology:
Stochastic modeling
CoSMoS framework
Run theory
Wet spell
Dry spell
Threshold
Monte Carlo simulation
500 100-year synthetic time series, CoSMoS
Precipitation time series of case study gauging station
Input data
ARFIMA (0,d,0)
model
500 100-year synthetic time series, ARFIMA
synthetic time series CoSMoS+ARFIMA

## Slide 9
Bologna, Italy
209 years of daily data
1813-2021
Moment | Daily values (mm)
Mean | 1.86
Standard Deviation | 6.02
Skewness | 6.17
Kurtosis | 58.97
Daily statistics:
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
Case study:

## Slide 10
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
DD = time span between the start and the end of a negative run
DF =
DI = , DS=
MD =
Threshold (T) = mean annual rainfall Tupper and Tlower are defined as 20% higher and 10% lower than the defined T.
A negative run starts when xi < Tlower is satisfied and ends when xi > T.
If the interval between two negative runs is equal to only one time interval and the rainfall in that time period is xi < Tupper these runs are combined and considered as a single drought event.
Multi-year droughts are identified as consecutive dry spells with duration exceeding 3 years.
Run theory:
(Guo and Montanari, 2023)

## Slide 11
The Autoregressive Fractionally Integrated Moving Average (ARFIMA) model is a generalization of classical time-series models that allows for long-range dependence in stochastic processes (Granger and Joyeux, 1980; Hosking, 1981). Unlike standard ARIMA models, which assume integer orders of differencing, ARFIMA models introduce a fractional differencing parameter that captures persistence over long time horizons.
The fractional parameter enables the model to represent slowly decaying autocorrelations commonly observed in economic, financial, hydrological, and geophysical data (Montanari et al., 1997).
In an ARFIMA (p, d, q) model, the p and q orders are related to the autoregressive (AR) and moving average (MA) structures, respectively. The fractional integration parameter d describes long term persistence. When (0 < d < 0.5), the process exhibits long-memory behaviour characterized by hyperbolically decaying autocorrelation functions.
ARFIMA models provide a flexible framework for modelling persistence. This property allows past observations to influence the present value with weights that decay gradually over time, therefore reproducing cycles of multi-year droughts.
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
ARFIMA:

## Slide 12
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS:
Model input:
    the observed time series: 209 years of daily data
    a specified marginal distribution function: Weibull type III
    the autocorrelation function: Pareto type III
    the desired number of lags: 50
The Complete Stochastic Modelling Solution (CoSMoS) model was introduced by Papalexiou (2018) and is capable of simulating intermittent hydroclimatic processes such as precipitation.
It is able to preserve seasonality, intermittency, first and second order statistics.By preserving these characteristics of the data we ensure the generation of synthetic time series with high degree of realism and accuracy, therefore giving the opportunity to identify extreme events.
The basic assumption underlying CoSMoS is that any process -stationary or cyclostationary- can be generated by transforming a specific “parent” Gaussian process. More precisely, any process {X(t)} with a specified marginal distribution and a has an underlying parent Gaussian process which can be identified.
CoSMoS is implemented through the python toolbox PyCoSMoS.

## Slide 13
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS implementation:

## Slide 14
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS implementation:

## Slide 15
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS implementation:

## Slide 16
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
Month | diff_mean(mm) | diff_mean(%) | diff_std(mm) | diff_std(%) | diff_max(mm) | diff_max(%)
January | 0.04 | 2.64 | 0.21 | 0.04 | 44.03 | 0.34
February | -0.05 | -2.93 | -0.58 | -0.10 | -50.18 | -0.32
March | -0.20 | -11.71 | -0.36 | -0.07 | 6.73 | 0.08
April | -0.12 | -5.99 | -0.38 | -0.07 | -9.69 | -0.15
May | -0.10 | -4.72 | -0.15 | -0.02 | -3.69 | -0.05
June | -0.13 | -7.12 | -0.22 | -0.04 | -19.76 | -0.21
July | -0.11 | -9.22 | -0.42 | -0.08 | -20.69 | -0.25
August | 0.02 | 1.78 | 0.30 | 0.06 | 3.95 | 0.05
September | 0.11 | 5.30 | 0.30 | 0.04 | 0.49 | 0.00
October | -0.11 | -4.03 | -0.39 | -0.05 | 5.39 | 0.05
November | -0.07 | -2.65 | -0.22 | -0.03 | -21.87 | -0.19
December | -0.13 | -7.21 | -0.78 | -0.14 | -59.32 | -0.56
CoSMoS implementation:

## Slide 17
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS implementation – Bias correction:
The autocorrelation function, probability distribution function and seasonal structure of the simulated ensemble time series are in good agreement with the observations, discrepancies remain in the marginal moments.
The scope of this work is to identify and compare multi-year drought characteristics, so it is important to prevent any systematic error arising from mismatches in the marginal moments.
To correct biases in the simulated time series, we applied the method of quantile mapping (QM). The QM method adjusts the values of the simulated time series so that their cumulative distribution matches the one of the observations, while preserving the temporal dependences.
Time series Origin Moment | Observed | CoSMoS | CoSMoS Bias corrected
Mean | 675.40 | 701.36 | 680.43
Standard deviation | 185.21 | 154.70 | 183.37
Skewness | 0.22 | 0.43 | 0.30
Kurtosis | -0.20 | 0.27 | -0.22

## Slide 18
s
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS + ARFIMA implementation
ACF shows slow decay
PACF exhibits no sharp cutoff
Hurst parameter: H=0.63
Applied to the annual time series

## Slide 19
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS + ARFIMA implementation
Residuals exhibit white noise behavior which indicates that long-term dependence is captured by the ARFIMA model.
Preserves long-term dependence, persistence.

## Slide 20
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS + ARFIMA implementation
Preserves long-term persistence
Hsim=0.59

## Slide 21
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
CoSMoS + ARFIMA implementation
Monte Carlo simulation:
100 years, adequate representation of multi-year droughts.
500 simulations to achieve a statistically stable estimates.

## Slide 22
Chart: Drought duration (DD)
| Historical | ARFIMA ensemble (0,d,0) | Simulations Quantile mapping | SSP2.6 | SSP8.5
DD | 6.55 | 5.47 | 4.77 | 4.89 | 5.61
Historical
Run theory application:
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
MME of 13 GMCs from CMIP6

## Slide 23
Historical
Chart: Drought intensity (DI)
| Historical | ARFIMA ensemble (0,d,0) | Simulations Quantile mapping | SSP2.6 | SSP8.5
DI | 0.212 | 0.225 | 0.196 | 0.154 | 0.158
Run theory application:
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
MME of 13 GMCs from CMIP6

## Slide 24
Historical
Chart: Drought frequency (DF)
| Historical | ARFIMA ensemble (0,d,0) | Simulations Quantile mapping | SSP2.6 | SSP8.5
DF | 0.053 | 0.064 | 0.07 | 0.062 | 0.057
Run theory application:
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
MME of 13 GMCs from CMIP6

## Slide 25
Historical
Chart: Maximum Deficit (MD%)
| Historical | ARFIMA ensemble (0,d,0) | Simulations Quantile mapping | SSP2.6 | SSP8.5
MD | 0.4616 | 0.4484 | 0.3791 | 0.2988 | 0.321
Run theory application:
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”
MME of 13 GMCs from CMIP6

## Slide 26
We need to target on mitigating the impacts of droughts to avoid their adverse consequences.
Stochastic models serve as a valuable tool for generating synthetic time series incorporating the inherent variability, interdependence, intermittency and seasonality.
By applying stochastic methods we limit the lack of predictability and “surprise” related to natural processes.
The key point is to understand the advantages of each stochastic model and choose the appropriate for each specific goal.
The integration of stochastic models combines the advantages of both CoSMoS in the representation of daily (fine scale) precipitation structure and the ARFIMA in capturing the long-term persistence of the process.
The results offer valuable insights in drought risk estimation and consequently aid in adopting the appropriate mitigation strategies, water management policies and therefore creating drought resilient societies reducing the underlying surprise element.
Conclusions:
“Integration of stochastic and statistical approaches for drought risk estimation through long-length time series”