## Slide 1
European Geosciences Union General Assembly 2026
Beyond Evolutionary Algorithms: A scalable River-Network Approach to Water Distribution Network Design
Surendra Kumar Sahu1, Dnyanesh Borse2, Basudev Biswal1
1 Department of Civil Engineering, Indian Institute of Technology Bombay, Mumbai, India
2 Department of Civil, Environmental and Construction Engineering, University of Central Florida, Orlando, USA
Session HS5.4.3: Digital water and interconnected urban infrastructure
Supplementary material for

## Slide 2
A 2018 NITI Aayog report highlighted:
600+ million people
are facing high to extreme water stress.
0.2+ million deaths annually
due to inadequate safe drinking water.
120th position
India is placed 120th among 122 countries in the water quality index.
Motivation:
Problem Statement and Motivation
Did you know?
England & Wales
Water utility assets valued at £278.3B, with £44B spent on maintenance & replacement (2015–2020)
US EPA
The US EPA reports a funding gap of $160B in water & wastewater infrastructure (ASCE, 2021).
Research Papers
Over 300 journal papers on WDS design & optimization (Mala-Jetmarova et al., 2018).
Borse, 2024, PhD Thesis, IIT Bombay: Adapted river network concepts for pipe networks (Hanoi WDN), yielding quick, near-optimal results.
Despite extensive research, a quick and reliable model for large real-world WDNs is still missing.

## Slide 3
The Core Idea: Learning from Nature
(Borse, 2024, PhD Thesis, IIT Bombay)
River Network | WDNs
Rainwater converges to an outlet | Water is distributed from a source
Minimizes energy expenditure (Rodríguez‐Iturbe et al., 1992b) ……..1 | Minimizes construction & operational cost …….2
River Network | WDNs
Rainwater converges to an outlet | Water is distributed from a source
 | Minimizes construction & operational cost …….2
Goal: To design a low-cost WDN by mimicking the natural efficiency of river systems.
  Problem: WDN design is NP-hard, needing heavy optimization.
  Inspiration: River networks self-organize into efficient, energy-minimizing trees.
  Approach: A simple probabilistic algorithm evolves networks toward low-cost efficiency.
Simple Analogy:

## Slide 4
Iterative spanning-tree construction with hydraulically-informed selection
Problem
Find the cheapest set of pipe diameters from a discrete catalogue such that pressure ≥ Pmin at every demand node.
Why it is hard
Combinatorial: XN candidate diameter assignments
Hydraulically coupled: every diameter affects pressures everywhere
Discrete + nonlinear: no gradient information available
Algorithm pipeline (one iteration)
1
Build Tree
Probabilistic spanning tree
from reservoirs to all nodes
2
Size Pipes
Continuity-based diameter
from cumulative demand
3
Verify Hydraulics
EPANET solver checks
pressure at every node
Repeat for N iterations · keep cheapest feasible design
The algorithm has three independent knobs:
Tree shape
η, β, γ, δ, θ
Pipe sizing
V_global
Search effort
N iterations
Probabilistic Growth Algorithm for WDN Design

## Slide 5
Two-stage roulette guided by a hydraulic attractiveness score
Attractiveness score for every node v
Q
cumulative demand reaching v through the tree
L
downstream path length from a reservoir to v
H
head difference along that path
Roll of γ, δ, and θ
γ > 0 → favour high-demand nodes
δ < 0 → favour short paths from source
θ < 0 → favour easy-to-reach nodes (low head loss)
Each iteration grows the tree edge by edge
Step 1 Pick a parent from the frontier
Roulette weights: (v)η, exponent η sharpens the selection.
High η → almost always picks the most attractive frontier node.
η = 0 → uniform random pick (heuristic ignored).
Step 2 Pick a child from the parent's neighbours
Roulette weights: (u)β, exponent β sharpens the selection.
Step 3 Repeat until every node is assigned
Result: a directed spanning tree rooted at the reservoirs, covering all the demand nodes. Every iteration produces a different tree because the roulette is stochastic.
Probabilistic Tree Growth
High The chosen child is added as a tree edge, its neighbors enter the frontier with updated ϕ values

## Slide 6
Continuity-based sizing, catalogue snapping, and parallel iteration
1
Cumulative demand
For each tree pipe, flow = sum of demands of all downstream nodes.
2
Theoretical diameter
D = √( 4Q / (π · Vglobal) )
From continuity at fixed sizing velocity V_global.
3
Snap to catalogue
Choose the closest of the available commercial diameters; cost = length × unit price.
Trade-off: higher V → smaller D → cheaper pipes, but more head loss → fewer feasible designs.
Feasibility check
Apply diameters to the network and run EPANET hydraulics in memory.
An iteration is feasible when pressure ≥ Pmin at every demand node.
Loop pipes (those not in the spanning tree) default to the smallest catalogue diameter.
Pipe Sizing and Feasibility Check

## Slide 7
Hanoi Network (HAN)
1 reservoir • 32 demand nodes • 34 pipes • 3 loops
6 diameters, Fujiwara and Khang (1990)
GoYung Network
1 reservoir • 22 demand nodes • 30 pipes • 9 loops
8 diameters, Kim et al. (1994)
Balerma Network (BIN)
Real-world Large WDN
VirtRome
Case Studies
4 reservoir
443 demand nodes
454 pipes
8 loops
10 diameters
Reca and Martínez (2006)
1 reservoir
3558 demand nodes
4021 pipes
211 km of pipes
15 diameters
Sitzenfrei, R., et al. (2020)
4 reservoir
150,630 demand nodes
157,044 pipes
15 diameters
Beyond the reach of standard evolutionary algorithms
Sitzenfrei, R., et al. (2020)

## Slide 8
GoYung
Figure: Evolution of design cost with iterations
Cost – 177.09 million won
Time – 6.47 sec (50 iterations)
Vmin – 0.8 m/s
Vmax – 1.2 m/s
Large WDN
Figure: Evolution of design cost with iterations
Cost – € 4.71 million
Time – 7.86 min (100 iterations)
Vmin – 1.0 m/s
Vmax – 1.8 m/s
VirtRome WDN
Figure: Evolution of design cost with iterations
Cost - € 81.99 million
Time – 6.34 days, 30 iterations
Vmin – 0.8 m/s
Vmax – 1.37 m/s
Results and Discussion

## Slide 10
Surendra Kumar Sahu @IIT Bobay, India

## Slide 11
Conclusion
Novel river-network-inspired algorithm showed robust performance across scales
Rapid Solutions
Generates competitive, near-optimal network designs in seconds
Achieved costs of $6.15M (Hanoi), 177.09M won (GoYung), and €2.478M (Balerma)
Proven Scalability
Successfully handled large-scale networks
Obtained the cost of €2.478M (Large network), and €81.99 M (VirtRome)
Hybridization Power
River Network + GA achieved global optimum for Hanoi with 64% time reduction and 60% fewer evaluations
The primary breakthrough: It offers efficient initialization, reducing computational cost for traditional metaheuristics and improving solution quality.

## Slide 12
Sitzenfrei, R., Wang, Q., Kapelan, Z., & Savić, D. (2020). Using complex network analysis for optimization of water distribution networks. Water Resources Research, 56, e2020WR027929. https://doi.org/10.1029/2020WR027929
Mohsen Hajibabaei, Sina Hesarkazzazi, Amin Minaei, Dragan Savić, Robert Sitzenfrei; Pareto-optimal design of water distribution networks: an improved graph theory-based approach. Journal of Hydroinformatics 1 September 2023; 25 (5): 1909–1926. doi: https://doi.org/10.2166/hydro.2023.091
Reca, J., and J.Martínez (2006), Genetic algorithms for the design of looped irrigation water distribution networks, Water Resour. Res., 42, W05416, doi:10.1029/2005WR004383.
Zheng, F., A. R.Simpson, and A. C.Zecchin (2011), A combined NLP-differential evolution algorithm approach for the optimization of looped water distribution systems, Water Resour. Res., 47, W08531, doi:10.1029/2011WR010394
Naser Moosavian, Barbara J. Lence; Fittest Individual Referenced Differential Evolution Algorithms for Optimization of Water Distribution Networks. Journal of Computing in Civil Engineering 1 November 2019; 33 (6). doi: https://doi.org/10.1061/(ASCE)CP.1943-5487.0000849
Dnyanesh Borse, Basudev Biswal; Emergence of efficient channel networks in fluvial landscapes. Advances in Water Resources June 2025; 200: 104962. doi: https://doi.org/10.1016/j.advwatres.2025.104962
REFERENCES

## Slide 13
THANK
YOU!