## Slide 1
UK-Flow15: Sub-hourly river flow data observations from 1369 river gauges in the UK, 1948-2023
Felipe Fileni, Hayley J. Fowler, Elizabeth Lewis,
Fiona McLay, Gemma Coxon, David Archer,
Emma Bruce, Longzhi Yang, Matt Fry,
Hollie Cooper, and Ollie Swain
abstract and information

## Slide 2: Why Visit UK-Flow15?
      Build it
I’m Interested in producing high-resolution flow datasets.
      Use it
I Want to use 15-min flows for scientific outputs.
      Apply it
I’m Curious how it informs policy and decisions.
      Explore it
This presentation just caught my attention, and I want to know more about it.
Title slide + QR abstract

## Slide 3
Getting started
Inside the data
Using the data
Why it matters
Why build it?
How long did it take?
Dataset coverage
Dataset Structure
Visual Quality Control
Statistical Quality control
Planned updates
Access to high-res data matters!
Real-world impact of the data
Data suitability
Artefact removal
Hydrological modelling
Event study
Extreme study
Home

## Slide 4: Why build a 15-min dataset?
A summary of UK datasets in 2022…
Sub-daily flows nowhere to be found!
Build it ->
(Fileni et al. 2023)
Home
Explore it!

## Slide 5: How Long did it take?
Build it ->
<- Build it
a scoping phase, in which we explored which data were available and valuable;
a consolidation phase, where the dataset was organised into a semi-final version;
a refinement phase, during which the dataset was further improved and additional data incorporated
Home
Explore it!

## Slide 6: Dataset coverage
Build it ->
<- Build it
1369 stations
1.8 billion observations
Earliest record: 1948
Largest catchment: 9948km2
Smallest catchment: 0.85km2
Use it->
(Fileni et al, in review, a)
Home
Explore it!
Paper
Data
(Fileni et al, 2025,a)

## Slide 7: Dataset structure
Build it ->
<- Build it
Use it->
<- Use it
(Fileni et al, in review, a)
Home
Explore it!
Time series (core data)
Datetime: timestamp
Value: river flow (m³/s)
Resolution: native data timestep
QC_code: outcome of quality control checks
Metadata (7 files for full transparency)
Identification metadata: station info, location, source
Quality control metadata: flags, checks, detected issues
Traceability metadata: full record of processing decisions

## Slide 8: Visual Quality Control
Build it ->
<- Build it
Use it->
<- Use it
(Fileni et al., in review, b)
Home
Explore it!
Automated checks flag anomalies, but cannot always confirm their validity
Visual inspection helps distinguish real hydrological events from artefacts
Essential for identifying issues such as rating curve shifts, truncations, and timing errors

## Slide 9: Statistical Quality Control
Build it ->
<- Build it
Use it->
<- Use it
(Fileni et al., in review, b)
Home
Explore it!
Automated statistical QC enables consistent, scalable detection of anomalies at national-scale datasets
Paper
GitHub
(Fileni)

## Slide 10: Planned Updates
Build it ->
<- Build it
Home
Explore it!
Data & Quality Control
Integration of level data in the dataset
Request of some of the missing flow stations/time periods
Update the dataset to 2025
Workflow Development
Ensure that we have a procedure in place for sporadic updates of the data
Further evaluation of automated QC

## Slide 11: Data suitability
Use it->
<- Use it
Home
Explore it!
Which data to pick?
When do you need high resolution data?
High Flow in fast response catchments
High Flow in groundwater dominated catchment
vs

## Slide 12: Artefact removal
Use it->
<- Use it
Home
Explore it!
(Fileni et al, in review, a)
Paper
(Fileni)
Github
UK-Flow15 data
Open access: all available data is provided to the user
User responsibility: data suitability depends on the analysis → filtering may be required
Transparent QC: data are flagged, not removed
Reproducibility: clear procedures provided for high-flow screening and filtering

## Slide 13: Hydrological modelling example
Use it->
<- Use it
Apply it ->
(Kay, 2026)
Home
Explore it!
Impacts of using sub-daily outputs for future-flood estimates:
Flood increases are consistently higher when models are calibrated at hourly resolution (median ≈ +11.8% at the 10-year return period)
The effect is amplified in smaller catchments (median ≈ +12% at 10-year RP)
The strongest increases occur in north-west UK, particularly for small catchments (median ≈ +16% at 10-year RP)

## Slide 14: Event study example
Use it->
<- Use it
<- Apply it
Apply it ->
(Archer et al., submitted)
Home
Explore it!
High temporal resolution data captures rapid flood dynamics and impacts
Summer convective storms generate extremely fast, localised responses
Combining high-resolution rainfall and flow data enables reconstruction of the full event:
rainfall -> runoff ->damage
e.g. Keltie Burn, 2004

## Slide 15: Extremes study example
Use it->
<- Use it
<- Apply it
Apply it ->
(Fileni et al., submitted)
Home
Explore it!
15-min data:
Captures short-duration, high-intensity events driving summer extremes
Reveals seasonal shifts in flood-generating processes
Avoids underestimation of extremes seen in daily datasets

## Slide 16: Access to high-res data matters!
Apply it ->
<- Apply it
Home
Explore it!
Unlocks the representation of real flood dynamics
Peak Datasets: Capture only the peak events without representation physical processes within the catchment
Daily datasets: Underestimation of events on mesoscale catchments which need higher resolution data for flood wave representation

## Slide 17: Real-world impact of the data
Apply it ->
<- Apply it
Home
Explore it!
adapted from (Fileni et al, 2025b)
Sub-daily flows were one of the missing pieces for updating the guidelines for flood risk assessments under climate change in the UK.

## Slide 18: Summary on how we built the dataset
<- Build it
Home
Explore it!
Scope & data collection
Identify user needs
Gather available data
Building a consistent dataset
Checking the structure of collected data
Harmonisation and standardisation
Identifying shortcomings of the data
Quality control framework
Visual verification of the data for artefact detection
Automated anomaly detection
Transparent flagging for communication
to understand that a dataset will never be perfect…
… and that there’s always scope for an update if there’s demand.
Leads to
Which requires
Nevertheless, it’s needed

## Slide 19: Summary on how to use the dataset
<- Use it
Home
Explore it!
The dataset
UK-wide coverage
Simple timeseries csv format
Rich metadata available for full context
1) Check suitability
Do you need that high of a resolution?
Do you need a continuous series?
Do you need flows only (or also other products)?
Case studies
Hydrological modelling
Flood event studies
Large sample extremes
Used in
Before use
2) Clean the data
Use metadata to identify and exclude unsuitable data for your specific analysis
Data ready for use!

## Slide 20: Summary on the applicability of the dataset
<- Apply it
Home
Explore it!
High resolution data improves
Hydrological Modelling Better calibration of models at event scale
Statistical analysis
Ability to capture and represent flood event dynamics
Climate change
Ability to capture the sub-daily flood intensification within the years
Reducing Uncertainty
Better estimation of extreme events
Better representation of climate change
Impact on Practice
More robust flood risk estimation guidelines
Improved design flood estimates
Enhanced flood resilience
By
Leading to