## Slide 1
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
Email: Xiaobin.Qiu@newcastle.ac.uk
Wechat: xiaowo616563

## Slide 2
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
We lack reliable gridded precipitation data for tracking extreme rainfall in Great Britain
The opportunity:
Blended datasets can capitalize on the complementary strength of both sources to close this data gap
Rain gauge:
Highly accurate at the point scale
Too sparse for continuous national coverage
Weather radar:
Good spatial coverage (1 km )
Beam blockage, ground clutter and electronic noise
1. The Problem

## Slide 3
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
2. The Method
A dual–engine pipeline: Holistic Radar Quality Control combined with the Gauss Blending Method
Engine 1: Rule-Based Radar QC Framework
Detects beam blockage and bad pixels using continuity and uniqueness assumptions of rainfall field.
Replaces bad data using the Gauss Interpolation Method.
Without requiring ancillary datasets.
Raw Radar Rainfall → Remove Bad Rainfall → Corrected Rainfall
Engine 2: Gauss Blending Method (GBM)
Radar Rainfall + Gauge Rainfall → Blended Rainfall
Adapts the Gauss-Seidel numerical technique to seamlessly merge spatial radar structures with gauge data. Simple, highly efficient, avoiding over-smoothing.

## Slide 4
Ground clutter (wind farm)
Radar beam blockage
Radar malfunction
Ship Traffic
Electronic noise
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
2.1 Quality issues for radar rainfall (bad rainfall)
2. The Method

## Slide 5
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
2. The Method
2.2 Three assumptions for radar rainfall fields (normal rainfall)
Rainfall fields are schematic representations for illustration purposes only, generated by ChatGPT.

## Slide 6
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
2. The Method
2.3 Quality Control Framework for Radar Rainfall

## Slide 7
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
2. The Method
2.4 Gauss Blending Method to emerge gauge and radar rainfall
Rainfall fields are schematic representations for illustration purposes only , generated by ChatGPT

## Slide 8
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
3.Results & Impact
(1) Quality Control of Radar Rainfall Data
(2) Blending Radar and Gauge Rainfall
(3) GRaD-GB (1H1K): Gauge–Radar Precipitation Dataset (1 hour and 1 km) for Great Britain (2006-2023)
The most intense rainfall ever recorded in the UK (July 18, 2017, Coverack)

## Slide 9
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
3.Results & Impact
Proven Accuracy
Group 2: Final GBM Blending Impact
▼ 29%
Reduction in Radar RMSE
▲ 31%
Increase in Correlation (CC)
▼ 14.5%
Improvement in RMSE & MAE
▼ 22%
Reduction in Mean Relative Error
Group 1: QC Framework Impact
Radar QC Framework: effectively detect problematic radar rainfall and improve its accuracy.
GRaD-GB (1H1K): A new hourly, 1-km gauge–radar merged dataset spanning 2006–2023.
Why it Matters: A good dataset for tracking storm life cycles, managing flood risk, and driving hydrological modelling.

## Slide 10
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
References
Qiu, X., Green, A.C., Blenkinsop, S., Fowler, H.J., 2026a. Quality control of the composite radar quantitative precipitation estimation product for Great Britain. Journal of Hydrology 666, 134755. https://doi.org/10.1016/j.jhydrol.2025.134755
Qiu, X., Green, A.C., Blenkinsop, S., Fowler, H.J., 2026b. Developing a radar-rain gauge hourly blended precipitation dataset for Great Britain using the Gauss Blending Method. Journal of Hydrology 668, 134954. https://doi.org/10.1016/j.jhydrol.2026.134954
Contact
Xiaobin Qiu
Post-doc researcher
School of Engineering, Co-Centre for Climate + Biodiversity + Water
Newcastle University, UK
Email: Xiaobin.Qiu@newcastle.ac.uk
Wechat: xiaowo616563

## Slide 11
Developing a Gauge–Radar Merged Precipitation Dataset (1 hour and 1 km) for Great Britain: GRaD-GB (1H1K)
Xiaobin Qiu, Amy C. Green, Stephen Blenkinsop, and Hayley J. Fowler
Thank you