## Slide 1
From Present-Day Validation to Future Projections: AR6 SSP Scenario Assessment of Water Availability, Irrigation Demand, and Paddy Rice Yield in the Zhuoshui River Basin Using a Water–Crop Model
Po-Hao Chu1, Yun-Chi Chung1, Dong-Hong Wu3, and Li-Chiu Chang1,2
1Department of Water Resources and Environmental Engineering,Tamkang University, New Taipei City, Taiwan
2Department of Artificial Intelligence,Tamkang University, New Taipei City, Taiwan
3Department of Agronomy, National Chung Hsing University,Taichung City, Taiwan
Reporter:Po-Hao-Chu Date:2026/05/07
ICWE 水環境資訊研究中心
Information Center for Water Environment

## Slide 2
Hydrological Monitoring Stations and Data Source
Input Data Processing
Data Source: Water Resources Agency (WRA), Taiwan
Groundwater: First-layer wells averaged as relative groundwater level.
Streamflow: One key gauging station selected.(Xizhou Bridge)
Rainfall: TCCIP 3×3 grid-average historical observations.

## Slide 3
Feature Importance Analysis for Paddy Yield Prediction
Random Forest
𝑦 ̂=𝑓(𝑟𝑎𝑖𝑛,𝑔𝑤,𝑓𝑙𝑜𝑤)
SHAP
𝑦 ̂=∅_0+∅_𝑟𝑎𝑖𝑛+∅_𝑔𝑤+∅_𝑓𝑙𝑜𝑤
Random Forest
SHAP
factor | contribution(%)
Ground water | 60.1
Stream flow | 26.1
rainfall | 13.8
year | Real_yield | Predict_yield
2007 | 6283.712 | 6632.973
2008 | 7245.319 | 7040.418
2009 | 7520.427 | 7443.65
2010 | 7371.465 | 7500.232
2011 | 7795.354 | 7813.055
2012 | 7428.671 | 7454.263
2013 | 6951.794 | 6978.443
2014 | 7155.977 | 7095.043
2015 | 7632.872 | 7688.947
2016 | 7320.25 | 7141.525
2017 | 7693.519 | 7586.372
2018 | 8644.664 | 8260.036
2019 | 7519.449 | 7594.227
2020 | 7661.934 | 7709.423
2021 | 8274.9 | 8088.802
2022 | 7711.829 | 7732.926
2023 | 8339.501 | 8199.219
predict yield
Groundwater_May
Groundwater_June
Streamflow_Feb
GW Apr
Rainfall last Dec
Streamflow May
GW Feb
Rainfall last Dec
Streamflow Jan
Streamflow Mar
GW Jan
GW Mar
Rainfall Jan
Streamflow Apr
GW last Dec
GW June
GW last Nov
Rainfall Feb
Streamflow last Nov
Rainfall April
Annual Contribution of Hydrological Factors
Annual Contribution of Hydrological Factors
percent
year
Rainfall
Ground water
Stream flow

## Slide 4
Linking SHAP-Identified Groundwater Importance to Rice Physiological Water Demand
Annual Contribution of Hydrological Factors
Annual Contribution of Hydrological Factors
Annual May Groundwater
Annual June Groundwater
Water depth
10-20cm
Water depth
3-5cm
0cm
Water depth
5-10cm
0cm
0cm
0cm

## Slide 5
LSTM-Based Monthly Accumulated Streamflow Prediction at Xizhou Bridge Station
Dataset |  | RMSE (10⁴ tons/month)
train | 0.913 | 16267
test | 0.895 | 15416
Dataset |  | RMSE (10⁴ tons/month)
train | 0.913 | 16267
test | 0.895 | 15416
train
test

## Slide 6
LSTM Prediction of Basin-Average First-Layer Groundwater Levels
Dataset |  | RMSE(M)
train | 0.65 | 0.674
test | 0.485 | 1.07
Dataset |  | RMSE(M)
train | 0.65 | 0.674
test | 0.485 | 1.07
train
test

## Slide 7
Thank you very much!
Gmail：henry66211chu@gmail.com
School:Department of Water Resources and Environmental Engineering,Tamkang University
Professor: changlc@mail.tku.edu.tw