## Slide 1: Using flood impact data for evaluating hydrometeorological warnings in Sweden
J. Svatoš, S. Karimi, R. van de Beek, J. Olsson, N. Hjerdt

## Slide 2
Flood warning system
25 years of impact data
~10 000 records of emergency service responses and flood-affected roads
What type of flood events are handled well and how can it be improved?

## Slide 3
Flood warning system
25 years of impact data
~10 000 records of emergency service responses and flood-affected roads
What type of flood events are handled well and how can it be improved?

## Slide 4: Very few impacts explained by warnings

## Slide 5: Very few impacts explained by warnings
Filter impact data
Use sub-daily hydrological model
Focus on outputs beyond streamflow
Lessons learnt:

## Slide 6: Insights on using flood impact data for evaluating hydrometeorological warnings in Sweden
J. Svatoš, S. Karimi, R. van de Beek, J. Olsson, N. Hjerdt
How to use impact data to improve the warning system?
Do flood warnings correspond with recorded impacts?
Benefit of filtering impact data
Evaluation of the existing warning system
Methodology
Benefit of sub-daily hydrological model
Case study:
Västernorrland cloudburst September 2025
Benefit of outputs beyond streamflow
Conclusion

## Slide 7
Emergency service responses (MSB)
Severity code: 1-7
(little – very large impact)
Coordinates
Time
Flood-affected roads (TrV)
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Flood impact data

## Slide 8: Flood impact data
Flood-affected roads (TrV)
Emergency service responses (MSB)
In total ~10 000 records over 25 years
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 9: Flood-related warnings at SMHI
This study considered if hindcast data exceeded thresholds on the day of impact or the day before in the subcatchment of the impact, not if warnings were actually issued
Click here for a comparison of exceeded thresholds and issued warnings
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 10
Overall between 2011-2023
  34% impacts covered by warnings
  26% impacts exceeded thresholds
Warnings have become more accurate over time, especially with the introduction of an impact-based approach in 2021
Differences also due to lower threshold levels until 2021, hydrological model improvements and using forecast vs. hindcast data
Thresholds were used in this study for consistency in methodology
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Comparison of exceeded thresholds and issued warnings

## Slide 11: Hydrometeorological data
Operational S-HYPE hydrological model [1]
  ~40 000 subcatchments (median size 7 km2)
  Daily (6-6UTC) and hourly model runs with identical parameters[2] and precipitation data[3]
  Hourly model is still in testing phase for operational forecasting
  Outputs: simulated streamflow (COUT) and total generated runoff (CRUN)
Return periods calculated by fitting annual maxima from 1991-2020 to a Gumbel distribution by method of moments[4]
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
CRUN serves as a proxy for small streams not explicitly modelled in S-HYPE

## Slide 12: How many recorded impacts were covered by the existing SMHI flood warning system?
Count: 9836
Highest exceeded threshold per impact:
Yellow
Orange
Red
None
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 13: Larger flood events were explained better
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 14: Minor benefit of removing non-severe impacts
When impact severity classified as no or little impact
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Count: 8411
Count: 9836

## Slide 15: Major benefit of removing isolated impacts
When distance to nearest other impact on the same day > 100 km
Count: 7104
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Count: 9836

## Slide 16: Proposed impact filtering technique:
Use only severe non-isolated impacts when ≥ 4 in a day
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Count: 4269
Count: 9836

## Slide 17: Major benefit of applying sub-daily model
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Added max return period of CRUN from 1h, 3h, 6h, 12h, 24h accumulations

## Slide 18: More red warnings explain large flood events
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 19: Improvement primarily in summer
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Unexplained winter impacts remained above 70%
Proportion of unexplained impacts in August decreased from 56% to 32%

## Slide 20: Relative importance of output variables
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
CRUN (total runoff) was a more important predictor of impacts than COUT (streamflow)
Precipitation thresholds explain <5% impacts

## Slide 21: Västernorrland 6-7 September 2025
More than 100 mm of rainfall
40 destroyed roads, 2 derailed trains
Only yellow warning issued
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 22
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 23: Daily model considerably underestimated magnitude
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 24: Sub-daily runoff is necessary to capture sub-grid flashy streams which cause many impacts
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion

## Slide 25: Conclusion
Important to filter only relevant impacts
Sub-daily runoff is effective in explaining summer cloudbursts
Impacts from winter processes (urban melt, rain-on-snow) still not represented well in the S-HYPE model
Home
Methodology
Evaluation
Impact filtering
Sub-daily model
Beyond streamflow
Case study
Conclusion
Abstract page
Contact:
jiri.svatos@ec.europa.eu
niclas.hjerdt@smhi.se
www.linkedin.com/in/jiri-svatos
Original methodology
New methodology

## Slide 26: References
[1] Lindström et al. (2010). Development and testing of the HYPE (Hydrological Predictions for the Environment) water quality model for different spatial scales. Hydrology Research, 41(3-4), 295-319.
[2] Fuentes-Andino et al. (2022). Exploring the potential for parameter transfer from daily to hourly time step in the HYPE model for Sweden. Hydrological Sciences Journal, 67(13), 1988-2001
[3] https://www.smhi.se/data/nederbord-och-fuktighet/nederbord/griddad-nederbord--och-temperaturdata
[4] Bergstrand et al. (2014). Nationwide hydrological statistics for sweden with high resolution using the hydrological model s-hype. Hydrology Research, 45(3), 349–356.