## Slide 1
Indian Institute of Technology Mandi | 6 May 2026
PROBABILISTIC FRAMEWORK FOR ENHANCED LANDSLIDE SUSCEPTIBILITY MAPPING FOR RAINFALL-INDUCED LANDSLIDES
Presented By :
Tanvi Chauhan
PhD Scholar
School of Civil and Environmental Engineering
Supervisor: Dr. K. V. Uday
Associate Professor, IIT Mandi
Co-Supervisor: Prof. Vikas Thakur
Dean, NTNU Norway

## Slide 2
OVERVIEW
IIT Mandi| 2026
  Landslides: Background
  Objective
  Motivation for the study
  2023 Monsoon Event (Himachal Pradesh)
  Implementation
  Result
  Conclusion
  Methodology

## Slide 3
IIT Mandi| 2026
LANDSLIDES: BACKGROUND
• India ranked 1st with the highest potential frequency of fatal landslides.
• 12% of the Indian landmass is highly susceptible to landslides.

## Slide 4
Source: https://www.ndtv.com
Source: www.thenewzradar.com
Source: https://www.ndtv.com/topic/mandi-landslide
Notes: Climate changes: Alteration of rainfall patterns
Population surge: Increasing demands for infrastructure development in landslide-prone areas
road cuts: Expose the slopes directly to the environment, making it more vulnerable for failure.

## Slide 5
Motivation for study
Annual precipitation in India for 1901-2022 (https://climateknowledgeportal.worldbank.org/country/india/climate-data-historical)
Need for an accurate LSM assessment in Hilly terrain
Notes: Climate changes: Alteration of rainfall patterns
Population surge: Increasing demands for infrastructure development in landslide-prone areas
road cuts: Expose the slopes directly to the environment, making it more vulnerable for failure.

## Slide 6
Objective
Develop a local-scale, probabilistic landslide susceptibility framework that integrates qualitative and quantitative assessments, utilising natural and anthropogenic factors in machine learning, and evaluate its transferability across multiple landslide events.
IIT Mandi| 2026
Existing LSM approaches fail to capture local-scale variability and anthropogenic impacts, especially in Himalayan terrains
There is a need for an integrated, transferable framework that integrates natural and human-induced factors across multiple landslide events.

## Slide 7
Historic, Spatial, and Seasonal Rainfall Patterns in H.P. (Sana et al. 2024)
Event: 2023 Monsoon in H.P.
  The 2023 monsoon was marked by 1334.9 mm of record-breaking rainfall (IMD)
  In the 2023 monsoons, 43 flash floods reported in H.P. (Tiwari et al. 2024)
  5400 hillslope landslides and road cut slope failures (Sana et al. 2024)

## Slide 8
2023 Monsoon Impact in H.P.
IIT Mandi| 2026
Shimla Summer Hill Landslide 2023
(https://www.indiatoday.in)
Massive landslide in Anni near Bus stand
Thunag Debris Flow
Shamti Landslide, Solan
Kullu Sainj Area (Pre and Post monsoon)
(Sana et al. 2024)

## Slide 9
METHODOLOGY
IIT Mandi| 2026
Desk study
Data Acquisition & Preprocessing
Site Investigation
Qualitative Assessment
LHEF for LHZ
Geology
Geomorphology (DEM, Slope, Aspect, Curvature)
Anthropogenic factors
(Roads, NDVI, LULC)
Quantitative ML Assessment
Inventory
POF
Validation
Ground Truth Validation
Calibrated localized LSM
Site specific Recommendations
Notes: Address the gaps missed while Quantitative assessment filled by site visit detailed assessment

## Slide 10
STUDY AREA
IIT Mandi| 2026
Site investigations for Qualitative assessment

## Slide 11
Landslide site 1
IIT Mandi| 2026

## Slide 12
Landslide site 2
IIT Mandi| 2026

## Slide 13
Landslide site 3
IIT Mandi| 2026

## Slide 14
LHEF (Anbalagan 1992)
IIT Mandi| 2026
Parameter | Thunag | Rakhera | Jalanal
Lithology | 2.0 | 1.0 | 1.3
Structure | 1.5 | 0.8 | 0.6
Slope | 1.7 | 1.2 | 1.2
Land Use | 1.5 | 1.2 | 1.2
Hydrology | 0.5 | 1.0 | 0.8
Relative Relief | 0.6 | 0.6 | 1
Total Score | 7.8 (Very High Hazard zone) | 5.8 (Moderate Hazard zone) | 6.1 (High Hazard Zone)
Qualitative analysis
Landslide Hazard Evaluation based on Total Estimated Hazard

## Slide 15
Quantitative analysis
Landslide Inventory
Slope
CF: Elevation, Slope, Aspect, Curvature, LULC 2023, NDVI, Distance to roads, Distance to rivers.

## Slide 16
Pre-NDVI
Post-NDVI
Multi-source geospatial CF, including topographic, geological, hydrological, vegetation, and anthropogenic parameters were prepared in GIS.
Random Forest (RF) and XGBoost (XGB) models were trained using cross-site validation:
Train (T+R) → Test (J)
Train (T+J) → Test (R)
Train (R+J) → Test (T)

## Slide 17
IIT Mandi| 2026
Results

## Slide 18
IIT Mandi| 2026
Results
RF
Z | PoF Range | Anbalagan Equivalent | Description
I | 0.00 - 0.20 | < 3.5 | VLH
II | 0.21 - 0.40 | 3.5 - 5.0 | LH
III | 0.41 - 0.60 | 5.1 - 6.0 | MH
IV | 0.61 - 0.80 | 6.1 - 7.5 | HH
V | 0.81 - 1.00 | > 7.5 | VHH
XGB

## Slide 19
IIT Mandi| 2026
Key Findings
RF and XGBoost showed strong cross-site prediction capability with high ROC–AUC values: Train (T+R) - Test (J): RF = 0.969, XGB = 0.959
Train (T+J) - Test (R): RF = 0.950, XGB = 0.942
Lower performance for Train (R+J) - Test (T) (RF = 0.849, XGB = 0.836) indicates reduced generalisation in highly disturbed anthropogenic terrains.
SHAP analysis identified NDVI difference as the dominant controlling factor, followed by road influence, distance to road, and drainage proximity.
Results suggest that landslides in the study area are controlled more by anthropogenic disturbance and vegetation degradation than by terrain geometry alone.
ML-derived Probability of Failure (PoF) was calibrated with Anbalagan (1992) LHEF hazard classes to identify technogenic omission zones and improve hazard interpretation.

## Slide 20
IIT Mandi| 2026
Site | Hazard Level | Key Field Observation | Specific Recommendation
Thunag | VHH | Muck dumping & Road construction | Controlled muck disposal, Breast walls, and Bio-fencing.
Rakhera | MH | Toe erosion & Catchment discharge | Check dams in the catchment, Toe-protection (Gabions), and Lined chutes for drainage.
Jalanal | HH | Weathered sandstone & Erosion | Shotcreting or Geomeshes to prevent surface weathering, and Horizontal drains.
Site-specific Recommendations

## Slide 21
THANK YOU
Presented By : Tanvi Chauhan