## Slide 1
Do Process-Based Models Really Fall Short?
Rethinking Channel Routing to Bridge the Gap with Machine Learning Models
Ekant Sarkar¹*, Akshay Kadu¹,², Vijay Katari¹, Basudev Biswal¹
¹ Department of Civil Engineering, Indian Institute of Technology Bombay, Mumbai, India ² Stantec ResourceNet Pvt. Ltd., Pune, India
Central question:
Can targeted fix to channel routing make a process-based model competitive with LSTM?
1
Why this study?
But why?
A large part of the process-based versus machine-learning performance gap arises from linear, time-invariant routing.
But how?
Let’s take HBV and its routing module.
Original HBV routes runoff using a fixed triangular transfer function.
Replace this routing module with the Iterative Routing Model (IRM).
IRM accounts for variation of velocity with streamflow.
2
The HBV-IRM workflow
HBV gridded runoff
Route runoff to outlet using IRM
3
Performance against LSTM benchmarks
Figure: 64 CAMELS catchments, validation NSE distributions, and CDF comparison for HBV, HBV-IRM, global LSTM, and individual LSTM.
Key results
~78% of the performance gap between HBV-to-global-LSTM is closed by HBV-IRM.
4
Where the routing fix matters most?
Figure: Climate-regime boxplots.
What climate-regime tells us?
• HBV-IRM shows a higher lower-quartile in water-limited basins than both LSTM setups.
• Explicit routing physics remains useful when low-flow periods reduce the information available to data-driven models.
Answer to the central question:
Yes, routing matters. Improving routing makes process-based models competitive with machine learning while remaining physically interpretable.
Selected references: Sarkar et al. (2026). Taming the non-linearity : An iterative conceptual routing model for improving flood peak prediction. Environmental Modelling and Software, 197, 106843. https://doi.org/10.1016/j.envsoft.2025.106843.
Sarkar et al. (2026). Fixing the Routing Module to Achieve Machine-Level Performance in Streamflow Prediction. Authorea. February 24, 2026. DOI: 10.22541/au.177196151.17762877/v1
Median NSE across all catchments
HBV 0.65
HBV–IRM (this study) 0.72
Global LSTM 0.74
Individual LSTM 0.69
Because machine learning often outperforms
process-based hydrological models.
Let’s test whether better routing
can close the performance gap.
Our hypothesis
Inside the IRM
Start with initial velocity
Sum arrivals to provisional
Update velocity
Check convergence:
Is ?
Accept converged
If not converged, repeat routing with
Travel time:
LSTM models show higher uncertainty in arid basins than HBV-IRM.
MAXBASHBV = 2.95 days
Roughness coefficient = 0.036
Where, s=slope, n = roughness coefficient, b = channel width
Abstract ID: EGU26-2852
Contact