## Slide 1
Tawi River Basin is one of the major sub-basins of Chenab River in western parts of the Himalayas
The highest flood discharge -13552 m3/s (6th September 2014 which was 4.8 m higher than the danger level at Jammu).
Annual discharge is decreasing by 23 MCM per year, and water demand is rapidly growing due to urbanization and a population increase of 20% per decade (Kour et al., 2022).
Flashy nature of catchment owes to less ground water recharge.
Population Distribution Map
Catchment composed of erodible soil strata
Introduction
Objectives
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 2
Integrated assessment of hydro-meteorological extremes and water scarcity in the Tawi River catchment under climate change
Investigating the anticipated changes in hydro-meteorological extremes over the Tawi River basin in India, utilizing data from CMIP6 models for 2 oC and 3 oC global warming .
Analyzing the Spatio-temporal variability of water availability, specifically examining blue and green water resources in the context of a changing climate compared to a designated base period.
Examining the potential for future water scarcity and characterizing hydrological drought events within the Tawi River basin.
Utilization of FAHP (fuzzy analytic hierarchy process) to prioritize catchments within the Tawi River basin.
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 3
CMIP6: Coupled Model Intercomparison Project Phase 6
SSP2-4.5: Shared Socio-economic Pathways (Middle of the road scenario) & radiative forces ~4.5 W/m2
SSP5-8.5: Shared Socio-economic Pathways (fossil-fuel based development) & radiative forces ~8.5 W/m2
DEM: Digital Elevation Model
LULC: Land Use Land Class
2W: 2 oC Warming
3W: 3 oC Warming
NF: Near Future
FF: Far Future
BW: Blue Water
GW: Green Water
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 4
Datasets Used
S. No. | Datasets | Source | Spatial Resolution | Temporal Resolution
1 | Catchment boundary | Hydro-SHEDES | 90 m | -
2 | DEM | SRTM (NASA) | 30 m | -
3 | Soil cover | FAO | 0.9 km | -
4 | Land use classification | ESA (year 2020) | 10 m | -
5 | Meteorological data | IMD & TAMU (year 1979-2020) | 0.25o/ 26 km | Daily
6 | Future Climate Data | CMIP 6 (provided by Mishra et al. 2020) | 0.25o/ 26 km | Daily
7 | Discharge Data | CWC (year 1991-2018) | Jammu gauging station | Daily
8 | Future Population Data | SEDAC | 0.125o/ 13.8km | Decadal
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 5: Hydrometeorological extremes
Indices | Definition | Unit
PRCPTOT | Annual total precipitation on wet days | mm
CDD | Number of rainy days in a year (with rainfall intensity ≤ 1 mm/day) | days
CWD | Number of rainy days in a year (with rainfall intensity ≥ 2.5 mm/day) | days
R95p | Annual total precipitation when annual rainfall ≥ 95th percentile | mm
R99p | Annual total precipitation when annual rainfall ≥ 99th percentile | mm
R10 | Annual count of days when precipitation ≥ 10 mm | days
R20 | Annual count of days when precipitation ≥ 20 mm | days
Rx1day | Max 1-day precipitation amount | mm
Rx5day | Max 5-day precipitation amount | mm
TXx | Monthly maximum value of daily maximum temperature | (oC)
TXn | Monthly minimum value of daily maximum temperature | (oC)
TNx | Monthly maximum value of daily minimum temperature | (oC)
TNn | Monthly minimum value of daily minimum temperature | (oC)
Q95 | High flow (95th percentile value of streamflow) | m3/s
Q05 | Low flow (5th percentile value of streamflow) | m3/s
Various meteorological extremes developed by the Expert Team on Climate Change Detection and Indices (ETCCDI), as formulated by (Zhang et al. 2011).
Rainfall
Temperature
Discharge
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 6: Hydrometeorological extremes
Indices | Definition | Unit
PRCPTOT | Annual total precipitation on wet days | mm
CDD | Number of rainy days in a year (with rainfall intensity ≤ 1 mm/day) | days
CWD | Number of rainy days in a year (with rainfall intensity ≥ 2.5 mm/day) | days
R95p | Annual total precipitation when annual rainfall ≥ 95th percentile | mm
R99p | Annual total precipitation when annual rainfall ≥ 99th percentile | mm
R10 | Annual count of days when precipitation ≥ 10 mm | days
R20 | Annual count of days when precipitation ≥ 20 mm | days
Rx1day | Max 1-day precipitation amount | mm
Rx5day | Max 5-day precipitation amount | mm
TXx | Monthly maximum value of daily maximum temperature | (oC)
TXn | Monthly minimum value of daily maximum temperature | (oC)
TNx | Monthly maximum value of daily minimum temperature | (oC)
TNn | Monthly minimum value of daily minimum temperature | (oC)
Q95 | High flow (95th percentile value of streamflow) | m3/s
Q05 | Low flow (5th percentile value of streamflow) | m3/s
Various meteorological extremes developed by the Expert Team on Climate Change Detection and Indices (ETCCDI), as formulated by (Zhang et al. 2011).
Rainfall
Temperature
Discharge
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 7: Global Warming Periods
13 CMIP6 models.
2oC and 3oC Warming of global temperature over Pre Industrial period (1850).
Equal weight multi model ensemble, arithmetic mean (AMME) was used.
Source: IPCC report AR6, 2021
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 8: Blue and Green Water computation
Addressing water security by classifying fresh water resources into blue and green water
Blue Water: flowing through surface and subsurface medium which are stored in lakes, aquifers and manmade structures, that can be directly used for human consumption.
Green Water: water stored in unsaturated soil layer and vegetation canopy is classified as green water
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 9: Drought Analysis Fuzzy Analytical Hierarchy Process (FAHP)
Description | Range
Non-drought | 0.0 ≤ Index value
Mild drought | -1.0 ≤ Index value < 0.0
Moderate drought | -1.5 ≤ Index value < -1.0
Severe drought | -2.0 ≤ Index value < -1.5
Extreme drought | Index value < -2.0
Hydrological Drought
Streamflow drought index (SDI)
Following eight attributes (or parameters) for prioritization
cumulative streamflow for the hydrological year and the time scale
V and Sp are the long-term mean and standard deviation of cumulative streamflow
Rainfall
Average Temperature
Blue Water
Green water
Agricultural Area
Forest Area
Hydrological drought
Population Density
More enhanced decision-making framework
FAHP can classify evaluation factors into target level, criterion level, and factor level
Widely-used multi-attribute decision-making methods
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 10
SWAT calibration and validation
Extreme Precipitation Indices
Chart: Q Observed (m3/s)
Chart: Q Observed (m3/s)
Calibration (2007-2010)
Validation (2011-2014)
Percentage change in future precipitation extremes w. r. t. base period (1991-2020): (A) SSP2-4.5 (B) SSP5-8.5
 |  | PRCP TOT | R95p | R99p | Rx1 Day | Rx5 Day | CWD | CDD | R10 | R20
SSP2-4.5 | 2 warming | - | + | - | - | - | - | + | - | 
 | 3 warming |  | - | - | + | - | - | + |  | 
 | EF (2021-50) |  | + | + | + |  |  |  |  | 
 | FF(2071-00) | + | + | + | + | - | + | - |  | 
SSP5-8.5 | 2 warming |  | - | - | + | + |  |  | - | 
 | 3 warming |  |  |  |  |  |  |  |  | 
 | EF (2021-50) |  | + | - | - |  |  | - |  | 
 | FF (2071-00) |  |  |  |  |  |  |  |  | 
 |  | PRCP TOT | R95p | R99p | Rx1 Day | Rx5 Day | CWD | CDD | R10 | R20
SSP2-4.5 | 2 warming | - | + | - | - | - | - | + | - | 
 | 3 warming |  | - | - | + | - | - | + |  | 
 | EF (2021-50) |  | + | + | + |  |  |  |  | 
 | FF(2071-00) | + | + | + | + | - | + | - |  | 
SSP5-8.5 | 2 warming |  | - | - | + | + |  |  | - | 
 | 3 warming |  |  |  |  |  |  |  |  | 
 | EF (2021-50) |  | + | - | - |  |  | - |  | 
 | FF (2071-00) |  |  |  |  |  |  |  |  | 
+ Positive trends ; - Negative trends ; Significant positive trend (significance level 95%) ; Significant negative trend (significance level 95%)
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 11
SWAT calibration and validation
Extreme Precipitation Indices
Chart: Q Observed (m3/s)
Chart: Q Observed (m3/s)
Calibration (2007-2010)
Validation (2011-2014)
Percentage change in future precipitation extremes w. r. t. base period (1991-2020): (A) SSP2-4.5 (B) SSP5-8.5
 |  | PRCP TOT | R95p | R99p | Rx1 Day | Rx5 Day | CWD | CDD | R10 | R20
SSP2-4.5 | 2 warming | - | + | - | - | - | - | + | - | 
 | 3 warming |  | - | - | + | - | - | + |  | 
 | EF (2021-50) |  | + | + | + |  |  |  |  | 
 | FF(2071-00) | + | + | + | + | - | + | - |  | 
SSP5-8.5 | 2 warming |  | - | - | + | + |  |  | - | 
 | 3 warming |  |  |  |  |  |  |  |  | 
 | EF (2021-50) |  | + | - | - |  |  | - |  | 
 | FF (2071-00) |  |  |  |  |  |  |  |  | 
 |  | PRCP TOT | R95p | R99p | Rx1 Day | Rx5 Day | CWD | CDD | R10 | R20
SSP2-4.5 | 2 warming | - | + | - | - | - | - | + | - | 
 | 3 warming |  | - | - | + | - | - | + |  | 
 | EF (2021-50) |  | + | + | + |  |  |  |  | 
 | FF(2071-00) | + | + | + | + | - | + | - |  | 
SSP5-8.5 | 2 warming |  | - | - | + | + |  |  | - | 
 | 3 warming |  |  |  |  |  |  |  |  | 
 | EF (2021-50) |  | + | - | - |  |  | - |  | 
 | FF (2071-00) |  |  |  |  |  |  |  |  | 
+ Positive trends ; - Negative trends ; Significant positive trend (significance level 95%) ; Significant negative trend (significance level 95%)
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 12
Extreme Temperature indices
The hottest days are expected to be notably warmer (up to 50 oC) in the FF than that of the observed period (up to 43 oC)
Analyzing Intensity-Based Temperature Index Variations with Base Period
(A)
(B)
(C)
(D)
TXx : Monthly maximum value of daily maximum temperature ; TXn : Monthly minimum value of daily maximum temperature ; TNx : Monthly maximum value of daily minimum temperature ; TNn : Monthly maximum value of daily maximum temperature
 |  | TXx | TXn | TNx | TNn
SSP2-4.5 | 2 warming |  |  |  | 
 | 3 warming |  |  |  | 
 | EF (2021-50) |  | + |  | 
 | FF(2071-00) |  | + | + | +
SSP5-8.5 | 2 warming |  |  |  | 
 | 3 warming |  |  |  | 
 | EF (2021-50) |  |  |  | 
 | FF (2071-00) |  |  |  | 
 |  | TXx | TXn | TNx | TNn
SSP2-4.5 | 2 warming |  |  |  | 
 | 3 warming |  |  |  | 
 | EF (2021-50) |  | + |  | 
 | FF(2071-00) |  | + | + | +
SSP5-8.5 | 2 warming |  |  |  | 
 | 3 warming |  |  |  | 
 | EF (2021-50) |  |  |  | 
 | FF (2071-00) |  |  |  | 
+ Positive trends ; - Negative trends ;
Significant positive trend (significance level 95%); Significant negative trend (significance level 95%)
These trends suggest a warmer winter across the basin, with limited fluctuations in both maximum and minimum temperatures, resulting in more day-to-night temperature variation.
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 13
Extreme Annual Runoff
Q95 increases consistently, notably ~30% in Chenani and Domel under SSP5-8.5 in FF.
Q05 decrease for most subbasins, a maximum decline of 8.5% under SSP2-4.5
SSP2-4.5 showed Q95 in Udhampur decreased (~21.7%) in 3° C GWL
Projected change in discharge w.r.t the base period (A) Annual high flow Q95 (B) Annual low flow Q05
Domel | SSP2-4.5 |  | SSP5-8.5 | 
 | Q95 | Q05 | Q95 | Q05
2 warming |  |  |  | 
3 warming |  | - |  | 
EF (2021-50) |  |  |  | 
FF(2071-00) |  |  |  | 
Domel | SSP2-4.5 |  | SSP5-8.5 | 
 | Q95 | Q05 | Q95 | Q05
2 warming |  |  |  | 
3 warming |  | - |  | 
EF (2021-50) |  |  |  | 
FF(2071-00) |  |  |  | 
Udhampur
Chenani
Ramnagar
Domel
+ Positive trends ; - Negative trends ;
Significant positive trend (significance level 95%);
Significant negative trend (significance level 95%)
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 14
Catchment Scale Projections
The average annual BW in the catchment is also observed to increase, corresponding to increasing annual rainfall.
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 15
Sub-Catchment Scale Projections
Rainfall
Blue Water
SSP2-4.5
SSP2-4.5
SSP5-8.5
SSP5-8.5
2 °C
3 °C
NF
FF
2 °C
3 °C
NF
FF
Increased by 40.52%, 36.60%, and 38.16% in sub-basins 4, 5, and 8 during the FF under the SSP5-8.5 scenario.
Sub-basins 1, 3, 6 and 9 are observed where increase is minimum in each timeframes and under both SSPs.
Maximum increase in FF under SSP5-8.5.
However, the increase was substantially less in sub-basins 1, 3, 6, and 9 in 2 °C GWL and NF.
Base Period (1991-2020)
Base Period (1991-2020)
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 16
Sub-Catchment Scale Projections
Green Water Flow
Green Water Storage
SSP2-4.5
SSP5-8.5
SSP2-4.5
SSP5-8.5
2 °C
3 °C
NF
FF
2 °C
3 °C
NF
FF
The expected increase in GWF availability is more evident under SSP2-4.5 than under SSP5-8.5
The GWF component showed the highest growth in sub-basin 2 and the lowest in sub-basin.
Most of the subbasins projected a decrease in GWS within the range of -5%.
A very substantial increase of 3% was observed by the end of the century under SSP5-8.5
Base Period (1991-2020)
Base Period (1991-2020)
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 17
Drought Analysis
Catchment Scale
Sub-Catchment Scale
Temporal variation of hydrological drought SDI with respect to the base period
SSP2-4.5
SSP5-8.5
2 °C
3 °C
NF
FF
The SDI variability under both SSPs indicates the possibility of mild drought in the future, potentially causing water stress in the region.
Time Frames | SDI | 
 | SSP2-4.5 | SSP5-8.5
2 warming |  | 
3 warming |  | -
EF (2021-50) |  | 
FF(2071-00) |  | 
Time Frames | SDI | 
 | SSP2-4.5 | SSP5-8.5
2 warming |  | 
3 warming |  | -
EF (2021-50) |  | 
FF(2071-00) |  | 
+ Positive trends ; - Negative trends ;
Significant positive trend (significance level 95%);
Significant negative trend (significance level 95%)
Base Period (1991-2020)
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets

## Slide 18
Prioritized catchments
Performance Score (PS) | Priority Level
PS < 2 | Low Priority
2 ≤ PS < 3.5 | Moderate Priority
PS ≥ 3.5 | High Priority
Prioritization of catchments in the Tawi River basin under climate change adaptation (A), (C) NF and FF for SSP2-4.5 (B), (D) NF and FF for SSP5-8.5
The subbasins 1, 3, 6, and 9 were observed to be major regions that are impacted by water shortages under SSP2-4.5 in NF
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets
SSP2-4.5
SSP5-8.5
NF
FF

## Slide 19
Climate Trends: Rainfall patterns shifting, intensifying, and warming temperatures observed. Annual discharge variations highlight the necessity for water management.
Future Water: Projections foresee increased water factors, except for green water storage, posing challenges for urban water scarcity. Addressing demand, enhancing efficiency, and sustainable planning are pivotal.
Water Scarcity: Future forecasts indicate heightened drought risks, necessitating proactive resource management to mitigate impacts.
Prioritization: Integrated approach using hydrological modeling and AHP effectively prioritizes catchments, offering valuable insights for preliminary assessments.
Adaptation Urgency: Catchment prioritization stresses urgent need for proactive measures amid varying vulnerability levels, safeguarding water resources and ensuring resilience to climate change.
Conclusions
Introduction
Objective 2
Study Area
Methodology
Results
Literature Review
Timeframe and Targets