## Slide 1
Multi–decadal climate variability and capacity planning
of off–grid hybrid renewable energy systems
Yuting Cui1 , Jakub Jurasz1
Why is one weather year not enough for robust hybrid energy system design?
1Faculty of Environmental Engineering, Wroclaw University of Science and Technology, 50–377 Wroclaw, Poland
Scan for abstract
2. System and annual optimization setup
1. Introduction and research goal
3. Forty–five years of renewable resource variability
4. Weather variability reshapes capacity planning and performance
5. Moderate curtailment captures most benefits
Fig. 1. Off–grid solar–wind–diesel–pumped hydro storage (PHS) system
Annual model co-optimizes wind, solar, diesel generators(DG), and PHS capacities.
Objective function: minimize the levelized cost of electricity (LCOE).
Fig. 2. Daily wind and solar capacity factors over 1980–2024
Wind and solar resources both show clear inter–annual variability.
Wind is more irregular, while solar is more seasonally structured.
Wind capacity factor
Solar capacity factor
Day of year
Day of year
Fig. 4. Inter–annual variation in carbon intensity, LCOE, and cost structure
Fig. 3. Annual optimal capacities under 0%, 10%, and 20% curtailment limits
(a) 0% curtailment scenario
(b) 10% curtailment scenario
(c) 20% curtailment scenario
curtailment
curtailment
curtailment
Wind and solar capacities vary across weather years; DG remains comparatively stable.
Relaxed curtailment lowers LCOE and carbon intensity, but adverse weather years remain visible.
Relaxed curtailment enables larger renewable capacities.
6. Storage expansion shifts the cost–emission balance
Most cost–emission gains occur before about 15–20% allowable curtailment.
Fig. 5. Median LCOE and carbon intensity response to curtailment
Fig. 6. LCOE and carbon intensity distributions across PHS storage capacities
Off–grid hybrid systems are key to low–carbon electricity supply in remote areas.
Many planning studies rely on single–year renewable resource inputs, which can hide weather–driven planning bias.
We use 45 years of hourly wind and solar data to quantify capacity variability, curtailment marginal effects, and storage cost–emission trade–offs.
Larger PHS lowers carbon intensity but raises LCOE.
Further PHS expansion (>675MWh) yields limited carbon intensity gains at higher LCOE.
Take–home
messages
1. Single–year planning is not robust
Optimal capacities and performance vary widely across weather years. Multi–decadal assessment is essential.
2. Moderate curtailment captures most of the benefit
Relaxing the curtailment to 15–20% captures most of the improvement in cost and emissions.
3. Storage expansion creates a cost–emission trade–off
More storage lowers carbon intensity but raises the levelized cost of electricity. Balanced design is the key.
Acknowledgements:
The results reported here were obtained as part of project no. 2022/47/B/ST8/01113 funded by the Polish National Science Centre (Narodowe Centrum Nauki).