## Slide 1
Development and application of regional inversion systems for China:
methane emission tracking and mitigation
Yifan Li1,2, Drew C. Pendergrass2, Daniel J. Jacob2, Yunxiao Tang2, Jiaxin Qiu1, Bo Zheng1*
1 Tsinghua University, China 2 Harvard University, USA
For further information, please contact: lyf22@mails.tsinghua.edu.cn
Research motivation & Study objectives
Background
Regional-scale methane emission inversion
This study aims to:
Develop regional inversion frameworks
      → improve accuracy & reduce latency and cost
Apply to high-emission regions
      → quantify trends, identify drivers, and guide mitigation
Methane mitigation is critical for near-term climate control
Accurate regional estimates enable targeted mitigation
Yet current estimates remain highly uncertain and inconsistent
CH4
  Greenhouse gas with ～10-year lifetime
  Higher warming potential than CO2
  Rapidly increasing atmospheric concentration
Limited observations
Sparse and uneven spatial coverage
Discontinuous temporal coverage
Large biases and high background values
Number: 0 100 200 300 400
Complex framework
CH4
Concentration
Emission
High uncertainty
Computationally expensive
Model
Algorithm
Observation
High-resolution
Nonlinear
High boundary errors
Region
Atmospheric
condition
Geographical boundaries
Surface station
Satellite (GOSAT)
Major challenges in regional inversion
Prior input uncertainty
Meterology
Prior emissions
Inconsistent spatiotemporal resoultion
Uncertainty with spatial heterogeneity
Sinks: Soil absorption / OH / Cl / ...
Spatial distribution of emissions
Satellite-based inversion by data assimilation
Ground-based inversion by collocated air pollutants
Data assimilation: Local Ensemble Transform Kalman Filter
Minimize: J(x) = (x - xb)T(Pb)-1(x - xb) + γ(y -H(x))TR-1(y - H(x))
State vector
(emis./conc.)
Prior error
ensemble spread
Obs.
Observation operator
maps x into observation space
Inconsistent sources
t: downwind site
b: background site
EnhCGas = Gasd - Gas4,b
EnhR= EnhCCH4 / EnhCCO
τgas= 1/([OH] ∙ kgas)
CF = exp(t/τCH4) / exp(t /τCO)
FR = EnhR ∙ CF ∙ MCH4/MCO
FCH4 = FR ∙ FCO,inv
China’s CH4 emissions (2000–2021)
Mean emission: 48.4 ± 13.8 Tg yr-1
Emission trend: +1.1 ± 0.2 Tg yr-2
Socioeconomic development: +92.1 Tg
Declining Emission intensity: -78.1 Tg
Applied to China
Robustness & comparability: enabling long-term, large-scale inversion
Computational efficiency & transferability: applicable to observation-limited regions
Key factors:
Boudary conditions & Prior errors
CO
CH4
CH4
CO
CO
CH4
Well-mixed
Trajectory filter
ΔCH4 / ΔCO
Concentration
ΔCH4 / ΔCO
Emission flux
Satellite
-based CO flux
CH4 emissions
Method
(Weekly, 0.5º × 0.625º)
China’s CH4 emissions (2019–2024)
2019: 61.1 Tg → 2024: 66.8 Tg
Total: + 5.7 Tg & Livestock: +2.7 Tg
East 24%, South 21%, Southwest 18%
Applied to East Aisa
Weekly assimilation
LETKF algorithm
IterativeUpdate
Optimized
posterior
(Next prior)
TROPOMI
Bias-corrected
Observed CH4
CH4
Agriculture
Energy
Wetlands
Waste
Simulated CH4
Prior input
Bias-corrected
boundary condition
Method
Li, Y., Zheng, B.*. Tracking regional CH4 emissions through collocated air pollution measurement: a pilot application and robustness analysis
in China. npj Climate and Atmospheric Science 2025, 8 (1), 127.
Li, Y., Pendergrass, D., Jacob, D., Tang, Y., Qiu, J., and Zheng, B.*: Shifting Drivers of China's Methane Emissions amid Economic Growth and
Mitigation between 2019–2024. EGUsphere [preprint], 2026.
Related
Papers
Chart: 
| Combined wetland and inland freshwaters | Wetlands only | Biomass and biofuel | Fossil fuels | Agriculture and waste | Other natural sources
 | 242.8019 | 181.22 | 30.3745 | 95.0828 | 246.4769 | 42.5296
Wetlands &
freshwater
Biomass burning
& biofuel
Agriculture
& waste
Fossil fuel
Sources:
Paper 2
Paper 1
China
India
The U.S.
Brazil
600
400
200
0
Emissions (t grid-1)
Enhancement
concentration
Downwind
Background
- China’s CH4 emissions have increased by 2.3% yr-1 since 2000,
driven by socioeconomic development.
- Single-site observations constrain large-scale emissions.
- A promising tool for synergistic non-co-emitted gases inversion.
- Livestock largely drives China’s CH4 emission increase after 2019.
- We extend the global tool (CHEEREIO) to regional scales.
- Efficient LETKF enables near-real-time, high-precision, and
scalable inversion across regions.
Take
Home
Message
Notes: https://www.egu26.eu/authors/presenters.html
1.978 m × 1.183 m