## Slide 1: Instantaneous PPP convergence with a Decoupled Clock Model
marcus.glaner@geo.tuwien.ac.at
Marcus Franz Wareyka-Glaner1, Gregor Möller1
1 Department of Geodesy and Geoinformation, Technische Universität Wien, Austria
06 Mai 2026

## Slide 2: Decoupled Clock Model (DCM)
idea: code and phase measurements are not synchronized with the same level of precision
separate receiver code and phase clock error
uncommon parameterization
Wareyka-Glaner, 06/05/2026
receiver clock error
receiver code clock error
receiver phase clock error

## Slide 3: Uncombined Decoupled Clock Model
Code
Phase
Wareyka-Glaner, 06/05/2026

## Slide 4: Uncombined Decoupled Clock Model
Code
Phase
receiver code clock error
receiver phase clock error

## Slide 5: Uncombined Decoupled Clock Model
Code
Phase
reparametrized, details:
Naciri & Bisnath (2021)
Wareyka-Glaner, 06/05/2026

## Slide 6: Parameters
+ ambiguities + ionospheric delays
datum of the phase observations was lost (decoupling receiver clock)
define datum of ambiguities with a datum satellite (DS):
  ambiguities of DS are not estimated
  set ambiguities of DS to zero
→ float ambiguities are free of any delays or biases
→ LAMBDA 4.0 (Massarweh et al., 2024)

## Slide 7: Float
Fixed
, float, fixed parameters
, float, fixed ambiguities
, covariance matrices

## Slide 8: Test case
Software | (https://github.com/TUW-VieVS/raPPPid)
Data | 26 IGS MGEX stations, June 29, 2025
Observations | GPS: L1 + L2 + L5, GLONASS: G1 + G2 Galileo: E1 + E5a + E6, BeiDou-3: B1 + B2a + B3 1 sec interval, reset of solution: every 15 min
Satellite products | WUM MGEX rapid (Geng et al., 2022) orbits, clocks, biases, attitude
Processing mode | static-kinematic, post-processing
Wareyka-Glaner, 06/05/2026

## Slide 9: Stations
Wareyka-Glaner, 06/05/2026
receiver type:
Septentrio PolaRx5
Javad TRE-3 Delta
Trimble Alloy
… missing antenna calibrations for some GNSS frequencies

## Slide 10: ANTEX Corrections
missing E6 antenna calibration: → PCV: take nearest available
→ PCO: linear interpolation
… processed frequencies

## Slide 11: Fixed Results
TTCF … time to correct fix, achieved when 2D < 5 cm for the complete remaining period

## Slide 12: Single station
fixed solution
3D < 10 cm: 99.65%
3D < 5 cm: 98.04%
AREG (Arequipa, Peru)
more results and details: Wareyka-Glaner, M. F. (under review). Instantaneous PPP convergence with a decoupled clock model, triple-frequency multi-GNSS observations, and integer ambiguity fixing. GPS Solutions

## Slide 13: Summary
DCM is an elegant and innovative approach for PPP-AR
instantaneous convergence with rapid satellite products
future work:
  3+ frequencies
  real-time processing

## Slide 14: References
Geng, J., Wen, Q., Zhang, Q., Li, G., & Zhang, K. (2022). GNSS observable-specific phase biases for all-frequency PPP ambiguity resolution. Journal of Geodesy, 96(2), 11. https://doi.org/10.1007/s00190-022-01602-3
Glaner, M. F., & Weber, R. (2023). An open-source software package for Precise Point Positioning: raPPPid. GPS Solutions, 27(4), 174. https://doi.org/10.1007/s10291-023-01488-4
Naciri, N., & Bisnath, S. (2021). An uncombined triple-frequency user implementation of the decoupled clock model for PPP-AR. Journal of Geodesy, 95(5), 60. https://doi.org/10.1007/s00190-021-01510-y
Massarweh, L., Verhagen, S., & Teunissen, P. J. G. (2024). New LAMBDA toolbox for mixed-integer models: Estimation and evaluation. GPS Solutions, 29(1), 14. https://doi.org/10.1007/s10291-024-01738-z

## Slide 15: Supplementary

## Slide 16: raPPPid
open-source PPP software
GitHub: https://github.com/TUW-VieVS/raPPPid
documentation: https://vievswiki.geo.tuwien.ac.at/en/raPPPid
Wareyka-Glaner, 06/05/2026

## Slide 17
Software raPPPid (VieVS PPP) (Glaner & Weber, 2023)
Data 26 globally distributed IGS MGEX stations (June 29, 2025)
Observations GPS: L1+L2+L5, GLONASS: G1+G2, Galileo: E1+E5a+E6, BeiDou-3: B1+B2a+B3
Observation ranking GPS: WC, GLONASS: PC, Galileo: CQX, BeiDou: IPDX
Observation interval 1 sec, reset of solution: every 15 min
Processing mode post-processing, uncombined DCM, static-kinematic
Raw observation noise code 30cm, phase 2mm
Observation weighting elevation weighted, sin²(elev), cutoff angle 5°
Correction models Phase Wind-Up, solid Earth tides, relativistic effects, PCO + PCV, ocean loading
Troposphere model VMF3 + GRAD, residual zenith wet delay is estimated, process noise 5mm /√h
Float ambiguities constant, zero-difference, cycle-slip detection: dLi-dLj + HMW
PPP-AR fixing cutoff 10°, reference satellite = highest satellite
Fixing LAMBDA 4.0 (Massarweh et al., 2024)
Orbits, Clocks, Biases, Attitude WUM MGEX rapid (Geng et al., 2022)
Wareyka-Glaner, 06/05/2026

## Slide 18
missing antenna calibration: → PCV: take nearest available
→ PCO: linear interpolation (or nearest)
E5
B2a+b

## Slide 19: Missing Calibrations
Station | Antenna | Missing calibrations
MAW1 | AOAD/M_T AUST | GPS, GLONASS, Galileo, BeiDou
MIZU | SEPCHOKE_B3E6 NONE | Galileo E6, BeiDou B1, B3
NNOR | SEPCHOKE_B3E6 NONE | Galileo E6, BeiDou B1, B3
OWMG | TRM159900.00 NONE | GPS L5, Galileo, BeiDou
QUIN | ASH701945E_M SNOW | GPS L5, GLONASS, Galileo, BeiDou
YKRO | ASH701945C_M NONE | BeiDou B2a
ZAMB | AOAD/M_T NONE | GPS L5, Galileo, BeiDou
stations of the test case lacking antenna calibrations

## Slide 20: Statistics
FIXED |  | 
Ø TTCF1 (2D < 5 cm) | 2.44 | s
no correct fix | 0.00 | %
Ø 2D error | 0.60 | cm
Ø 3D error | 1.83 | cm
stdev 3D error after 15 min | 1.30 | cm
2D < 5 cm | 99.78 | %
3D < 5 cm | 96.59 | %
Ø ZTD error | 0.69 | cm
FLOAT |  | 
Ø convergence2 (2D < 10 cm) | 6.55 | min
no convergence | 5.81 | %
Ø 2D error | 10.71 | cm
Ø 3D error | 17.55 | cm
stdev 3D error after 15 min | 3.80 | cm
Ø ZTD error | 1.67 | cm
1 … time to correct fix, achieved when 2D < 5 cm for the complete remaining period
2 … achieved when 2D < 10 cm for the complete remaining period

## Slide 21: Fixed Results
TTCF … time to correct fix, achieved when 2D < 5 cm for the complete remaining period

## Slide 22: Histogram of TTCF
grey: cumulative distribution function
green: probability distribution function
TTCF within 3 seconds: 91.82 %
TTCF within 4 seconds: 99.32 %

## Slide 23: Datum Satellite
change of the DS after about 1.5 hours
affects, , and
does not affect and
→ consider change of DS in parameter vector

## Slide 24: Variables
reparametrized
frequency
geometric distance
speed of light
wet mapping function
noise and negligible errors
receiver code clock error
receiver phase clock error
Inter-Frequency Bias
receiver phase biases
zenith wet delay
ionospheric delay