## Slide 1: Predicting Air Pollution from sparse and movable observation points using machine learning techniques
Abhishek Ajit Sabnis, Mihai Mitrea, Lya Lugon, Karine Sartelet, Marc Bocquet, Xiaoyuan Cheng, Shupeng Zhu, Sibo Cheng
(Supplement material to Poster)

## Slide 2: Introduction
Motivation
We need
Accurate and fine scale monitoring
Urban planning
https://animalia-life.club/qa/pictures/effects-of-air-pollution-on-environment
https://www.geodair.fr/donnees/consultation
Climate change
mitigation policies
Current infrastructure of sensor stations is not sufficient to monitor full-grid pollutants

## Slide 3: Introduction
Problem Statement
Can we use machine learning to reconstruct the pollution field?
Task: Reconstruct multi variable field for NO2, O3, PM10, PM2.5
Challenge: Sparse number of available sensors that can vary temporally

## Slide 4: What are the existing limitations?
Ground truth simulations
ML model prediction
Example: 32 timesteps of NO2
Model input
(Voronoi Tessellations)
Most methods model pollutants individually (ignoring intrinsic interactions among pollutants)
Methods trained on synthetic data do not evaluate on real-world observations
Real world sensors switch on-and-off over time (temporal missing data)
NO2
O3
Create jointly processed ML based model trained on simulation data and evaluate on real world data

## Slide 5: Data Preparation
Simulation data (for training model)
. . .
t = 0
t = T
Simulation dataset
Jan 01 2014 to Dec 20 2014
(Hourly recording)
Step 1: Mask with sensor location
Step 2: Create Voronoi Tessellations
t = n
Apply augmentations on simulation dataset to mimic the real-world data distribution
NO2
O3
PM10
PM2.5
Before
After

## Slide 6: Model Training
Neural Network
(VUnet/ ViTAE/ CLSTM)
Multi pollutant Voronoi tessellation
Prediction
. . . .
Mean Ensemble
prediction
Predictions
Diffusion sampling
Sample n-dim Gaussian Noise
Voronoi
Embedding
Deterministic
Generative
Neural Network (Unet)

## Slide 7: Model Testing
Real world observation data
Inner city boundary
Randomly discard 2 sensors( )
. . .
s1
s20
Jan 01
Jan 07
Jan 15
Missing data
Construct Voronoi Tessellations
ML model prediction
Evaluate against heldout test points

## Slide 8: Methodology
Generative – Diffusion model
Add noise
Back Sampling
Denoiser (UNet model)
(Noisy Image)
Voronoi embedding
SDE Solver++
Denoised Image
Neural Network
Reverse Diffusion
Forward Diffusion

## Slide 9: Results
Simulation data
NO2 Ground
Truth
Discriminative (VUnet)
Generative (Diffusion)
Kriging (Traditional)
O3 Ground
Truth

## Slide 10: Results
Simulation data
PM10 Ground
Truth
Deterministic (VUnet)
Generative (Diffusion)
Kriging (Traditional)
PM2.5 Ground
Truth

## Slide 11: Results
Simulation data – Ensemble effect of Generative model
NO2
O3
PM10
PM2.5
Stochasticity enables ensembling in diffusion models and it outperforms the best discriminative model.
95% confidence bounding ellipse for ground truth vs predicted points of diffusion model

## Slide 12: Results
Simulation Data
NO2
O3
Demonstration of reverse sampling in diffusion model along with the power spectral graph of intermediate outputs.
The reconstruction happens in a coarse-to-fine manner with low frequency components (coarse structure) getting aligned followed by high frequency (fine details)
Diffusion implicitly performs alignment in frequency domain!

## Slide 13: Results
Real world data
Deterministic
Generative

## Slide 14: Results
Real world data
NO2
O3
PM10
PM2.5
Diffusion model has best alignment of power value with polyphemus (ground truth)
Distribution of ground truth vs predicted for real world data for Diffusion model. The error distribution for outer and inner city point is similar which shows our model performs irrespective of location being around a denser sensor network