## Slide 1: A first exploration of compound events including rainfall and potential adaptation measures in deltas
Dagmar Mennes, Frances Dunn, Hans Middelkoop, David Gold, and Marjolijn Haasnoot
Utrecht University, The Netherlands
EGU 2026
Compounds event including rainfall
Modeling framework
First results
Conclusion
Next
Background
 online presentation page
Pico navigation
main menu
Arrows can be used to navigate through slides in a subsection
Notes: Hey who am I what am I doing

## Slide 2: A first exploration of compound events including rainfall and potential adaptation measures in deltas
2 minute-madness
Improve the understanding of illustrative past and potential future compound events including rainfall by analysing their drivers, impact and responses.
ANP. (2022)
 To the online presentation page
Notes: Hint on influence on CC but assume much knowledge
Hint on adaptation stuf
- models often single hazards
- maladaptation offten occurs.

## Slide 3: Background of compound flooding in the Netherlands
Adaptation is often focused on individual events, potentially overlooking compound event risks (Haasnoot et al., 2020; Van Alphen, 2016; Schlumberger et al., 2024; Simpson 2021).
Developing adaptation strategies for compound events is difficult due to the uncertainty in their occurrence, complexity and the extremes of the events (IPCC, 2022)
We aim to create a method to understand the risks posed by uncertain rainfall including compound events, by analyzing past and potential future compound event scenarios with various adaptation strategies.
Background

## Slide 4: Definition of compound events and adaptation
“A compound event is an event that is created by multiple (not necessarily extremes) events (e.g., rainfall and a storm flood) or variables (e.g., a precondition) that together contribute to a societal or environmental risk or impact”.
 Extreme rainfall is the main driver in this research
Adaptation of figure 1 by Zscheischler et al., (2020)
Compounds event including rainfall
Notes: First what is a CER
Definitie
Afkorting
figuur
  Waaruit bestaat het
    Modulator groot stysteem e.g. lage druk systeem
    Driver regen/SS
    Hazard overstroming
    Impactschade
    Adaptatie miste een hazard stopt niet bij schade maar adaptatie vind plaats om risico te verminderen

## Slide 5: Potential compound events including rainfall in the Netherlands over the last 25 years
Compounding rainfall events
  Type of events:
    Multivariant: two simultaneous drivers
    Pre-condition: prior event influences the main event
Many Dutch storms often don’t include extreme rain. Climate change is expected to increase the possibility for extreme rainfall during storms which makes the occurrence of compound events with extreme rainfall more likely
Compound events with extreme rain | Year
Noorderzijlvest region (rain and storm surge) | 2012
Summer rain Limburg July 2021 (saturated soil and intense rainfall) | 2021
Storm Ciaran (rain and storm surge) | 2023
High water Zwolle (High river discharge and storm surge) | 2023
5 December ‘Sinterklaas’ storm | 2013
Dudley, Eunice and Franklin: triple storm | 2022
Storm Poly | 2023
Storm Boris | 2024
Storm Conall | 2024
Storm Darragh (twin storm) and Storm Eowyn | 2024
Storm Bert | 2024
Compounds event including rainfall
Notes: Side note for the identified events
  Some of the events are also caused due to mechanical failure.
  Some events with extreme rainfall not ‘perfect’ due to parameters like the rainfall intensity but are still included.
Archetypes CER events
Mention location of
Type of events most common
  Main drivers
What type of areas
lake ijssel
----------------------------------
Many potential hazard with, unfortunately missing rain sometimes for storms
  Climate change --> more rainfall in storms expected so potenitally more cer
Database shows devision in archetype regions
  Brought back to two main regions: east/west NED
    East: high relatively fast draining

## Slide 6: Archetype areas based on historical events and the hydrogeomorphology
Two main areas
  East: relatively high elevation, gravity drainage
  West: relatively low elevation, manual drainage (pumps)
Adaption of figure by Maas, B., Juch, S. & Bruijn (2025)
Compounds event including rainfall

## Slide 7: Model set up and stress test for various event scenarios and archetype
Model layout: polder archetype
  Agricultural fields, canals, lake and sea
Stress testing of various rainfall compound scenarios with different adaptation strategies
  Asses the effectiveness of different adaptation measures on impact parameters for different hazard scenarios
  Find robust adaptation strategies for various future scenarios
Method/toolkit for stress testing: Exploratory Modelling and Analysis (EMA) Workbench
Modeling framework
zoom in
zoom in
Adaption of figure 8 by Napier, John. (2021)

## Slide 8: Model set up for polders
Modeling framework
pump and/or sluice
pump
Activity of the pumps and sluices depends on the water level, and predefined thresholds in the next part of the system.
Adaption of figure 8 by Napier, John. (2021).
sea
polder
canal and/ or lake
zoom out

## Slide 9: XLRM framework for model set up
Uncertainties Rainfall timing and amount Sea level rise Storm surge | Policy levers and strategies Storage capacity Assigned flood areas Pump capacity Sluice capacity Dike strengthening |  | 
Model Bucket model | Impact parameters (Performance metrics) |  | 
 | Polder land Max inundation depth Max inundated area Duration of inundation | Canal Max water level Duration of elevated water levels | Lake Max water level Duration of elevated water levels
Robust Decision Making | RAND
zoom out
Modeling framework

## Slide 10: Run set up for a multivariant compound rainfall event
Rainfall scenarios: range 25300 mm in 1 hr
Sea level rise (SLR) scenarios: range 02 m
Storm Surge: 2 m on the day of the rainfall
Adaptation strategy: include a pump at the lake
First Results
Drivers rainfall & storm surge
Hazard flooding
Impact Inundation depth and duration, duration of elevated water levels and maximum water levels
Adaptation
Include pump to drain the lake alongside a sluice

## Slide 11: First results of a multivariant rainfall including compound event Event: rainfall and a storm surge
First Results
Lake impact
Canal impact
Polder impact
zoom in
zoom in
zoom in
Inundation and water levels over time
Zoom in

## Slide 12
Inundation depth and water levels over time
zoom out
First Results
50 mm rain & 1 m sea level rise
For a limit sea level rise the system is still able to drain fully. For a larger sea level rise the lake and the canal drainage is no longer possible unless the pump at the lake side (adaptation measure) is installed.
50 mm rain & 0 m sea level rise
zoom to lake

## Slide 13
Lake water levels over time for different sea level rises 50 mm rain and 2 m storm surge on day of rain
First Results
zoom out
With pump
No pump
0,5 m sea level rise
1 m sea level rise
The sluice switches on and off depending on the tides, and the pumps only work when needed
1 m sea level rise stops the sluice and if installed the pump stays on until the whole system is drained

## Slide 14: Polder impact Colour reflects the inundation duration (days)
First Results
zoom out
A sea level rise of 0.6 m hinders downstream discharge. As a result drainage of the polder is hindered, leading to longer inundation durations.
The pump at the lake side allows constant drainage of the system and thus sea level is no longer a controlling factor and the duration only depends on rain.
A storm surge, which hinders the sluice downstream, slightly increases the duration of inundation.
First Results

## Slide 15
First Results
zoom out
Canal water level impact Colour reflects the duration of elevated water levels (days)
First Results
First Results
When the sea rises above 0.6 m the sluices downstream are hindered, which limits the canal discharge increasing the duration of the impact
2 meter storm surge increases the duration of the higher water levels with a few hours
The instalment of the pump at the lake allows for continues drainage of the canal lowering the duration of the impact

## Slide 16
First Results
zoom out
Lake water level impact Colour reflects the duration of elevated water levels (days)
First Results
SLR crosses a threshold and the sluices at the lake side become hindered. This hinders the discharge form the canal leading to long durations of high water levels
2 meter storm increases the duration of the elevated water levels with a few hours
The adaptation measure at the lake (installment of the pump) allows for continues drainage in the canal lowering the duration of the impact
Sea level rise starts hindering and eventually stops the discharge from the lake leading to long durations of the impacts
The pump ensures a constant discharge from the lake to the sea leading to a maximum impact of 9 days

## Slide 17: Conclusion
The Netherlands is susceptible to rainfall including compound events based on past events and it is expected that climate change will increase the risk
The susceptible areas in the Netherlands can be subdivided into manual draining and gravity draining regions
These first scenarios show that downstream event drivers influence the upstream impact by limiting the drainage of the system and adaptation is needed to limit the consequences
Conclusion
ANP. (2023)

## Slide 18: Team
Dagmar Mennes MSc
Dr. Frances Dunn
Dr. ir. David Gold
Prof. dr. Marjolijn Haasnoot
Prof. dr. Hans Middelkoop

## Slide 19: References
ANP. (2022, January 24). Limburg flood was beyond worst-case scenario: Report. NL Times. https://nltimes.nl/2022/01/24/limburg-flood-beyond-worst-case-scenario-report
ANP. (2023, November 23). Storm surge barriers to close on Thursday over flooding concerns. NL Times. Storm surge barriers to close on Thursday over flooding concerns | NL Times
Haasnoot, M., Kwadijk, J., Van Alphen, J., Le Bars, D., Van Den Hurk, B., Diermanse, F., Van Der Spek, A., Oude Essink, G., Delsman, J., & Mens, M. (2020). Adaptation to uncertain sea-level rise; how uncertainty in Antarctic mass-loss impacts the coastal adaptation strategy of the Netherlands. Environmental Research Letters, 15(3), 034007. https://doi.org/10.1088/1748-9326/AB666C
IPCC. (2022). Summary for Policymakers. In Climate Change 2022 – Impacts, Adaptation and Vulnerability (pp. 3–34). Cambridge University Press. https://doi.org/10.1017/9781009325844.001
Maas, B., Juch, S.& Bruijn (2025). Landelijk waterbeeld grootschalige extreme regen. Deltares. 21-10-2025
Napier, J. (2021). Living with Water: Infrastructure and Urbanism in Jakarta. Ecocycles, 7(1), 52–72. https://doi.org/10.19040/ecocycles.v7i1.191
Schlumberger, J., Haasnoot, M., Aerts, J. C. J. H., Bril, V., van der Weide, L., & de Ruiter, M. (2024). Evaluating Adaptation Pathways in a Complex Multi-Risk System. Earth’s Future, 12(5). https://doi.org/10.1029/2023EF004288
Simpson, N. P., Mach, K. J., Constable, A., Hess, J., Hogarth, R., Howden, M., Lawrence, J., Lempert, R. J., Muccione, V., Mackey, B., New, M. G., O’Neill, B., Otto, F., Pörtner, H. O., Reisinger, A., Roberts, D., Schmidt, D. N., Seneviratne, S., Strongin, S., … Trisos, C. H. (2021). A framework for complex climate change risk assessment. In One Earth (Vol. 4, Issue 4, pp. 489–501). Cell Press. https://doi.org/10.1016/j.oneear.2021.03.005
Van Alphen, J. (2016). The Delta Programme and updated flood risk management policies in the Netherlands. Journal of Flood Risk Management, 9(4), 310–319. https://doi.org/10.1111/jfr3.12183n
​Zscheischler, J., Martius, O., Westra, S., Bevacqua, E., Raymond, C., Horton, R. M., van den Hurk, B., AghaKouchak, A., Jézéquel, A., Mahecha, M. D., Maraun, D., Ramos, A. M., Ridder, N. N., Thiery, W., & Vignotto, E. (2020). A typology of compound weather and climate events. In Nature Reviews Earth and Environment (Vol. 1, Issue 7, pp. 333–347). Springer Nature. https://doi.org/10.1038/s43017-020-0060-z