## Slide 1
Simulating the fate and Transport of Microplastics (MP) in a river corridor (Rhine River)
Shabiha Sultana Rimi1, Christian Schmidt1, Jan H. Fleckenstein1,2
1Helmholtz Centre for Environmental Research, UFZ, Department of Hydrogeology, Leipzig, Germany; 2 Hydrologic Modeling Unit, BayCEER, University of Bayreuth, Germany
Motivation
Research Questions
Outcome
Method
Advection and turbulence processes drive MP transport.
Higher discharge increases suspended concentrations, reduces sedimented MP.
Elevated discharge enhances remobilization of deposited particles.
High-density MP shows greater deposition and lower resuspension than low-density MP.
Bank full discharge is 3903m3/s
Deposition from total MP input
    PS = 2.5%
    PVC = 2.84%
Major deposition is at banks
    PS = 33.5%
    PVC = 38.23%
Resuspension from deposited MP
    PS = 40%
    PVC = 6%
References
Rolf, M., Laermanns, H., Kienzler, L., Pohl, C., Möller, J. N., Laforsch, C., Löder, M. G. J., & Bogner, C. (2022). Flooding frequency and floodplain topography determine abundance of microplastics in an alluvial Rhine soil. Science of the Total Environment,
836, 155141. https://doi.org/10.1016/j.scitotenv.2022.155141
Lu, X., Wang, X., Liu, X., & Singh, V. P. (2023). Dispersal and transport of microplastic particles under different flow conditions in riverine ecosystem. Journal of Hazardous Materials, 442, 130033. https://doi.org/10.1016/j.jhazmat.2022.130033
Deltares. (2025). D-Flow Flexible Mesh User Manual (Version 2025, Revision 80442). Delft, The Netherlands: Deltares
Stadtentwässerungsbetriebe Köln. (2026). Hochwasser­geschichte Kölns. Steb-Koeln.De.
Widespread occurrence of MP across natural compartments.
MP are transported through river corridor to land and oceans.
Floods mobilize and re/distribute MP, enhancing deposition
How MP are transported in fluvial system?
Where are they deposited in floodplains?
How much of MP mobilized during and deposited after the flood event.
3.5 km Rhine River section in Cologne, Germany
Flood event : 2021 winter (3.5 years return period) (Stadtentwässerungsbetriebe Köln,2026)
3D Hydrodynamic model: Delft3D FM
  Triangular grid (25 m resolution)
  11 vertical sigma layers.
  Boundary Conditions
    Upstream: discharge, Downstream: water surface elevation
  Calibration parameter Manning’s n, varied on landuse : 0.027–0.04)
Constant upstream MP input (1 µm/m³)
MP type (diameter: 0.1mm)
  Polyvinylchlorid (PVC): 1195 kg/m³)
  Polystyrene (PS): 1030 kg/ m³
Polystyrene (PS)
Polyvinylchlorid (PVC)
A
B
D
Flood 2021 (February)
D
Ponding after flood
C
Resuspension
Resuspension
Flow path under 3 different flow conditions
Pond 2
Pond 3
Pond 1
Pond 1
Pond 2
Pond 3
Chart: Date
Conclusion