## Slide 1: Satellite-based climate data records of the surface solar radiation Jörg Trentmann, Uwe Pfeifroth, Steffen Kothe, Vivien Priemer

## Slide 2
Surface Solar Irradiance / Sunshine duration highly relevant, e.g. climate monitoring, solar energy assessments
Most studies rely on surface observations, e.g., BSRN, GEBA, national networks
Spatial and temporal information of surface radiation can accurately be derived from satellite observations….
Surface Irradiance / Sunshine Duration
Sanchez-Lorenzo et al., JGR, 2015

## Slide 3
Spatial and temporal information of surface radiation can accurately be derived from satellite observations, because…
  … satellites can well detect clouds (= bright) during daytime
  … clear-sky solar radiative transfer is well simulated assuming auxiliary data (e.g., water vapor, aerosol) is available
Surface Irradiance / Sunshine Duration

## Slide 4: CM SAF Surface Solar Radiation Data Records
Global radiation (SIS), Direct irradiance (SID, DNI), Sunshine Duration (SDU)
Resolution
  Spatial: 0.05° × 0.05°
  Temporal: 30-min, daily, monthly
Coverage
  Spatial: Meteosat full disk
  Temporal: 1983 to 2017
Accuracy
  SIS: 5 W/m2 (mm) / 12 W/m2 (dm)
Surface Solar Radiation Dataset – Heliosat (SARAH)
Resolution
  Spatial: 0.25° × 0.25°
  Temporal: daily, monthly means
Coverage
  Spatial: global
  Temporal: 1982 to 2015
Accuracy
  SIS: 9 W/m2 (mm) / 19 W/m2 (dm)
CLARA (Clouds, Albedo, Radiation based on AVHRR)
SARAH and CLARA are freely available from the CM SAF:
www.cmsaf.eu
More information: Poster P.112, Thursday
Notes: Data freely available, without restrictions

## Slide 5
Global radiation (SIS)
Sunshine Duration (SDU)
Accuracy: 5 W/m2 (mm) / 12 W/m2 (dm)
Stability: ~ 1 W/m2/dec
Accuracy: 17 h (ms) / 1 h (ds)
Stability: ~ 1 hr / dec

## Slide 6
Pfeifroth et al (2018), J. Geophys. Res., 123, 1735-1754, doi:10.1002/2017JD027418.
Climate Analysis, Trend Analysis
Solar Energy Modeling
Urraca, et al., (2017), Solar Energy, 158, 49-62, doi:10.1016/j.solener.2017.09.032.
Quality control of surface measurements
Merging of surface and satellite data
e.g., PV GIS (JRC); Poster P.76; Friday
Walawender, J (2018) CM SAF Visiting Scientist Report
„Sunny Days“, Budapest

## Slide 7
TCDR
ICDR
+

## Slide 8
Climate Monitoring: Climatology + recent data
CM SAF provides (almost) near-realtime data for SARAH-2 (dt ~ 3 days)

## Slide 9
Positive anomaly of sunshine duration in 2018 in Western / Northern Europe
Normal sunshine duration in Southern and Eastern Europe
Germany: 2018 close to the all-time record (2003)

## Slide 10
Positive anomaly of sunshine duration in 2018 in Western / Northern Europe
Normal sunshine duration in Southern and Eastern Europe
Germany: 2018 close to the all-time record (2003)

## Slide 11
CM SAF Surface Solar Radiation Data Records
What’s next in SARAH-3 (available in 2021)
  Improved retrieval over snow-covered surfaces
  Improved surface albedo (aerosol?) input
  Use of (daily!) ERA-5 water vapor information

## Slide 12
Daily Global Radiation
Evaluation with surface measurements (Germany)
Good agreement with surface measurements

## Slide 13
Daily Global Radiation
Systematic under-estimation of surface radiation in snow-covered situations
e.g., March:
  bias: -21 W/m2
  abs. bias: 26 W/m2
Problem: Snow is classified as cloud
Notes: CDC snowmask is used for the snowdays
1983-2015 every month
SARAH underestimates in cases of snow, because due to the Heliosat method the snow is often deteced as clouds -> radiation is reflected back and will not reach the surface -> radiation smaller as in reality
This effect ist larger at days with less clouds (higher values) due to the higher incoming radiation
Heliosat is only able to detect snow , if there is the whole month snow. -> the clear sky value includes the snow
Largest difference betweenn snow and no snow days in March
higher global irradiance (SIS) than in the other winter months and more snow than in the other spring and autumn months
Less constant snow regions -> Snow vanishes in more regions, less regions with completly snow

## Slide 14
Snow Detection
HelSnow
Status quo: Separation between cloud and snow problematic (only 3 spectral channels available from historic satellites)
Approach: Separation between Cloud and Snow based on ‚motion‘
Intelligent / modern / efficient programming (OpenCV: ‚optical flow‘) allows the processing of long time series
18 March 2006, 1200 + 1230 UTC

## Slide 15
Snow Mask (based on HelSnow)
Mean Number of Snowdays, NDJFMA, 1989 - 2015
Resolution
  Spatial: 0.05° × 0.05°
  Temporal: daily
Coverage
  Spatial: Meteosat full disk
  Temporal: 1989 to 2015 (1983 - 2017)
Accuracy
  Moderate quality
    bias: 0.46
    POD: 0.36
    ETS: 0.23
Realistic spatial distribution and temporal variability of snow coverage, but not meant for climate analysis
2009/2010
2013/2014

## Slide 16
Surface Radiation (SARAH-2)
10 March 2010

## Slide 17
Surface Radiation (SARAH-2.5)
10 March 2010

## Slide 18
Surface Radiation (SARAH-2.5)
March 2006
Substantial improvement of data quality over snow (March 2006, Germany):
  bias: -13.3 W/m2 (SARAH-2: -23.8 W/m2)
  abs. bias 18.6 W/m2 (SARAH-2: 26.3 W/m2)
Accuracy of satellite-derived surface solar radiation still below average under snow-covered conditions

## Slide 19
Summary
CM SAF provides surface radiation climate data records (SARAH / CLARA) with high accuracy and stability as well as corresponding near-realtime data (SARAH-ICDR)
For Europe / Africa, we provide high resolution (temporal / spatial) data of surface radiation and sunshine duration
Combined use of TCDR / ICDR allows local / regional climate monitoring
Reduced quality of surface radiation data under snow-covered conditions; new snow detection scheme allows improved retrieval of surface radiation
5th CM SAF User Workshop (3–5 June 2019) & EUMETSAT Advanced Climate Training Course (5–7 June 2019), Mainz, Germany