## Slide 1: Towards the combination of in-situ and satellite-based solar radiation data in near-realtime - The project DUETT at DWD Anna Klameth, Sven Brinckmann, Jörg Trentmann UP1.5 Atmospheric measurements: Instruments, experiments, networks and long-term programs using in-situ and remote sensing techniques
Quelle: https://www.dwd.de/DE/forschung/atmosphaerenbeob/wettersatelliten/satelliten_meteosat_node.html
Bild: S. Wacker

## Slide 2
1
2
3
4
Introduction to DUETT
Current status DUETT
Validation results DUETT
Summary and outlook
Quelle: https://www.dwd.de/DE/forschung/atmosphaerenbeob/wettersatelliten/satelliten_meteosat_node.html
OUTLINE

## Slide 3: 1 Introduction to DUETT
.
TODAY
FUTURE
PARAMETER SUNSHINE DURATION AT DWD STATIONS
new solar radiation measuring network at DWD
  automation
  high quality sensors (WMO)
  economic efficiency
improving quality and spatio-temporal resolution of satellite data
combination of both data sources in near-realtime = DUETT
METEOSAT generations
2023 ~
spatial
resolution
temporal
resolution
number of
channels

## Slide 4: DUETT (10/2019 – 07/2023)
.
pyranometer data
future 42 stations (DWD)
every 10 min
satellite data based on METEOSAT 11 (SEVIRI)
every 15 min
near-realtime
detailed collection of user requirements
development of merging algorithms global radiation /sunshine duration
operational near-realtime production
area-wide high-quality data sets for Germany

## Slide 5: 2 Current status DUETT
.
development of algorithms based on geostatistics completed (s. presentation S. Brinckmann, UP2.3 on 9th September, 09.45 am)
operational test phase started recently (until May 2023)
Product details:
  hourly data (HH:50 UTC)
  2x2 km raster; derived station data
  area of Germany
  available at HH+1:05 UTC
DUETT 1-h-sum
DUETT 1-h-mean
Global radiation
Sunshine duration

## Slide 6: 3 Validation results DUETT
.
validation period: 03/2021 – 02/2022
current software version 001 (reprocessed)
global radiation: ~ 70 independent validation stations
sunshine duration: ~ 200 independent stations
available validation stations sunshine duration
number of stations
available validation stations global radiation
number of stations

## Slide 7: Global radiation: comparison SAT vs. DUETT for validation stations
SAT- station data
mean bias: 5.9 W/m² (all day)
mean abs. bias: 18.8 W/m² (all day)
W/m²
date
DUETT- station data
mean bias: 3.2 W/m² (all day)
mean abs. bias: 15.7 W/m² (all day)
W/m²
date

## Slide 8: Results over all validation stations (03-12/2021)
green: station data blue: DUETT
hourly differences
mean day course
sunshine duration
hour (UTC)
sunshine duration (min)
mean bias: 4 min
mean abs. bias: 7 min
hourly differences (daytime) (UTC)
zoomed in
number of hourly values
hourly differences
mean day course
global radiation
mean bias: 9 W/m²
mean abs. bias: 38 W/m²
hour (UTC)
global radiation (W/m²)
hourly differences (daytime) (UTC)
number of hourly values

## Slide 9: Spatial analysis – global radiation (03-12/2021)
.
sunny: SDU > 50 Min, partly cloudy: SDU 10-50 Min, cloudy: SDU < 10 Min

## Slide 10: Spatial analysis – sunshine duration (03-12/2021)
.
sunny: SDU > 50 Min, partly cloudy: SDU 10-50 Min, cloudy: SDU < 10 Min

## Slide 11: Station-based analysis – good examples
.
Global radiation
Sunshine duration
station Berus
station Elpersbuettel
global radiation - DUETT (W/m²)
global radiation - station data (W/m²)
correlation: 0.98
n = 7162
sunshine duration - DUETT (min)
sunshine duration - station data (min)
correlation: 0.92
n = 7170

## Slide 12: Station-based analysis – challenging examples
Global radiation
26th December 2021, 11:50 UTC
snow cover and clear sky
26th Dec 2021 11:30 UTC

## Slide 13
sunshine duration, Oberstdorf
topographic shadowing
Sunshine duration (min)
hour (UTC)
mean day course
green: station data
blue: DUETT

## Slide 14: 4 Summary and outlook
improvement of satellite data through operational combination with in-situ measurements in near-realtime
best performance of DUETT - algorithms with homogeneous conditions (sunny or overcast)
tendency towards overestimation of DUETT products
snow cover in clear sky conditions and topographic shadowing (at certain stations) challenging -> plans to integrate shadowing correction and snow mask
integration of METEOSAT Third Generation FCI data with higher spatio-temporal resolution in 2023
.

## Slide 15: Thank you for your attention !
Contact DUETT:
Anna.Klameth@dwd.de
Sven.Brinckmann@dwd.de
More about in UP 2.3