## Slide 1: Spatial structures in atmospheric boundary-layer flow – wind tunnel modeling
Klára Jurčáková and Radka Kellnerová
Institute of Thermomechanics of the Czech Academy of Sciences, Prague
EMS Annual Meeting 2022

## Slide 2: Motivation
Coherent structures = the building-blocks of turbulent ﬂow
What are the characteristics of these building-blocks and how are they organized?
Horseshoe and hairpin vortices
Adrian RJ, Meinhart CD and Tomkins CD. 2000. Vortex organisation in the outer region of the turbulent boundary layer. J Fluid Mech 422: 1-54.

## Slide 3: Field site – Kopisty observatory
lake
hilly forested area
Industrial area
Wind rose
at 80 m

## Slide 4: Field site – Kopisty observatory
Coherent structures in turbulent flow are of interest basic research
3D sonic anemometers
at heights 20, 40, 60, and 80 meters
Meteorological tower
80 m high
Operated by the Institute of Atmospheric Physics of the Czech Academy of Sciences

## Slide 5: Wind tunnel modelling of ABL
The aerodynamic boundary layer was first defined by Ludwig Prandtl in 1904.
Theory of turbulence, thermal effects, similarity theories
ABL is a special case of aerodynamic boundary layer.
Turbulence self-similarity, similarity numbers – Reynolds number
Outer scales are limited by the wind-tunnel dimensions, inner scales are limited by viscous dissipation

## Slide 6: Wind tunnel modelling of ABL
Scaled models (1:100 to 1:1000), time runs faster (100:1 to 1000:1)
Scaled model of ABL in wind tunnel, using vortex generators and roughness
Characteristics as roughness length, intensity of turbulence, integral length scale, power spectra, etc., must match in the given scale.

## Slide 7: Particle Image Velocimetry - PIV
2 velocity components in 2D plane
Time- resolved PIV – analysis of flow dynamics
Correlation of two consecutive images

## Slide 8: Kopisty Observatory model
Time is rescaled to the full scale
Along-wind velocity fluctuations:
  Blue – low-momentum regions
  Red – high-momentum regions

## Slide 9: Temporal correlation - autocorrelation
Velocity time series
Autocorrelation function

## Slide 10: Temporal correlation - autocorrelation
Velocity time series
Autocorrelation function
Integral time scale
Integral length scale
L=t·U
Taylor hypothesis of frozen turbulence

## Slide 11: Two-point correlations – spatial corr.
Correlations of Along-wind velocity fluctuations at two points
1/e value larger than field of view
Lateral velocity component

## Slide 12: Two-point correlations – spatial corr.
Correlations of Along-wind velocity fluctuations at two points
1/e value larger than field of view

## Slide 13: Two-point correlations – spatial corr.
Correlations of Along-wind velocity fluctuations at two points
1/e value larger than field of view

## Slide 14: Spatio-temporal correlations
Two-point correlations with a time lag
Drift of the maximal correlation ≈ average advective velocity of coherent structures

## Slide 15: Further processing
Other velocity components, cross-moments
Quadrant analysis – sweep and ejection events, conditional sampling
Measurement in vertical
Extreme value statistics
Critical points of comparison between wind-tunnel results and observations
Averaging time
Thermal stability

## Slide 16: Take away
Wind tunnel modelling is a tool to help us understand spatio-temporal connections important for boundary layers dynamics
Taylor hypothesis of frozen turbulence is applicable in fully developed turbulence further from the surface
Acknowledgement
This work was carried out thanks to the support of the Czech Ministry of Education, Youth, and Sports (project no. LTC 20056), and the institutional support RVO 61388998.
Thank you for your attention!