## Slide 1: Impact of Sea-Breeze Regimes on Wind Power Production at the Pecineaga Wind Farm (Romania)
Crina Radu, Ionut Lita, Georgeta Bandoc, and Adrian Dobre
Notes: [Sources]
User-supplied EMS-26_Radu-et-al.pptx.

## Slide 2: Romanian sea-breeze evidence remains limited
From Aristotle’s Meteorologica to >3,000 studies
(Radu et al, 2026)
• Black Sea studies document circulation structure, aerosols and regional dynamics, but Romanian coastal evidence remains limited.
• Sea breezes alter wind, temperature, convection, air quality—and the operating wind seen by coastal turbines.
• The open question is no longer whether they occur, but how often they matter for energy production.
Knowledge gap → quantify the energy relevance of objectively detected regimes.
Notes: [Sources]
Radu, C., Bandoc, G., Degeratu, M., “Sea Breeze Occurrence on the Romanian Black Sea Coast”, user-supplied manuscript, Introduction and Fig. 1.

## Slide 3: Pecineaga links coastal meteorology to operating turbines
SOUTH-EAST ROMANIA
Southern Dobrogea · Black Sea coastal sector
Wind-farm / land reference: 43.9148°N, 28.4709°E
Marine reference: 43.8922°N, 28.6941°E
8
SG170 turbines
48 MW
installed capacity
135 m
hub height
1999–2024
analysis period
How much of the park’s production is associated with pure and embedded sea-breeze regimes?
Pecineaga wind farm localization
The Pecineaga wind farm was officially inaugurated by Eurowind Energy on April 29, 2026.
Notes: [Sources]
Pecineaga_energy_attribution_integrated(1).docx, Abstract and methodological rationale; productie brize Pecineaga W jul-26.xlsb.xlsx, sheets Foaie1 and all.

## Slide 4: Detection evolved from expert screening to an objective hourly method
1
Empirical screening
Station wind and temperature · satellite fronts · synoptic fields
2
Sea Breeze Index
SBI compares synoptic wind forcing with the land–sea thermal gradient
3
Multi-parameter filter
Thermal contrast + marine wind rotation + speed response + synoptic consistency
4
Long-term application
Hourly classification transferred to the 1999–2024 Pecineaga dataset
Objective detection captures embedded regimes that manual screening tends to miss.
Notes: [Sources]
Radu et al., user-supplied manuscript, Data and Methods; Pecineaga_energy_attribution_integrated(1).docx, methodological rationale.

## Slide 5: SBI separates thermal forcing from the synoptic-flow direction
• C1b — pure sea-breeze regime used in the Pecineaga analysis: thermal forcing overcomes weak opposing offshore flow.
• C4 — embedded sea breeze: onshore synoptic and thermal components act in the same broad direction.
• Other quadrants represent blocked or thermally inhibited conditions and are not counted as productive sea-breeze regimes.
Romanian-coast critical SBI: 3.4 m² s⁻² K⁻¹
SBI plot for 2018 cases (Radu et al, 2026)
Notes: [Sources]
Radu et al., user-supplied manuscript, Theoretical Method and Fig. 4. Romanian-coast critical SBI value reported as 3.4 m² s⁻² K⁻¹.

## Slide 6: Initiation and inland advance are diagnosed separately
1
Marine baseline
Point 1
Fixed offshore reference
2
Initiation
4–1
Near-coastal land–sea contrast
3
Front advance
7–1
Primary inland propagation signal
4
Farm impact
7–4
Secondary sensitivity deeper inland
Events are retained only when SBI, thermal contrast and the wind response evolve coherently.
1
2
3
4
5
6
7
8
9
10
Meteo object, lidar
Existing wtg
New wtg
Spatial distribution of 3km era5 grid data used for analysis
Notes: [Sources]
Pecineaga_energy_attribution_integrated(1).docx, “Methodological rationale for the selection of analysis points”.

## Slide 7: Detect at 50 m; evaluate energy at the 135 m hub height
• ERA5-driven WRF (EMD), 3 km, hourly, 1999–2024
• Event detection at 50 m where the sea-breeze signature is strongest
• Fixed event timestamps carried to 135 m through vertical extrapolation
• 2021 lidar, 15-minute data, used to assess shear and PBL structure (for vertical extrapolation)
WindPRO production model
8 × SG170 6.0 MW
Turbine-specific power curve
Air-density correction
Direction-dependent wake response
Hourly regime subsets
The same production assumptions are retained for observed and counterfactual states.
Notes: [Sources]
Pecineaga_energy_attribution_integrated(1).docx, “Extension of Sea-Breeze Analysis to Turbine Hub Height”; user-supplied Excel production workbooks.

## Slide 8: Shapley allocation resolves nonlinear turbine response
Uₜₒₜₐₗ,t = UCG,t + USB,t
P(UCG + USB) ≠ P(UCG) + P(USB)
Near cut-in, two weak components can jointly produce power; opposing vectors can also reduce the resultant wind.
Two-component Shapley allocation
φSB,t = ½ [ESB,t + (Etotal,t − ECG,t)]
φCG,t = ½ [ECG,t + (Etotal,t − ESB,t)]
φSB,t + φCG,t = Etotal,t
Small negative residuals are treated as negligible calculation artefacts linked to the simplified PBL representation; final reporting uses aggregated contributions.
Notes: [Sources]
Pecineaga_energy_attribution_integrated(1).docx, “Attribution of Wind Power Production under Mixed Synoptic–Sea-Breeze Conditions”; Shapley (1953).

## Slide 9: Embedded sea breezes dominate productive regimes
Chart: 
| Pure (C1b) | Embedded (C4)
Detected hours | 7058 | 51337
7.3×
more embedded than pure hours
C1b: 3.1% of all hours
C4: 22.5% of all hours
Frequency—not event intensity alone—makes embedded regimes the main pathway to energy impact.
Notes: [Sources]
Productie_Oara_Parc_Eolian_1999_2024.xlsx, “Date Orare (1999-2024)”; counts recomputed from hourly category labels.

## Slide 10: Sea-breeze dynamics account for 15.65% of annual production
Chart: 
| Sea-breeze attributed | Remaining production
Mean annual energy | 28.29 | 152.45
15.65%
mean share of annual production
28.29 GWh/year
mean sea-breeze-attributed energy
The percentage is calculated after aggregating hourly allocations—not by averaging unstable instantaneous ratios.
Notes: [Sources]
Statistica_Briza_Marina_1999_2024.xlsx, “Sinteză & Extrema Briză”; Productie_Oara_Parc_Eolian_1999_2024.xlsx, “Rezumat Anual (AEP)”.

## Slide 11: The relative contribution peaks in spring
Chart: Share of seasonal production (%)
| Spring | Summer | Winter | Autumn
Sea-breeze share | 27.84 | 18.45 | 11.37 | 7.55
March 29.12%
April 30.70%
monthly maxima
November 5.88%
December 6.04%
Thermal contrast and sufficiently productive winds overlap most effectively in spring.
Notes: [Sources]
Statistica_Briza_Marina_1999_2024.xlsx, “Statistică Sezonieră” and “Statistică Lunară”.

## Slide 12: Interannual variability requires a homogeneity check
Chart: Annual production share (%)
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
Sea-breeze share | 28.65 | 28.41 | 27 | 27.4 | 21.18 | 29.54 | 10.06 | 10.59 | 12.98 | 13.77 | 10.17 | 11.06 | 13.19 | 13.21 | 11.02 | 10.67 | 12.45 | 13.79 | 12.92 | 8.74 | 11.95 | 11 | 12.96 | 15.95 | 14.16 | 12.29
MAX
2004
29.54%
MIN
2018
8.74%
The step after 2004 is flagged for sensitivity and PBL/decomposition checks—not interpreted as climate change.
Notes: [Sources]
Statistica_Briza_Marina_1999_2024.xlsx, “Statistică Anuală Detaliată”. Interpretation treats the discontinuity as a method/data-homogeneity issue rather than a climatic trend.

## Slide 13: Embedded regimes modify the marine-sector production pattern
• Pure sea-breeze cases do not show a stable marine-sector signature because the background flow is weak and directionally variable.
• Embedded cases display clearer alignment with marine inflow and modulate the already productive northerly to north-easterly sectors.
• A sea-breeze contribution therefore need not appear as a distinct easterly peak in the park-level wind rose.
Sea breeze acts mainly as a modifier of the prevailing coastal wind climate.
Mainly wind direction at Pecineaga wind farm
Notes: [Sources]
Pecineaga_energy_attribution_integrated(1).docx, directional-analysis interpretation and embedded figure “Energy Rose (C1b Shapley values) / Frequency (%)”.

## Slide 14: Sea breeze is a recurring part of Pecineaga’s energy climate
1
Embedded regimes dominate
C4 occurs ~7 times more often than pure C1b conditions.
2
Energy relevance is material
The final mean attribution could reach around 28 GWh/year, or around 15% of annual production.
3
Seasonality matters
The contribution peaks in spring, when thermal forcing overlaps productive winds.
4
Method choice matters
Hourly Shapley allocation conserves energy; PBL-related negative residuals are treated as negligible artefacts.
Implication: coastal wind-resource assessment and forecasting should represent sea-breeze regimes explicitly.
CONCLUSIONS
Notes: [Sources]
Synthesis of user-supplied manuscript, draft article and Excel statistics.

## Slide 15: Thank you for atTention!