## Slide 1
Quantifying global-warming-induced changes in spatial and temporal patterns of heavy precipitation events and the implications to flood properties in Mediterranean catchments
Moshe Armon, Yair Rinat, Efrat Morin
Oshri Vizman
Galileo Conference
A European vision for hydrological observations and experimentation
NAPLES | ITALY | 12–15 JUNE 2023

## Slide 2
End of the century compared to its beginning, SSP5-8.5
IPCC Interactive Atlas, 2021
Total precipitation
Background, motivation and goal
Consecutive dry days
Research questions:
What are the expected changes in space-time properties of storm rainfall?
How these changes are expected to affect flood properties?
Our focus is on Heavy Precipitation Events (HPEs) in the Eastern Mediterranean
The eastern Mediterranean region gets drier with reduced total precipitation, fewer rainy days, and longer dry periods.

## Slide 3
Pseudo Global Warming (PGW)
29 CMIP5 models:
SLP, T, wind, moisture
Image source: ECMWF
Atmospheric conditions in historical HPEs from reanalysis
Change in atmospheric conditions, CMIP5, end 21st century, RCP8.5
WRF model (CPM)
41 historical HPEs
Armon et al., 2020; Armon et al., 2022
1-km, 10-min rainfall maps
Projection of heavy precipitation events (HPEs)
41 historical – future HPE pairs
with 1-km, 10-min resolution

## Slide 4
Areal coverage
Storm duration
Conditional rain rate
Historical
Future
Single storm analysis
HPE #1
(November 1991)
Armon et al., 2020; Armon et al., 2022
Mean areal rainfall
Historical 21.9 mm
Future 17.5 mm
Projection of heavy precipitation events (HPEs)
-20%
-38%
-24%
+30%

## Slide 5
Projection of heavy precipitation events (HPEs)

## Slide 6
Avi Arish
Oshri Vizman
Historical
Future
What are the expected changes in flood properties?

## Slide 7
Rinat et al., 2018; Rinat et al., 2021
Projection of streamflow
Hydrological model
41 historical – future HPE pairs
with 1-km, 10-min resolution
Mostly agricultural,
Mediterranean basins
18-70 km2
For each HPE and period: 43 south-north storm translations, -21 to +21 km, 1 km intervals
Historical
Future
Rinat, Armon and Morin, in preparation. Results are not final.

## Slide 8
A non-significant decrease in event streamflow peak discharge (-20%)
A significant decrease in event streamflow volume (-27%)
X 106
A significant decrease in event rain depth (-24%)
Projection of streamflow
Rinat, Armon and Morin, in preparation. Results are not final.
Flood volume
Flood peak discharge
Areal rain depth
Historical
Future
Historical
Future
X 106
Historical
Future
*Results are presented for a 42 km2 basin
*Changes in land-use and initial soil moisture are not yet included

## Slide 9
Summary
The eastern Mediterranean becomes drier, but space-time changes at the storm scale and the expected effect on floods are yet to be quantified.
Future heavy precipitation events (HPEs) in the eastern Mediterranean are expected to be drier and more spatiotemporally concentrated: lower rain amounts (-30%), shorter (-9%), reduced area (-40%), and higher conditional rain rates (+15%).
On-going research (not final): Future floods from HPEs in the Ramot Menashe region (mainly agricultural, Mediterranean basins 18-70 km2) are expected to have a lower total volume (-27%) and a lower peak discharge (-20%).
Research is still ongoing to examine:
  intra-basin changes (are there scales where flood peak increases rather than decreases?),
  the effect of initial soil moisture (the soil is drier at storm’s beginning)
  the effect land use changes (more built area).
Thanks for your attention