## Slide 1
Authors: Shannon de Roos*, Michel Bechtold, Louise Busschaert, Zdenko Heyvaert, Sujay Kumar, Hans Lievens, Jonas Mortelmans, Dirk Raes, Samuel Scherrer, Maxime Van den Bossche, Elias Fereres, Margarita Garcia-Vila, Pasquale Steduto, Theodore Hsiao, Lee Heng, Maher Salman, Gabrielle De Lannoy
Assimilation of Sentinel-1 backscatter data into AquaCrop v7
for soil moisture and biomass updating over Europe
* contact: Shannon.deroos[at]kuleuven.be

## Slide 2: Regional monitoring of agricultural production
de Roos et al. (2021), Geosci. Model Dev., doi: 10.5194/gmd-14-7309-2021
seasonal and inter-annual changes in
soil moisture and crop biomass production
Large scale applications  European continent
  Spatial resolution: 1-km
  Temporal resolution: daily
Introduction of errors by
general input and model assumptions
Use of independent observations to update model simulations via data assimilation

## Slide 3: model
observations
Regionally gridded AquaCrop v7
MERRA-2 re-analysis forcings [50km  1km]
STATSGO/FAO soil textural classes [1 km]
Generic C3 crop w/ annual growth cycle
Rainfed agriculture (no irrigation)
Sentinel-1 (S1)
CSAR (5.4 GHz)
Co-polarisation; VV & cross-polarisation; VH
1 km spatial resolution
Temporal resolution: ~3 days
 Total backscatter signal (ϒ°; dB) contains information on soil moisture and vegetation
 Simulations of soil moisture (m3/m3) & crop dry biomass (ton/ha)

## Slide 4
Step 1: AquaCrop biomass & soil moisture to backscatter signal (dB)
de Roos et al.(2023), Remote Sens Environ., doi: 10.1016/j.rse.2023.113621
The data assimilation (DA) set-up
WATER CLOUD MODEL
soil moisture (m3m-3)
dry biomass (ton ha-1)
wet biomass (-)
ϒ°AquaCrop (dB)
ϒ°S1 (dB)

## Slide 5
The data assimilation (DA) set-up
Step 2: backscatter data assimilation for AquaCrop soil moisture and biomass updating
EnKF
24
ensemble members

## Slide 6: Experiments data assimilation (DA)
Experiment 1 ϒ° VV to update soil moisture
 perturb meteorological input (rainfall, temperature, ETo)
 perturb soil moisture
Experiment 2 ϒ° VV + ϒ° VH to update soil moisture and biomass
 perturb meteorological input (rainfall, temperature, ETo)
 perturb soil moisture & biomass
Site 1: West Germany
Site 2 : South France
Site 3 : NW Spain
ISMN soil moisture in situ points

## Slide 7: Results: DA impact
Experiment 1 – ϒ° VV
to update surface soil
moisture (SSM)
Experiment 2 – ϒ° VV + ϒ° VH
to update SSM & Biomass (B)
Site 3 (NW-Spain)
Site 3 (NW-Spain)
2015
2016
2017
DMP
[ton ha-1 day-1]
Biomass
[ton ha-1]
SSM
[m3 m-3]
0
0.10
0
10
0.5
0
2015
2016
2017
2021
2020
2019
2018
Cumulative B daily B
OL DA
in situ
SMAP
OL
DA
OL
DA
DMP
2021
2018
2020
2019
Biomass
[ton ha-1]
SSM
[m3 m-3]
DMP
[ton ha-1 day-1]
0.5
0
0
0
15
0.15
OL DA
in situ
SMAP
OL
DA
OL
DA
DMP
2018-07-30
2018-07-30

## Slide 8: Results: soil moisture and vegetation updating
R [-]
Anomaly R [-]
Small improvements in correlations for SSM with SMAP 1km for both experiments
Updating of biomass does not improve daily biomass production compared to Dry Matter Productivity
OL DA
OL DA
SSM: AquaCrop vs. SMAP
Biomass: AquaCrop vs. DMP

## Slide 9: Summary and outlook
SAR assimilation to update AquaCrop variables holds potential
Further research needed for biomass updating:
  Compare updates to other vegetation products to explore full potential
Model framework needs improvements:
  Better representation of soil properties
  Need for more detailed crop information

## Slide 10: References
Publications:
  de Roos, S. and De Lannoy, G. J. M. and Raes, D.(2021). Performance analysis of regional AquaCrop (v6.1) biomass and surface soil moisture simulations using satellite and in situ observations, Geoscientific Model Development 14 (12), doi:10.5194/gmd-14-7309-2021
  de Roos, S., Busschaert, L., Lievens, H., Bechtold, M., and De Lannoy, G. J. M.(2023). Optimisation of AquaCrop backscatter simulations using Sentinel-1 observations, Remote Sensing of Environment, 294, doi: 10.1016/j.rse.2023.113621
Evaluation datasets:
  SMAP 1-km: Fang, B., Lakshmi, V., Cosh, M., Liu, P.-W., Bindlish, R., and Jackson, T. J.(2022). A global 1-km downscaled SMAP soil moisture product based on thermal inertia theory. Vadose Zone Journal, doi:10.1002/vzj2.20182.
  DMP: Wolfs, D., Swinnen, E., Van Hoolst, R., and Toté, C.(2022). Copernicus global land operations “vegetation and energy”“cglops-1” product user manual: Dry matter productivity (dmp)–gross dry matter productivity (gdmp)–collection 300m–version 1.1.
  ISMN: Dorigo, W. A., Wagner, W., Hohensinn, R., Hahn, S., Paulik, C., Xaver, A., Gruber, A., Drusch, M., Mecklenburg, S., van Oevelen, P., Robock, A., and Jackson, T.(2011) The international soil moisture network: a data hosting facility for global in situ soil moisture measurements. Hydrology and Earth System Sciences, doi: 10.5194/hess-15-1675-2011