## Slide 1: An innovative membrane-based sensor technology for large-scale measurements of gas concentrations in the subsurface
Detlef Lazik
Gerrit H. de Rooij
Mohammad R. Hashar

## Slide 2: Measurement principle: exchange of gases between a buried gas-permeable tube and the surrounding soil changes the gas pressure in the tube
Gases in soils: N2, O2, CO2, H2O
The tubular membrane should be much more permeable for the target gas than for the other gases.
For CO2: polydimethylsiloxane. 5 to 10 times more permeable to CO2 than to N2 and O2, very permeable to H2O.
Gas-permeable tubular membrane
filled with reference gas
Surrounding soil with the target gas in the gas-filled pore space
Diffusive exchange between the soil and the tube
Conditioning step: Flush the tube with a reference gas until the tube wall has steady-state diffusive fluxes
Measurement step: Close the tube at both ends and let the target gas diffuse into it

## Slide 3: Measurement principle: Do not wait for equilibrium, but use the initial pressure change inside the tube instead!
After the conditioning step, the concentration profile of the target gas in the membrane constituting tube wall is steady.
When valves close both ends of the tube at t = 0, the pressure inside the tube starts to change. In the initial stage, the changes in partial pressures inside the tube are proportional to the soil partial pressures of the various gases ().
The concentration () of gas k at the inside (outside) of the tube wall equals (with the solubility of gas k in the tube wall).
Ri
Ra
r
Gas-permeable tubular membrane
r
0
Ri
Ra
t = 0
t > 0
Gas movement through the tube wall is governed by the diffusion equation:
with the diffusion coefficient (L2T-1)
The solution for early times (approximately steady-state):
The geometry factor (L-2) accounts for and.

## Slide 4
Ideally, the tube material is only permeable to the target gas. In that case, the entrance of the target gas into the tube proportionally dilutes the gases comprising the reference gas mixture. The solution simplifies to a linear equation with calibration constants and :
Calibration can be avoided by flushing a second tube with air enriched with the target gas. A third (reference) tube is in a gas-tight casing open on either end to provide a reference pressure. All tubes are installed together to ensure similar and temp.
For CO2 measurements, the effect of water vapor needs to be accounted for by exposing the reference tube to air saturated with water vapor (RH = 100%). Combining pressure differences allows to separate the signals of H2O and CO2.
Measurement principle: Installing multiple tubes eliminates the need for calibration
Soil air Soil air RH 100%
Air Air + CO2 Air

## Slide 5: Study Site in Brandenburg, Germany
Wooded meadow
Pine forest
Mixed forest
Google maps
Google maps

## Slide 6: Schematic set-up of a gas-sensor in the field
Pressure sensors
Above-ground control Buried gas-permeable tubes
Valve cascades
Purge gas vessels with pressure gauges
Tubes before covering with soil material
Scheme for laying the gas-permeable tubes in the soil
Gas-permeable tubes
Pits for side drilling
Soil surface
Actuator box
Air+CO2
Air
Air

## Slide 7: The system is being set up in the field
The centralized purge gas supply system forces us to design a system that can deliver purge gas to different gas-sensors at different distances in such a way that they all receive their purge gas at equal pressure. We are designing and testing a system with parallel valves (valve cascades) to achieve the needed pressure with high precision.
The control hardware, electronics, and the purge gas system will be housed in a hut (a modified container) with permanent power supply.
Electrical wires (to drive the valves and various sensors) and gas-tubing (to flush the buried tubes) run from the housing to the three fields.
Wooded meadow
Pine forest
Mixed forest

## Slide 8: Transient response (top) and steady-state control response (down)
Gas pressure (P1) in vessel 1
Chart: t [min]
Chart: t [min]
Chart: t [min]
Chart: t [min]
Chart: t [min]
Chart: t [min]
Gas pressure (P2) in vessel 2
CO2 concentration in vessel 2

## Slide 9
Thank you for your attention

## Slide 10: Development of the housing system for gas-sensors
Mechanical structure of the first sample for an actuator box. Pressure sensors (1) and valves (2) are fixed on a mounting plate. Fittings are used to connect the pressure measurement to the gas-tubing, which, including cables and tubes, are fed through the mounting flange (3) into the actuator box. (4) shows an actuator box assembled except for the media connection, and (5) shows the final closed box.
Components of the housing system produced using the MSLA process with a 3D printer (Elegoo Saturn 2), (1) mounting plate (2) mounting flange (3) connector (4) spacer (5) actuator box
1
2
3
4
5