## Slide 1
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
https://doi.org/10.5194/egusphere-gc8-hydro-40
Alessio Gentile1, Davide Gisolo1, Davide Canone1, and Stefano Ferraris1
1Interuniversity Department of Regional and Urban Studies and Planning (DIST), Politecnico and Università degli Studi di Torino, Torino, Italy
GC8-Hydro
NAPLES | ITALY | 12-15 JUNE 2023
Reproducing in-situ measurements over a high-elevation grassland using HYDRUS-1D and a snow isotope model

## Slide 2
Research question
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
1/15
“Main discrepancies between simulated and measured values can be generally attributed to uncertainties related to infiltration during snow melt. The actual quantity and timing of infiltrating water often remain unknown in soils where soil frost, snow cover, and snow melt may play a crucial role. Snow drift and irregular thawing of soil may produce differences in the infiltration pattern.”
Can we reliably model water flow and solute transport in a remote natural soil profile where soil water dynamics are strongly influenced by snow melt ?
Introduction
Methods
Results and Discussion
Conclusions

## Slide 3
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
2/15
Introduction
Methods
Results and Discussion
Conclusions
Study site: a high-elevation grassland
Dora del Nivolet outlet point
Naples
Elevation: 2711 (2390-3430) m a.s.l. Area: 16.99 km2
Soil moisture probes
(10,20,40 cm)
Eddy covariance station
Precipitation isotope sampler
Soil and vegetation samples for isotopic analysis
Aosta Valley
Google Earth ©

## Slide 4
Introduction
Methods
Results and Discussion
Conclusions
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
3/15
Real weather sensor
Snow depth doppler
Cosmic Ray
…A bit more about the monitoring station
Webcam
Chart: Cosmic Ray SWE

## Slide 5
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
4/15
Introduction
Methods
Results and Discussion
Conclusions
Study site: a high-elevation grassland
Dora del Nivolet catchment during winter (January, 2018)
Dora del Nivolet catchment during summer (July, 2019)

## Slide 6
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
5/15
Introduction
Methods
Results and Discussion
Conclusions
Dual-isotope plot and fractionation
mean evaporation slope = 3.07
Benettin et al. (2018)
Chart: 
| -16.795000000000002 | -13.27 | -6.4 | -6.6 | -8.7799999999999994 | -12.12 | -15.11 | -21.36 | -13.92 | -11.6 | -16.420000000000002 | -8.01 | -5.71 | -7.78 | -4.0046991917917012 | -10.061166284792725 | -5.9408797049538107 | -7.3046101601756845 | -11.015352698938557 | -12.255774608740069 | -16.28176137587883 | -14.568136239096646 | -14.746693551180329 | -11.002072001835169 | -8.8143961401157949 | -15.225614743543437 | -7.086665348043387 | -3.5664472474716149 | -6.7 | -8.1999999999999993 | -11.469568369727995 | -14.095202020229408 | -19.957672808219588 | -18.0732190048858 | -16.209739135768768 | -11.702866372162475 | -10.784704453872701 | -8.4036427321698284 | -5.775310948700735 | -7.1550399003955363 | -13.706781379586028 | -19.767028197562695 | -18.799606965162486 | -13.310091359456161 | -15.487963718397358 | -13.660320140484799 | -6.0582580899791383 | -8.6 | -8.3702435915281708 | -7.9861448307272553 | -8.3350926066495283 | -13.899745251887111 | -14.424884836299043 | -16.776293995904251
Precipitation | -137.0075 | -103.425 | -40 | -41 | -58.43 | -86.62 | -115.2 | -176.28 | -106.15 | -91.54 | -128.72 | -58.94 | -32.97 | -50.48 | -20.5553 | -67.8709 | -35.9661 | -46.2876 | -73.2183 | -90.307 | -128.816 | -116.2838 | -115.0655 | -81.0162 | -61.1685 | -112.1801 | -50.8662 | -24.5858 | -41 | -52 | -83.2915 | -103.2725 | -159.3679 | -134.6082 | -117.9217 | -85.9971 | -74.6879 | -56.6227 | -41.3967 | -48.7017 | -95.0449 | -153.0147 | -146.2305 | -103.5749 | -123.6202 | -100.5873 | -35.9422 | -56 | -45.6047 | -43.8098 | -49.5704 | -100.4438 | -107.3938 | -132.8781
Dora | -105.91 | -104.1567 | -105.535 | -107.89 | -105.38 | -102.27 | -102.96 | -97.99 | -102.95 | -92.87 | -98.16 | -103.98 | -105.27 | -106.23 | -108.6 | -102.8 | -95.8 | -93.7192 | -94.0526 | -92.0319 | -95.6222 | -92.5096 | -93.2163 | -95.2686 | -96.515 | -110.061 | -109.5256 | -108.3738 | -108.7916 | -103.7971 | -103.6842 | -99.0787 | -101.3093 | -99.1891 | -99.7708 | -101.5575 | -105.0419 | -108.322 | -104.1407 | -98.2139 | -100.1292 | -92.5745 | -97.1092 | -101.2375 | -101.3606 | -97.5006 | -101.5698 | -102.279 | -106.9973 | -106.0182 | -100.843 | -97.6104 | -86.6607 | -94.5462 | -91.6385 | -95.3078 | -99.0584 | -98.7136
Source | -111.54 | -112.7967 | -112.565 | -112.12 | -111.43 | -110.81 | -108.44 | -105.83 | -104.1 | -108.2 | -109.3 | -112 | -101.4683 | -101.4788 | -100.5808 | -102.1453 | -100.7665 | -95.9917 | -95.7705 | -116.5991 | -112.7597 | -109.5275 | -109.9401 | -109.488 | -107.9262 | -106.0296 | -105.1161 | -101.6639 | -103.755 | -107.9765 | -113.4901 | -114.5288 | -111.6566 | -109.777 | -102.2256 | -102.5874 | -99.3824 | -101.9956 | -104.1638 | -104.1937 | -100.8044 | -99.9714 | -110.915 | -113.1168 | -113.0385 | -108.9453 | -104.9506 | -105.2921 | -101.4324 | -102.3566 | -102.8556 | -105.2979 | -105.9232
SA | -110.058 | -111.9227 | -110.0327 | -107.5667 | -108.4267 | -108.1774 | -102.4723 | -104.9608 | -111.4631 | -111.0091 | -105.5867 | -107.5805 | -107.5372 | -107.2565 | -107.6127 | -114.9733 | -113.1598 | -111.9549 | -110.0669 | -109.1245 | -108.6062 | -105.306 | -105.8891 | -108.5382
Soil | -54.7215 | -45.1924 | -45.471 | -32.9189 | -58.9596 | -87.6948 | -43.6739 | -84.1849 | -118.2351 | -122.5344 | -60.6218 | -95.0865 | -48.9459 | -51.9024 | -54.0854 | -51.7977 | -59.0454 | -63.1987 | -121.1819 | -141.1682 | -125.3635 | -141.6056 | -138.2902 | -49.7459 | -140.0897 | -132.6505 | -69.5624 | -123.9368 | -52.7 | -59.8225 | -123.4761 | -77.1764 | -93.5103 | -135.4421
Gin | -35.4864 | -75.8246 | -79.4683 | -70.0551 | -38.2855 | -49.4882 | -44.7046 | -55.0317
Mir | -32.177 | -49.0958 | -85.9449 | -90.7931 | -64.8973 | -37.296 | -27.2392 | -50.5823
Sal | -49.5113 | -99.9412 | -99.9683 | -80.3896 | -100.9537 | -62.6852 | -55.9764 | -56.3739
Tri | -13.8961 | -39.2717 | -82.1162 | -69.2266 | -79.6527 | -78.6716 | -55.1325 | -62.1266 | -50.9229
Gen | -53.2885 | -69.7442 | -83.5257 | -84.1356
LMWL | -201.276 | -192.5698 | -183.8636 | -175.1574 | -166.4512 | -157.745 | -149.0388 | -140.3326 | -131.6264 | -122.9202 | -114.214 | -105.5078 | -96.8016 | -88.0954 | -79.3892 | -70.683 | -61.9768 | -53.2706 | -44.5644 | -35.8582 | -27.152 | -18.4458 | -9.7396 | -1.0334 | 7.6728 | 16.379 | 25.0852 | 33.7914 | 42.4976 | 51.2038 | 59.91 | 68.6162 | 77.3224 | 86.0286 | 94.7348 | 103.441
GMWL | -190 | -182 | -174 | -166 | -158 | -150 | -142 | -134 | -126 | -118 | -110 | -102 | -94 | -86 | -78 | -70 | -62 | -54 | -46 | -38 | -30 | -22 | -14 | -6 | 2 | 10 | 18 | 26 | 34 | 42 | 50 | 58 | 66 | 74 | 82 | 90
Stream water isotopes:
Gentile et al. 2022, accepted, HESS
https://egusphere.copernicus.org/preprints/2022/egusphere-2022-921/

## Slide 7
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
6/15
Introduction
Methods
Results and Discussion
Conclusions
Snow accumulation and melt model (Ceperley et al. 2020)
where M(t) [mm/d] is the daily snowmelt, ζ [mm/°C/d] is the degree-day factor and hS (t) is the snow water equivalent [mm w.e.] at time t.
Snow accumulation is simulated with a linear transition between liquid and solid precipitation as a function of air temperature
Precipitation falls as snow at temperatures below a minimum threshold (Tcrit1) and as rain at temperatures above a maximum threshold (Tcrit2)
The accumulated snow begins to melt when the air temperature rises above a given temperature threshold, T0 :
SNOW ACCUMULATION
(Harpold et al., 2017;
Hock, 2003)
SNOWMELT
(Schaefli et al., 2014)
Parameter | Value
T0 [°C] | 0
ζ [mm/°C/d] | 4.3
Parameter | Value
Tcrit1 [°C] | -2
Tcrit2 [°C] | 2
Default value in H1-D
Default value in H1-D
Snow accumulation and melt are computed per elevation band
Notes: Air temperature is linearly interpolated to mean band elevation with a constant temperature lapse rate per study catchment (see Section 3), whereas precipitation is kept constant.

## Slide 8
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
7/15
Introduction
Methods
Results and Discussion
Conclusions
Snow isotope model (Ceperley et al. 2020)
Assumptions:
The isotopic composition of snowmelt (CS) is computed based on the following mass balance:
hs is the snow water equivalent
CP−fit is the sine curve fitted to observations
Peq is the equivalent precipitation (i.e., rain + snowmelt).
The initial condition is CS(t0)=CP − fit(t0).
The isotopic composition in the equivalent precipitation (CPeq) at each time-step can be obtained as:
“the isotope content of infiltrating water from the melting snow layer remains unknown” (Stumpp et al. 2012)
}
aS,i is the area of the snow-covered
elevation band i
ar,j is the area of the non-snow-covered
elevation band j
Total catchment area
Water in the snowpack is fully mixed.
Any rainfall on a pre-existing snowpack also mixes with the water stored in the snowpack.
Notes: Water in the snowpack is fully mixed: is a rough approximation during early snowmelt or intermittent snowpack events (Rücker, Boss, Kirchner, & von Freyberg, 2019), but which is a better approximation for seasonal snowpack during the peak snowmelt season when the snowpack is isothermal (Beria et al., 2018), and has been validated with snow lysimeter data (Ala-Aho et al., 2017)
Rainfall mixes with water in the snowpack: In this formulation, all rainfall mixing with an existing snowpack is assumed to exit during the same time step and neglects any water holding capacity of the snowpack or temporary refreezing (e.g., Schaefli et al., 2014).

## Slide 9
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
8/15
Introduction
Methods
Results and Discussion
Conclusions
Potential Evapotranspiration (ET0), Transpiration (TP), Evaporation (EP)
Aosta Valley
Ra = extraterrestrial radiation (mm/day)
Tmax = daily maximum air temperature (°C)
Tmin = daily minimum air temperature (°C)
HC = empirical coefficient (HC = 0.0023)
HE = empirical exponent (HE = 0.5)
HT = a factor needed to convert units of Fahrenheit to Celsius (HT = 32/1.8 = 17.8)
Z = station elevation (m a.s.l.)
Ravazzani et al. (2012)
Where k = 0.463 (Ritchie, 1972) LAI is the Leaf Area Index calculated from MODIS/061/MCD15A3H collection in GEE .
Spatial resolution: 500 m
Temporal resolution: 4 days
e.g. Nasta et al. (2013)

## Slide 10
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
9/15
Introduction
Methods
Results and Discussion
Conclusions
HYDRUS 1-D set up
60 cm
Sandy
Loam
Grass
1
0
Roots
distribution
- Atmospheric BC
with Surface Runoff
- Free drainage
Parameters
θR [-]
θS [-]
α [cm-1]
N [-]
KS [cm d-1]
L [-]
λL [cm]
Ρ [g cm-3]
Water Flow
parameters
Solute transport
parameters
Parameters in red are calibrated by using soil moisture and soil isotope (corrected from fractionation) measurements
Initial condition:
- In pressure head
- in liquid phase concentrations
- Concentration Flux BC
- Zero Concentration Gradient
Upper Boundary Condition
Lower Boundary Condition

## Slide 11
Time Variable Boundary Conditions
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
10/15
Introduction
Methods
Results and Discussion
Conclusions

## Slide 12
Soil and xylem water isotopic composition
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
11/15
Introduction
Methods
Results and Discussion
Conclusions

## Slide 13
Soil water content
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
12/15
Introduction
Methods
Results and Discussion
Conclusions

## Slide 14
Actual Evapotranspiration and parameters
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
13/15
Introduction
Methods
Results and Discussion
Conclusions
Parameters | Value
θR [-] | 0.11±0.001
θS [-] | 0.39
α [cm-1] | 0.059
n [-] | 1.48
KS [cm d-1] | 31.23±0.26
L [-] | 0.5
λL [cm] | 1.56±0.32
ρ [g cm-3] | 1.5

## Slide 15
Conclusions
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
14/15
Introduction
Methods
Results and Discussion
Conclusions
By using a classical snow melt/accumulation model and a snow isotope model under simplifying assumptions, H1-D closely reproduces soil moisture and soil water isotope measurements.
Actual evapotranspiration derived from H1-D has been compared with actual evapotranspiration measurements derived from the eddy-covariance station demonstrating very good correspondence with the actual measurements.
Water flow calibrated parameters are quite close to the H1-D pedotransfer values, while it is difficult to find past works, excluding Stumpp et al. (2012), that provide isotope longitudinal dispersivity values for comparison purposes.
Main discrepancies between model output and measurements can be due to:
uncertainties related to the timing and amount of snowmelt
assumptions of the snow isotope model
Modelled soil water content reveals a high-sensitivity to winter snowmelt events.

## Slide 16
Main References
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
15/15
Benettin, P., Volkmann, T. H. M., von Freyberg, J., Frentress, J., Penna, D., Dawson, T. E., and Kirchner, J. W.: Effects of climatic seasonality on the isotopic composition of evaporating soil waters, Hydrology and Earth System Sciences, 22, 2881–2890, https://doi.org/10.5194/hess-22-2881-2018, 2018.
Ceperley, N., Zuecco, G., Beria, H., Carturan, L., Michelon, A., Penna, D., Larsen, J., and Schaefli, B.: Seasonal snow cover decreases young water fractions in high Alpine catchments, Hydrological Processes, 34, 4794–4813, https://doi.org/10.1002/hyp.13937 , 2020.
Nasta, P. and Gates, J. B.: Plot-scale modeling of soil water dynamics and impacts of drought conditions beneath rainfed maize in Eastern Nebraska, Agricultural Water Management, 128, 120–130, https://doi.org/10.1016/j.agwat.2013.06.021, 2013.
Ravazzani, G., Corbari, C., Morella, S., Gianoli, P., and Mancini, M.: Modified Hargreaves-Samani Equation for the Assessment of Reference Evapotranspiration in Alpine River Basins, Journal of Irrigation and Drainage Engineering, 138, 592–599, https://doi.org/10.1061/(ASCE)IR.1943-4774.0000453, 2012.
Stumpp, C., Stichler, W., Kandolf, M., and Šimůnek, J.: Effects of Land Cover and Fertilization Method on Water Flow and Solute Transport in Five Lysimeters: A Long-Term Study Using Stable Water Isotopes, Vadose Zone Journal, 11, https://doi.org/10.2136/vzj2011.0075 , 2012.

## Slide 17
Session 4 – Using O-H stable isotopes for studying hydrological process understanding and the history of flowing waters
https://doi.org/10.5194/egusphere-gc8-hydro-40
Thank you for your attention!
Alessio Gentile1, Davide Gisolo1, Davide Canone1, and Stefano Ferraris1
1Interuniversity Department of Regional and Urban Studies and Planning (DIST), Politecnico and Università degli Studi di Torino, Torino, Italy
GC8-Hydro
NAPLES | ITALY | 12-15 JUNE 2023