## Slide 1
Optimizing irrigation parameters to improve land surface model irrigation simulations: an example over the Po Valley, Italy
Sara Modanesi1, Gabriëlle J. M. De Lannoy2, Michel Bechtold2, Louise Busschaert2 and Christian Massari1
1 Research Institute for Geo-hydrological Protection, National Research Council, Via Madonna Alta 126, 06128 Perugia, Italy
2 Department of Earth and Environmental Sciences, KU Leuven, Heverlee, Belgium.
sara.modanesi@irpi.cnr.it
GC8-Hydro
Session 3
Data assimilation, artificial intelligence, and hydrological observations
Backgroung image: Sentinel-2 from © Sentinel Hub

## Slide 2
  INTRODUCTION
  THE “NEW” WATER CYCLE IN THE ANTHROPOCENE
1
STEP 1
STEP 2
Importance to estimate human water uses

## Slide 3
2
  COMBINING LSM AND IRRIGATION
  CAN WE PROVIDE A BETTER CLOSURE OF THE WATER CYCLE?
Modanesi et al. 2021
https://doi.org/10.5194/hess-25-6283-2021
EXPERIMENT SETUP
1 km spatial resolution
Model spinup: 1982-2015
Model run: 2015-2020
MERRA-2 reanalysis meteorological forcing
PROBA-V land cover map
Sprinkler irrigation
Sprinkler irrigation (Ozdogan et al. 2010; 10.1175/2009JHM1116.1) needs 3 conditions:
Where irrigated croplands are located (GRIPC)
Growing season, defined at each grid cell
Root zone soil moisture availability (MA<SMth)
NOAH-MP LSM
http://dx.doi.org/10.1016/j.jag.2015.01.014
User-set parameter

## Slide 4
  COMBINING LSM AND IRRIGATION
  RESULTS
The study area is located in the Po river valley, an intensively irrigated area. Irrigation data are available at two test sites:
The Budrio farm (less than 1 ha);
Two districts close to Faenza (Faenza test sites; ~300 ha and ~700 ha).
Large Overestimations
BUDRIO: RMSE [mm/15 days]=31.10; R=0.74; bias [mm/15 days]=11.15
FAENZA: RMSE [mm/15 days]=40.98; R=0.78; bias [mm/15 days]=18.08
Modanesi et al. 2021
https://doi.org/10.5194/hess-25-6283-2021
3

## Slide 5
Sentinel-1 γ0VV and γ0VH DA to update SM and LAI
Ensemble Kalman Filter DA
Added components:
Sprinkler irrigation
Calibrated Water Cloud Model (WCM, https://doi.org/10.1029/RS013i002p00357)
0veg
0soil
+
Double interaction between soil moisture and irrigation
  SENTINEL-1 BACKSCATTER DATA ASSIMILATION
  NEW DEVELOPMENTS TO IMPROVE AGRICULTURAL WATER USES
Modanesi et al. 2021
https://doi.org/10.5194/hess-25-6283-2021
Modanesi et al. 2022
https://doi.org/10.5194/hess-26-4685-2022
4

## Slide 6
Budrio test site
BUDRIO
Irrigation data averaged over five fields (0.4 ha each)
AMOUNT OF IRRIGATION
Obs=917.2 mm
OL= 1220.1 mm
DA=842.5 mm
Soil Moisture
[m3/m3]
Irrigation
[mm/15 days]
Rainfall
[mm/day]
LAI
[-]
ET
[mm/day]
Pearson-R: SSM OL vs ASCAT= 0.74; SSM DA vs ASCAT=0.78
Pearson-R: ET OL vs MODIS=0.7; ET DA vs MODIS=0.72
Pearson-R:
IRR OL vs OBS=0.78
IRR DA vs OBS=0.65
DA improves model state simulations but it deteriorates Pearson-R when irrigation is simulated
DA improves irrigation bias
Method’s improvement: Busschaert et al. 2023 (https://doi.org/10.22541/essoar.167590826.62059121/v1)
Pearson-R: LAI OL vs PROBA-V= 0.69; LAI DA vs PROBA-V=0.71
Modanesi et al. 2022
https://doi.org/10.5194/hess-26-4685-2022
5
  SENTINEL-1 BACKSCATTER DATA ASSIMILATION
  RESULTS

## Slide 7
  OPTIMIZATION OF IRRIGATION PARAMETERS
  TOWARDS A BETTER CLOSURE OF THE WATER CYCLE?
6
Sprinkler irrigation (Ozdogan et al., 2010)
CALIBRATION
NOAH-MP LSM
CALIBRATION SETUP:
Genetic Algorithm (GA)
Least square (LS) objective fuction
First synthetic experiment using simulated soil moisture (Th set to 0.45)
Calibration: Jan. 2015 – Nov. 2015
Initial Th set to 0.35
Th range: 0.25-0.60

## Slide 8
  OPTIMIZATION OF IRRIGATION PARAMETERS
  RESULTS
7
Findings:
Soil moisture and irrigation are well reproduced
Some small peaks are present meaning that the calibration options still need to be optimized
Generally the tuned SMth parameters are close to the best convergence (i.e., Th=0.45)
Work in progress!
CALIBRATED PARAMETER First generation
CALIBRATED PARAMETER Last generation
Th [-]
Budrio fields
CALIBRATED PARAMETER Second generation
Th [-]
Th [-]
Soil Moisture
[m3/m3]
Irrigation
[mm/hr]
BUDRIO

## Slide 9
  TAKE HOME MESSAGES
8
Simulating irrigation in models is crucial to improve estimates of agricultural water uses
Models have limitations and satellite observations can provide useful information about the true state of the Earth surface
Combining LSM and Sentinel-1 SAR observations partly improves the water cycle description but the limitation of the WCM to reproduce vegetation-related features can affect DA performances
Model calibration to optimize irrigation parameters seems worth to be explored for a better estimate of agricultural water uses
Combining LSM and multiple RS products (i.e., thermal, optical and MW observations) through DA and/or calibration can be advantageous to build a digital replica of the our planet
Thank you for your attention!