## Slide 1
CRNS for remote sensing
soil moisture validation
Jannis Weimar, Markus Köhli
12.06.2023
Physikalisches Institut
Ruprecht-Karls-Universität
Heidelberg
GC8-Hydro Napoli

## Slide 2
Soil Moisture Measurement Gap
via
satellite remote sensing
(optical, microwave)
via
local techniques
(electrical resistivity, capacitance, etc.)
[1]
[2]
> 1 km
< 10 m
[1] ESA SMOS (http://www.esa.int/Our_Activities/Observing_the_Earth/SMOS/Horn_of_Africa_drought_seen_from_space)
[2] The Clay Research Group (http://www.theclayresearchgroup.org/images/ert.jpg)
Notes: 2

## Slide 3
Remote Sensing Upscaling
[1] J. Huang, et al. „Retrieving Heterogeneous Surface Soil Moisture at 100 m Across the Globe via Fusion of Remote Sensing and Land Surface Parameters”, Front. Water 28(2) (2020)
How to validate/calibrate satellite-based soil moisture measurements?
250 m upscaled
100 m upscaled
Difference between both
Wisconsin, USA
Notes: 3

## Slide 4
Cosmic Ray Neutron Sensing
.CRNS.

## Slide 5
CRNS: Basics
Incoming neutron
Isotropic Scattering in soil
λ = few cm
Scattering in air
λ ≈ 50 m
Detection
Rock
Water
Notes: 5

## Slide 6
CRNS: Basics
Cosmic-Ray Neutron Sensing
Only sensitive to hydrogen (soil chemistry plays a minor role)
Non-invasive, autarkic
Large support volume 10 hectare, 0.5 m deep
Can be extended by mobile measurements
Notes: 6

## Slide 7
Mobile Measurements – Full Coverage
Courtesy M. Schrön, UFZ Leipzig
Notes: 7

## Slide 8
Mobile Measurements Across Scales
Courtesy M. Schrön, UFZ Leipzig
Cooperation German Weather Service, F Beyrich, FESSTVal
Preliminary data
StyX Rover
UFZ Leipzig
Notes: 8

## Slide 9
Mobile Measurements
Opportunities
Large area soil moisture measurements:
  Full coverage for 1 km2/day with a resolution of 50 m
  Coarse sampling of larger areas e.g. a whole catchment
Snap-shot data for areas with no other data (e.g. ISMN) available
Challenges
Other hydrogen pools than soil moisture influence the signal (e.g. vegetation, rivers…)
Road effect
Notes: 9

## Slide 10
Our contribution
Neutron detectors
Neutron simulation
Notes: 10

## Slide 11
Our Offer
Use CRNS for non-invasive, large area on-demand mapping of soil moisture
Notes: 11

## Slide 12
The end
Thanks for your attention
Notes: 12

## Slide 13
Stationary and Roving Instruments
Stationary
Roving
Notes: 13

## Slide 14
Detector Footprint
horizontal
vertical
Notes: 14

## Slide 15
Neutron Energy spectrum
Notes: 15