## Slide 1: Integrating soil structure in hydrologic models of the unsaturated zone
Authors: Efthymios Chrysanthopoulos, Christos Pouliaris, Kostas Markantonis, Ioannis Tsirogiannis and Andreas Kallioras
GC8-Hydro-63

## Slide 2
Motivation
Most hydrologic models of the unsaturated zone to acquire hydraulic properties use the predictions of empirical equations (Pedotransfer functions – PTFs).
Commonly, soil texture is the main characteristic used by PTFs to predict the hydraulic properties of the unsaturated zone.
Furthermore, the samples of the databases used by these models to be trained are predominantly disturbed and only a few of them are undisturbed.
As a result, soil structure is pretty much ignored in hydrologic models of the unsaturated zone.
In this study, we have developed an organized approach to determine the hydraulic properties of the unsaturated zone and finally compare the performance of hydrologic models using predicted and measured hydraulic properties.

## Slide 3
Research Area
Epirus region –
Westernmost part
of Greece
Distinctive characteristic:
Elevated precipitation height (2000 mm/y)
Frequent flood events
One of the most productive agricultural areas of Greece. Main cultivation: Kiwi and citrus trees

## Slide 4
In order to manage water resources in the Louros-Aracthos-Amvrakikos system as efficiently as possible, the project e-Pyrros intends to establish an integrated network for monitoring hydro-environmental factors, aiming at:
The improvement of local agricultural ecosystems, the upgrading of the quality of agricultural production, and the monitoring of agricultural substances in all hydrological zones (surface, saturated, and unsaturated).
Research Area

## Slide 5
Major goal of the research program: optimization of agricultural production
Kiwi field
Area: 30 acres
Experimental kiwi field

## Slide 6
Experimental kiwi field

## Slide 7
Undisturbed soil samples
Electrical percussion hammer (Eijkelkamp)
Percussion gouge diameter: 64 mm.
Undisturbed soil samples up to 1 m. below the surface
Samples stored in pvc liner

## Slide 8
Undisturbed soil samples
10 cm.

## Slide 9
Custom permeameter cell

## Slide 10
Custom permeameter cell
Calculation of saturated hydraulic conductivity (Ksat)
8 cm/day
8 cm/day
7.5 cm/day
1.5 cm/day
2 cm/day
1.4 cm/day
1 cm/day
1 cm/day
1.2 cm/day
1.2 cm/day

## Slide 11
Soil Water Retention Curve
Centrifuge and salt solution method for SWRC estimation
0.01 kPa
2000 kPa
100 kPa
500 kPa
8000 kPa
Conventional
method
New
method
Centrifuge
(2 hours in each speed)
Salt
Solution (~63 days)

## Slide 12
Soil Water Retention Curve
Saturate samples until equilibrium

## Slide 13
Soil Water Retention Curve
0 -10 cm.
10 -20 cm.
20 -30 cm.
30 -40 cm.
40 -50 cm.
50 -60 cm.
60 -70 cm.
70 -80 cm.
80 -90 cm.
90 -100 cm.

## Slide 14
Evapotranspiration for Hydrus
Crop evapotranspiration (ETc) should be divided in potential evaporation (Ep) and potential transpiration (Tp):
  Ep = ETc e−Kgr ∗LAI
  Tp = ETc − Ep

## Slide 15
Evapotranspiration for Hydrus
Harmonic ANalysis of Time Series (HANTS)
Harmonic analysis is a branch of mathematics concerned with the representation of functions or signals as a superposition of periodic functions
Widely used algorithm to reconstruct time series and fill gaps in timeseries from satellite images

## Slide 16
Evapotranspiration for Hydrus
Reconstruction of LAI timeseries

## Slide 17
Hydrus
Hydraulic parameters estimated from soil texture data using Rosetta 3 model
1st model
2nd model
Hydraulic parameters calculated through laboratory experiments
Model period: Two years (2016-2018)
Time step: daily

## Slide 18
Hydrus
1st model (Results)
2nd model
(Results)

## Slide 19
Take home messages
In this study a falling head permeameter for undisturbed soil samples is developed, providing the capability to determine saturated hydraulic conductivity in large depths.
Two methods of measuring Soil Water Retention Curve are used, centrifugal method (rather new and time-efficient) and salt solution method (conventional and time consuming).
The use of undisturbed soil samples within the research framework aims to integrate soil structure in the determined hydraulic properties of the unsaturated zone.
The HANTS (Harmonic ANalysis of Time Series) algorithm is used to fill the gaps in LAI timeseries, providing the capability to increase the time resolution of satellite timeseries.
Finally, Hydrus 1D model (phydrus – python implementation) is employed to compare the performance of two models either with predicted or with measured hydraulic properties.

## Slide 20
GC8-Hydro-63
Acknowledgements:
This research is part of the Project “e-Pyrros: Development of an integrated monitoring network for hydro-environmental parameters within the hydro-systems of Louros-Arachthos-Amvrakikos for the optimal management and improvement of agricultural production” (MIS 5047059) and received financial funding from the Operational Programme “Competitiveness, Entrepreneurship and Innovation 2014-2020 (EPAnEK)”.

## Slide 21: Thank you for your attention
GC8-Hydro-63