## Slide 1: A novel combined approach for bridging scales in spatiotemporal soil moisture monitoring applying metrological principles
Sascha Oswald, Sebastian Rothermel, Gabriele Baroni, Anna Balenzano, Henrik Kjeldsen, Martin Schrön, and Miroslav Zboril
Acknowledgement:

## Slide 2: Problem of scales
Satellite remote sensing
Point-scale in situ measurements
Horizontal scale
(10-1 – 101) m
Invasive, affected by immediate surrounding
Sensor networks  maintenance & repair costs
Need for harmonization of methods
Need for metrological transfer standards
Only topmost soil layer (5 cm)
Validation practices based on point-scale data
Need for effective, representative ground-based methods
(103 – 104) m
“ gap ”
(102 – 103) m
[https://soilsensor.com]
[ESA Sentinel-1]
Cosmic-ray neutron sensing (CRNS)

## Slide 3: SoMMet
SoMMet
UP DE
TUBITAK
UFZ
PoliMi
JV
INRIM
CMI
IAPAN
CTU
CNR
DTI
SMU
PTB
UKCEH
UHEI
IRSN
UNIBO
CIEMAT
„…develop novel metrological tools and establish a metrological foundation for soil moisture measurements on multiple lateral scales, ranging from decimetre to kilometre, ensuring the traceability and harmonisation of the various soil moisture measurement methods.”

## Slide 4: Metrological principles
DTI, Denmark
PTB, Germany
Traceability chain
  Primary and secondary transfer standard for point scale calibration
  Traceability across scales from the lab to the outdoors
Metrology of neutron radiation
  Response function modelling
  Validation of multiple CRNS probes in the lab (neutron fields)
  Validation with Bonner Spheres (outdoors)
 Improvements in CRNS usage
  Metrologically traceable calibration
  Standardised estimates of uncertainty
   Comparability of CRNS
WP1: Traceability
WP2: Validation
WP3: Harmonization
WP4: Data fusion

## Slide 5: Test sites in SoMMet
Three high level test sites:
  Marquardt
  Bondeno Orchards
  Apulian Tavoliere
   Three measurement scales
   North-south gradient

## Slide 6: Apulian Tavoliere
General site info:
  Experimental Farm
  Durum wheat/tomatoes
  Extend: ~3km² (flat)
  Clay loam
  530mm mean precipitation
  15.8° C mean temperature
  13 point scale sensors
  1 CRNS (with multiple energy spectra)
  Well established remote sensing site
Foggia experimental farm

## Slide 7: Bondeno Walnut Orchards
General site info:
  Irrigated walnut orchard
  Extend: ~1.5km² (flat)
  Clay loam
  600mm mean precipitation
  14° C mean temperature
  1 CRNS and a few point scale sensors
  Regular manual TDR surveys

## Slide 8: Marquardt
General site info:
  Agricultural research site
  mixed land use
  Extend: ~0.6km² (slightly sloped)
  Loamy sand
  600mm mean precipitation
  11° C mean temperature
  15 CRNS
  27 point scale profiles (10 – 200cm)

## Slide 9: Marquardt‘s new cluster design

## Slide 10: Marquardt: preliminary results

## Slide 11: Marquardt: preliminary results

## Slide 12: Thank you!
Follow the project progress at: sommet-project.eu